## Slide 1: Overview of 802.11 Security
Jesse Walker, Intel Corporation
(503) 712-1849
jesse.walker@intel.com

## Slide 2: Acknowledgements
Bernard Aboba
Dave Halasz
Nikita Borisov
Duncan Kitchin
I am grateful to these individuals for allowing me to freely plagiarize their presentations and documents to prepare this presentation

## Slide 3: Agenda
Introduction and Goals
802.11 Security Today
What’s Wrong Today?
Proposed Encapsulation
Proposed Authentication, Authorization, and Key Management
Summary

## Slide 4: Introduction
802.11 security recently gained notoriety:
  Celebrated UC Berkeley paper by Borisov et. al. publicized attacks on 802.11
  Most of these were discussed privately in 802.11 TGe throughout last year and documented in doc. IEEE 802.11/00-362
  UC Berkeley group wasn’t participating in the process, but 802.11 was living in sin

## Slide 5: Goals
Develop a wider understanding of network security requirements
Explain how 802.11 security works now
Describe its major issues
Understand what is being done to address the issues

## Slide 6: Agenda
Introduction and Goals
802.11 Security Today
What’s Wrong Today?
Proposed Encapsulation
Proposed Authentication, Authorization, and Key Management
Summary

## Slide 7: 802.11 Security Today
Goals of existing 802.11 security
Existing security consists of two subsystems
  A data encapsulation technique called Wired Equivalent Privacy (WEP)
  An authentication algorithm called Shared Key Authentication

## Slide 8: Existing 802.11 Security Goals
Create the privacy achieved by a wired network
  Only prevent intellectual property from leaking through casual browsing
Simulate physical access control by denying access to unauthenticated stations

## Slide 9: WEP Encapsulation
802.11 Hdr
Data
WEP Encapsulation Summary:
Encryption Algorithm = RC4
Per-packet encryption key = 24-bit IV concatenated to a pre-shared key
WEP allows IV to be reused with any frame
Data integrity provided by CRC-32 of the plaintext data (the “ICV”)
Data and ICV are encrypted under the per-packet encryption key
802.11 Hdr
Data
IV
ICV
Encapsulate
Decapsulate

## Slide 10: WEP Authentication
Challenge (Nonce)
Response (Nonce RC4 encrypted under shared key)
STA
AP
Shared secret distributed out of band
Decrypted nonce OK?
802.11 Authentication Summary:
Authentication key distributed out-of-band
Access Point generates a “randomly generated” challenge
Station encrypts challenge using pre-shared secret

## Slide 11: Agenda
Introduction and Goals
802.11 Security Today
So What’s Wrong Today?
Proposed Encapsulation
Proposed Authentication, Authorization, and Key Management
Summary

## Slide 12: So What’s Wrong Today?
Properties of Vernam Ciphers
How to read WEP Encrypted Traffic
How to authentication without the key
Traffic modification
Lessons
Requirements for a networked data encapsulation scheme

## Slide 13: Properties of Vernam Ciphers (1)
The WEP encryption algorithm RC4 is a Vernam Cipher:
Pseudo-random number generator
Encryption Key K
Plaintext data byte p
Random byte b

Ciphertext data byte p
Decryption works the same way: p = c  b

## Slide 14: Properties of Vernam Ciphers (2)
Thought experiment 1: what happens when p1 and p2 are encrypted under the same “random” byte b?
c1 = p1  b
c2 = p2  b
Then:
Conclusion: it is a very bad idea to encrypt any two bytes of data using the same byte output by a Vernam Cipher PRNG.
c1  c2 = (p1  b)  (p2  b) = p1  p2
Ever.

## Slide 15: How to Read WEP Encrypted Traffic (1)
By the Birthday Paradox, probability Pn two packets will share same IV after n packets is P2 = 1/224 after two frames and Pn = Pn–1 + (n–1)(1–Pn–1)/ 224 for n > 2.
50% chance of a collision exists already after only 4823 packets!!!
Pattern recognition can disentangle the XOR’d recovered plaintext.
Recovered ICV can tell you when you’ve disentangled plaintext correctly.
After only a few hours of observation, you can recover all 224 key streams.
802.11 Hdr
Data
IV
ICV
24 luxurious bits
Encrypted under Key +IV using a Vernam Cipher

## Slide 16: How to Read WEP Encrypted Traffic (2)
Ways to accelerate the process:
  Send spam into the network: no pattern recognition required!
  Get the victim to send e-mail to you
    The AP creates the plaintext for you!
  Decrypt packets from one Station to another via an Access Point
    If you know the plaintext on one leg of the journey, you can recover the key stream immediately on the other
  Etc., etc., etc.

## Slide 17: How to Authenticate without the Key
Challenge (Nonce)
Response (Nonce RC4 encrypted under shared key)
STA
AP
Decrypted nonce OK?
With our background, an easy attack is obvious:
Record one challenge/response with a sniffer
Use the challenge to decrypt the response and recover the key stream
Use the recovered key stream to encrypt any subsequent challenge

## Slide 18: Traffic Modification (1)
Vernam cipher thought experiment 2: how hard is it to change a genuine packet’s data, so ICV won’t detect the change?
Represent an n-bit plaintext as an n-th degree polynomial:
p = pnxn + pn–1xn–1 +  + p0x0 (each pi = 0 or 1)
Answer: Easy as pie
Then the plaintext with ICV can be represented as :
px32 + ICV(p) = pnxn+32 + pn–1xn–31 +  + p0x32 + ICV(p)
If the n+32 bit RC4 key stream used to encrypt the body is represented by the n+32nd degree polynomial b, then the encrypted message body is
px32 + ICV(p) + b

## Slide 19: Traffic Modification (2)
But the ICV is linear, meaning for any polynomials p and q
IVC(p+q) = ICV(p) + ICV(q)
Conclusion: Anyone can alter an WEP encapsulated packet in arbitrary ways without detection!!
This means that if q is an arbitrary nth degree polynomial, i.e., an arbitrary change in the underlying message data:
(p+q)x32 + ICV(p+q) + b = px32 + qx32 + ICV(p) + ICV(q) + b
= ((px32 + ICV(p)) + b) + (qx32 + ICV(q))

## Slide 20: Lessons
Data encryption by itself offers no protection from attack
  “It’s access control, stupid”
  there is no meaningful privacy if the data authenticity problem is not solved
It is profoundly easy to mis-use a cipher
  “don’t try this at home”
  Get any cryptographic scheme reviewed by professionals

## Slide 21: Requirements for a networked data encapsulation scheme
Data traffic:
  packets must be authentication, not just encrypted
  packets must have sequence numbers to prevent replay
Authentication:
  Mutual authentication required
  Per-packet keys have to be tied to the authentication

## Slide 22: Agenda
Introduction and Goals
802.11 Security Today
What’s Wrong Today?
Proposed Encapsulation
Proposed Authentication, Authorization, and Key Management
Summary

## Slide 23: Encapsulation Proposal
Current TGe plan of record:
Use AES-128 as the new cryptographic primitive
Use AES in Offset Codebook Mode OCB mode
  Phil Rogaway submission to AES modes of operation
  algorithm provides both privacy and data integrity
Add session sequence number to avoid replay
Map base key to session key
  use OCB mode tag to compute session key, to minimize number of cryptographic primitives implemented

## Slide 24: AES Facts
NIST standard for iterated block ciphers
  Block cipher: encrypts or decrypts 128-bit blocks of data, not individual bytes
  Uses 128-, 192-, or 256-bit keys
  Highly parallelizable
Critical path instructions:
  88 S-box, XOR6, XOR5, XOR2, MUX2
Performance
  200 MHz Pentium Pro: 284 cycles/block

## Slide 25: Iterated Block Ciphers
Multiplexor
Register
Combinational Logic

## Slide 26: OCB Mode (Full last block)
EK
IV
R
Message M = m1 m2 m3 … mn-1 mn
+  1L+R
+  1L+R
EK
m1
c1
m2
c2
+  2L+R
+  2L+R
EK
...
EK
mn
cn
 nL+R
+  nL+R

m1  …  mn
tag
+  (n+1)L+R
EK

## Slide 27: OCB Mode (Partial last block)
EK
IV
R
Message M = m1 m2 m3 … mn-1 mn
+  1L+R
+  1L+R
EK
m1
c1
m2
c2
+  2L+R
+  2L+R
EK
...
EK
mn
cn
 nL+R
+  nL+R

m1  …  pad(mn)
tag
+  (n+1)L+R
EK
+  (n+2)L+R

## Slide 28: AES-Based WEP Format
802.11 Hdr
Data
Seq Num
Data
802.11 Hdr
128-bit IV
128-bit MIC
Encapsulate
Decapsulate

## Slide 29: Rationale
AES strong and fast and parallelizable
OCB mode provides both data authenticity and encryption
  This avoids many common implementation and design errors
  Minimizes number of gates to implement
  Fast and parallelizable
  Doesn’t fail catastrophically if IV is reused

## Slide 30: Agenda
Introduction and Goals
802.11 Security Today
What’s Wrong Today?
Proposed Encapsulation
Proposed Authentication, Authorization, and Key Management
Summary

## Slide 31: Approach
Based on existing protocols
  Kerberos V (RFC 1510)
  GSS-API (RFC 2743)
  IAKERB (draft-ietf-cat-iakerb-05.txt)
  EAP-GSS (draft-aboba-pppext-eapgss-02.txt)
  EAP (RFC 2284)
  802.1X/EAPOL
802.11enhancements
  MAC security management
  New model for authentication/association sequences

## Slide 32: IEEE 802.1X Terminology
Controlled port
Uncontrolled port
Supplicant
Authentication Server
Authenticator
802.1X
created to control access to any 802 LAN
used as a transport for Extensible Authentication Protocol (EAP, RFC 2284)
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 33: 802.1X Model
Associate
EAP Identity Request
EAP-Success
STA
AP
Authentication Server
EAP Auth Response
EAP Auth Response
EAP Auth Request
EAP Auth Request
EAP Identity Response
EAP Identity Response
Authentication traffic
Normal Data
Port Status:
EAP-Success

## Slide 34: EAP Framework
EAP provides a flexible link layer security framework
  Simple encapsulation protocol
    No dependency on IP
    ACK/NAK, no windowing
    No fragmentation support
  Few link layer assumptions
    Can run over any link layer (PPP, 802, etc.)
    Assumes no re-ordering
    Can run over lossy or lossless media
      Retransmission responsibility of authenticator (not needed for 802.1X or 802.11)
EAP methods based on IETF standards
  Transport Level Security (TLS) (supported in Windows 2000)
  GSS_API (including Kerberos)
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 35: EAP-GSS and IAKERB
EAP-GSS (draft-aboba-pppext-eapgss-02.txt)
  Use of GSS_API authentication methods within EAP
IAKerb (draft-ietf-cat-iakberb-05.txt)
  GSS-API method enabling proxy Kerberos
  STA not able to talk to KDC directly prior to authentication
  Initial authentication
    IAKERB enables STA to obtain TGT, Ticket to AP
  Handoff
    Ticket to AP

## Slide 36: Advertising Security Options
Modeled on “supported rates”
AP advertises security options in probe response
  Placed in probe response only if STA requests it in probe request
STAs collect this information prior to associations and can make association and roaming decisions based upon it

## Slide 37: Selecting security options
STA requests security options in association request from available options contained in probe response
AP accepts/rejects association based on request contents
No additional protocol handshakes necessary
  No impact on roaming performance

## Slide 38: Initial Contact
Associate
EAP Identity Request
EAP Identity Response
EAP-GSS Request (Empty)
EAP-GSS Response (IAKERB: AS_REQ)
AS_REQ
EAP-GSS Response (IAKERB: TGS_REQ)
TGS_REQ
EAP-GSS Request (IAKERB: TGS_REP)
TGS_REP
EAP IAKERB Response (Empty)
EAP-Success
EAP-Key (AP_REP)
EAP-Key (AP_REQ)
STA
AP
KDC
AS_REP
EAP-GSS Request (IAKERB: AS_REP)

## Slide 39: Operational Details
Authentication method defaults to IAKERB
  STA can attempt SPNEGO
  AP can choose IAKERB if it doesn’t support anything else
EAP-Key packets passed up and down via driver interface and 802.11 SAP
  On STA, GSS_API implementation needs to be able to generate AP_REQ, send it down to driver
  On AP, need ability to validate received AP_REQ, force 802.1X controlled port into authorized state
802.11 encryption turned on after AP_REQ/AP_REP exchange
  AP turns on encryption after sending AP_REP
  STA turns on encryption after receiving AP_REP
  If EAP-Key exchange occurs prior to completion of 802.1X, then part of the 802.1X exchange may be encrypted!

## Slide 40: Security Services
Authentication of client to KDC (TGS_REQ)
  PADATA typically NOT used with AS_REQ!
Authentication of KDC to client (AS_REP, TGS_REP)
Session key for client-AP communication (TGS_REP, AP_REQ)
TGT, Session key for client-KDC communication (AS_REP)
Authentication of client to AP (AP_REQ)
Authentication of AP to client (AP_REP)

## Slide 41: Roaming Within Realm
Reassociate
EAP-Success
EAP-Key (AP_REQ)
EAP-Key (AP_REP)
STA
AP
KDC
Assumes: APs can share identity and key

## Slide 42: Security Services
Authentication method defaults to IAKERB
802.11 encryption turned on after AP_REQ/AP_REP exchange
Authentication of client to KDC (TGS_REQ)
Authentication of KDC to client (AS_REP, TGS_REP)
Session key for client-AP communication (TGS_REP, AP_REQ)
TGT, Session key for client-KDC communication (AS_REP)
Authentication of client to AP (AP_REQ)
Authentication of AP to client (AP_REP)

## Slide 43: Agenda
Introduction and Goals
802.11 Security Today
What’s Wrong Today?
Proposed Encapsulation
Proposed Authentication, Authorization, and Key Management
Summary

## Slide 44: Summary
802.11 security doesn’t meet any of its security objectives today
802.11 TGe is working to replace
  Authentication scheme using 802.1X and Kerberos
  Encryption scheme using AES in OCB mode
More to come
  “The paint’s not dry”

## Slide 45: Feedback?