## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Selective Hopping for Hit Avoidance
Date Submitted: January 18, 2001
Source: KC Chen, HK Chen, CC Chao
Company: Integrated Programmable Communications, Inc.
Taiwan Laboratories Address: P.O. Box 4-2, Chupei, Hsinchu, Taiwan 302
TEL: +886 3 553 9128, FAX: +886 3 553 9153, E-Mail: {kc,hkchen,ccc}@inprocomm.com
Re: original document.
Abstract: Submission to Task Group 2 for consideration as the coexistence mechanism for 802.15.2
Purpose: Description of Proposal
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Selective Hopping for Hit Avoidance
KC Chen, HK Chen, CC Chao
Integrated Programmable Communications, Inc.

## Slide 3: Scenarios
Co-existence of 802.15 and 802.11 DS
  SCO in 802.15 is more sensitive in co-existence
Frequency hopping still follows FCC’s regulations
Other co-existence scenarios are not considered in this document
  Other FH at 2.4G Hz band
  Other DS at 2.4G Hz ISM band
  Shall be considered later
    Principle is applied.
    Procedures need more definitions.

## Slide 4: Frequency Arrangement of IEEE 802.11b and 802.15
802.11b Channel Number | Central Frequency (MHz) | Range (MHz) | Corresponding Bluetooth Channel Numbers
1 | 2412 | 2400-2424 | 0-22
6 | 2437 | 2425-2449 | 23-47
11 | 2462 | 2450-2474 | 48-72

## Slide 5: Frequency Partition
Partition Number | Corresponding Bluetooth Channel Number | Total Channel in the Partition | Corresponding 802.11 Channel Number
1 | 0-22,75-77 | 26 | 1
2 | 23-47,78 | 26 | 6
3 | 48-72,73-74 | 27 | 11

## Slide 6: Two-Layer Hopping Sequences
In case 802.15 hopping channel is within the frequency range of a 802.11 DS transmission
  Preferred (no DS interference) and non-preferred (under DS interference) bands
  Select one partition sequence from a set of possible ones.
  Original sequence is mapped into a new sequence according to the selected partition sequence.

## Slide 7: An Example of Mapping Original Sequence by Partition Sequence
23 | 22 | 53 | 40 | 57 | 42 | 21 | 36 | 25 | 38 | 27 | 63
2 | 1 | 3 | 2 | 3 | 2 | 1 | 2 | 2 | 2 | 2 | 3
1 | 1 | 2 | 2 | 3 | 3 | 1 | 1 | 3 | 3 | 2 | 2
75 | 22 | 27 | 40 | 57 | 69 | 21 | 10 | 52 | 65 | 27 | 37
Partition sequence
Corresponding partitions of original sequence
Original hopping sequence
Hopping sequence after mapping
P1 | P2 | P3
Colors

## Slide 8: An Example of Partition Sequence and Traffic
Tsco and Dsco are parameters of SCO traffic defined in the Bluetooth specification.

## Slide 9: An Example of Partition Sequence and Traffic (Cont.)
This partition sequence can be selected if
  EX1: a DS device is found in partition 2, and we want to build a full-duplex HV2 SCO link, Tsco=4, Dsco=0,1.
  EX2: a DS device is found in partition 1, and we want to build two full-duplex HV3 SCO links, Tsco=6, Dsco=2,3 and 4,5.

## Slide 10: Remarks
Uniform channel utilization can be achieved by uniform partition utilization and appropriate mapping.
A partition sequence with uniform partition utilization:
  Uniformly uses partitions in the whole sequence
  However, could use partitions non-uniformly if only the selected slots of the sequence are considered
SCO traffic reserves slots in a regular manner and can be fitted into partitions with no interference by properly selecting the partition sequence.
If a DS device is present in one partition, traffic up to 2/3 of channel capacity can be supported in this manner.
A set of partition sequences can be designed for optimal use in various interference situations and traffic requirements.

## Slide 11: Selective Hopping Avoidance System Architecture
Frequency Synthesizer
Multiplexer
Partition mapping re-mapping
Hopping sequence generation
Original/Mapped sequence selection
Partition sequence generation
Partition sequence selection procedure
RSSI (& 802.11b locking detection)
Demodulation with interference suppression
Error
Check
Interference identification
Traffic requirement
Hopping clock
RF input signal
Partition sequence change procedure
Packet target
Uniform channel usage requirement
Optional indicator
of 802.11 DS from
the 802.11-802.15
integrated device

## Slide 12: Interference Identification
It consists of
  Instantaneous interference detection: interference-free or not
    Checks of received packet and power level
    Utilization of channel silent duration between channel active time
    RSSI and Signal Locking as CCA in 802.11
  Hit ratio measurement
    Counting the interference ratio for each partition

## Slide 13: Partition Sequence Selection Under Uniform Channel Utilization
For partitions with interference hit ratios below threshold, corresponding hit ratios are set to be zero.
From the time slots reserved by the traffic requirements, calculate the partition usage vector for partition sequences.
Calculate the average hit probability H(p) for each type p of partition sequence
Select the partition sequences with minimal H(p)
If more than one in step 4, select the most evenly used one

## Slide 14: Partition Usage Vector
The partition usage vector U(p) is calculated for a partition sequence p given the time slots reserved by traffic requirement.
The k-th element of U(p), uk(p), is proportional to the relative frequency of partition k in the reserved time slots.

## Slide 15: Average Hit Probability
The average hit probability H(p) for each sequence with given traffic requirement is
where Np is the number of partitions,
R(k) is the measured hit ratio of the k-th partition,
uk(p) is the k-th element of the partition usage vector of the partition
sequence p.

## Slide 16: Multiple Partition Sequences with Minimal H(p)
If more than one sequences are with the same minimal value H(p), select the sequence that most evenly uses the partitions. This is done by selecting the sequence of type q with

## Slide 17: Partition Sequence Change Procedure
After the device decides to apply a new partition sequence, it starts to communicate with all its peers.
  Negotiate with peers to change to new hopping sequence
  In case no support of co-existence in peers, original sequence is still used.

## Slide 18: Original/Mapped Sequence Selection
Designed for backward compatibility
  Allowing original sequence and mapped sequence co-existing in a pico-net.
  Master selects an appropriate sequence based on the targeting receiver(s).
  A simple directory records
    Peers
    802.15.2 compliance or not
    Sequence used

## Slide 19: Partition Sequence Generation
One table contains all possible types of sequences.
To reduce implementation complexity, a small set of partition sequences, containing enough sequences to optimize hit probability for any combination of interference and traffic situations, is desired.
  For 802.15, SCO traffic has the highest priority need using partition sequences.
It can be generalized to all co-existing environments.

## Slide 20: Traffic Requirement

## Slide 21: Example of Partition Usage Vector
Partition sequence= Repeating {1 2 3 1 3 2}, time unit= 2 slots

## Slide 22: A Set of Partition Sequences

## Slide 23: Remarks
A set of partition sequences with reasonable size while it is enough for considered traffic requirements and interference situations.
Uniform channel utilization is achieved by selection of sequences in the uniform subset.
Allow non-uniform channel utilization by selecting among the uniform and non-uniform subsets.
Change of FCC rule is not required; and the scheme also applies and could have extra performance benefits in case of FCC rule change.

## Slide 24: Partition Mapping
Mod Nj
Mapping table of P3
Channels in Pj
P1
P2
P3
Nj
Select one table among the three
Selected channel number of original hopping sequence
Partition sequence

## Slide 25: Rearrangement as an Alternative of Sequence Generation
Temporary re-arrangement of pre-determined N channels of hopping sequence
  Taking advantage of interference duty cycle
  Can also be used for smaller ISM bandwidth at certain countries.
  Algorithm:
    Determine coming hopping channel suffering interference of a 802.11 DS transmission.
    Create the segment of upcoming N elements in the hopping sequence. Initial suggestion: N=4-8.
    Move those in the interference band to the end of the segment. The rest of sequence is kept the same.
    Inform/negotiate peer(s) as our earlier procedure.

## Slide 26: A Rearrangement Example
Assume 9 channels 0-8, divided into 3 partitions,P1={0-2},P2={3-5},P3={6-8}.
Interference at P1
Interference at P1
Idle time
of interference
7
3
2
6
0
5
1
8
4
5
2
6
Original hopping sequence
Rearranged segment of N=6
7
3
8
6
5
0
1
2
4
5
2
6
Rearranged hopping sequence

## Slide 27: Remarks
Rearrangement can be applied as an independent mechanism from the idea of partition sequence.
Rearrangement can also be jointly applied with partition sequence. In this case, it could be applied to the mapped sequence, and slots that have been protected by the partition sequence should not be re-arranged.

## Slide 28: ACL Link Considerations
The partition sequences are mainly designed to protect SCO traffic from interference.
In case of a DS device in a partition, each uniform partition sequence could protect up to 2/3 of its traffic capacity from interference. If SCO traffic does not fulfill it completely, ACL traffic can take advantage of the rest of it.
Rearrangement also helps to protect ACL traffic.

## Slide 29: Features of Selective Hopping Avoidance
Backward compatible (in function)
Meeting FCC regulations
  Global consideration
Traffic based
  Primarily SCO in 802.15
  Re-arrangement as an alternative
Just being extra module in implementation, that is, backward compatible in implementation
  Simple and no other new functions from 802.15/11
  Considering (802.11/802.15) integrated devices

## Slide 30: Response to Evaluation Criteria (I)
Collaborative or Non-collaborative
  Its default setup is non-collaborative but collaborative is also defined.
Improved WLAN and WPAN Performance
  WPAN throughput increases
  WLAN BER improves
Impacts on Standards
  Minimum change (ACL & SCO) in WPAN
Regulatory Impact
  None (for 79 bands & 23 bands)
Complexity
  One extra implementation module in link-layer

## Slide 31: Response to Evaluation Criteria (II)
Interoperability with Systems that do not include co-existence mechanism
  Yes
Impact on Interface to Higher Layers
  none
Applicability to Classes of Operation
  Yes, actually class independent.
Voice and Data Support in Bluetooth
  Yes, special design for SCO
Impact on Power Management
  none