## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [MAC proposal for the Low Rate 802.15.4 Standard]
Date Submitted: [10 March, 2001]
Source: [Ed Callaway] Company: [Motorola]
Address: [8000 W. Sunrise Blvd., M/S 2141, Plantation, FL 33322]
Voice:[(954) 723-8341], FAX: [(954) 723-3712], E-Mail:[ed.callaway@motorola.com]
Re: [WPAN-802.15.4 Call for Proposals]
Abstract: [This presentation represents Motorola’s proposal for the P802.15.4 MAC standard, emphasizing the need for a low cost system having excellent battery life.]
Purpose: [Response to WPAN-802.15.4 Call for Proposals]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: MAC Proposal for the Low Rate 802.15.4 Standard
Ed Callaway, Member of the Technical Staff
Motorola Labs
Phone: +1-954-723-8341
Fax: +1-954-723-3712
ed.callaway@motorola.com

## Slide 3: 15.4 is Different!
Assumptions
M2M is a major market that needs to be addressed.
Requirements differ from those of other WPANs
  More emphasis on longer battery life and lower cost.
  Less emphasis on message latency, channel capacity, and QoS.
  Support for larger space and device numbers.
  Location determination.
Since the requirements are different, the design should be, too!

## Slide 4: Cluster/Mesh Network
Suitable for a large number of devices (Scalable)
CH2
CH3
CH5
CH4
CH6
Cluster ID = 2
Cluster ID = 4
Cluster ID = 3
Cluster ID = 5
Cluster ID = 6
8
1
2
3
5
6
A
DD
1
0
2
3
4
6
7
8
12
10
11
9
13
14
20
22
5
CH1
Cluster ID = 1
1
2
3
4
5
6
7
Cluster ID = 0
9
All devices are physically identical, except the “Designated Device” Gateway

## Slide 5: Network Formation
A “Designated Device” (Gateway) initiates network formation by designating Cluster Head 0 (which may be separate from the DD).
DD
1
0
2
3
4
6
7
8
12
10
11
9
13
14
20
22
5
CH1
Cluster ID = 1
1
2
3
4
5
6
7
Cluster ID = 0
9
Network grows via inquiry/inquiry scan technique, similar to 15.1.
Each device is assigned a network address composed of the Designated Device ID, Cluster ID, and Device ID (total of 24 bits).
Designated Device assigns Cluster IDs; cluster heads assign device IDs.

## Slide 6: Routing
Each node maintains a “neighbor list” of devices it can hear (designating its parent), plus a list of children.
Nodes overhear network maintenance messages to identify children and the route to them.
First step in routing algorithm is to check the neighbor list; if destination is on the list, message is sent directly (“wormhole routing”).
Otherwise, message is sent to the parent; process is repeated until a node is reached that has the destination as a child (or on its neighbor list).

## Slide 7: Network Frame
To lower power consumption, node duty cycle is reduced to 0.1%.
However, for an asynchronous system, two nodes are unlikely to be simultaneously active.
Further, to achieve the low cost goal, inexpensive time base elements (preferably ceramic resonators or, ideally, MEMS devices) are desired, which have relatively poor frequency stability.
1 ms
1 s
T
x
R
x
1 ms
1 ms
1 s
T
x

## Slide 8: Aloha Statistics
  With short (1 ms) transmissions, collisions are unlikely.
  A liability (poor reference stability) is turned into an asset (randomized transmission timing).

## Slide 9: Dedicated Mediation Devices
To enable nodes to synchronize, Mediation Devices (MDs), which can record and replay messages, are dispersed throughout the network.
Dedicated MDs receive for a period of time (e.g., 2 s), transmit as needed, sleep, then repeat the process
MDs, like telephone answering machines, are simple: They must record and replay simple control words such as who is transmitting, who is desired, timing information, and perhaps short messages.
Receive
Receive
Receive
Tx
Tx
(sleep)
(sleep)
2 s
2 s
2 s
N s
N s

## Slide 10: Aloha, M.D.
Periodically each idle device in the network transmits an “Any traffic for me?” message.
The MD receives these messages, noting the time each was sent, and sends appropriate replies when the receiver of each node is active.

## Slide 11
A
B
MD
Node A sends an “I have traffic for node B” message, but B is sleeping. The MD intercepts node A’s message, including timing information.
When node B checks in with the MD, it finds out that A has a message, and when A will try to contact again.
Node B now knows A’s schedule, so they can now sync on the same time slot and start communication.
MD
Node A
Node B
MD Listen
1 s
1
2
2
3

## Slide 12: Distributed Mediation Devices
As a variation of the dedicated mediation device, the functionality of the MD can be distributed among all nodes in the network.
Each node becomes an MD at a random time, then returns to normal operation.
The frequency with which a node performs the MD function depends on several factors, including:
  Desired battery life
  Latency requirements
  Number of nodes in the network

## Slide 13: MAC Size
Software implementation of:
  Rx packet recovery, addressing, system timing
  Tx packet construction, addressing, system timing
  Mediation Device function
Requires:
  32 kB ROM
  4 kB RAM
  30 k gates CPU core (overkill)
1.8 mm2 in 0.18 um standard CMOS

## Slide 14: Vision
IEEE Standards have an obligation to support industry direction and emerging market opportunities.
Location determination and remote sensing of inventory alone is a $25 billion market, growing at 15 to 20% per year … industrial control and monitoring is larger still.
These markets cannot be met with existing star networks, due to cost and power concerns.
In this case, we must produce a standard that supports:
  applications requiring ultra-low cost & low energy nodes.
  applications that require large node numbers and scalability.
  node location determination.
An innovative solution is needed, and we believe that the Aloha MD approach is that solution.

## Slide 15
Criteria 1

## Slide 16
Criteria 2

## Slide 17
Criteria 3

## Slide 18
Criteria 4