## Slide 1
Submission Title: [Empirical Study for 802.11 b & Bluetooth Coexistence]
Date Submitted: [14th March’2001]
Source: [Vinay Mitter/Ivan Howitt] Company [University of Wisconsin-Milwaukee]
Address[Wireless & Signal Processing Lab,PO Box 784,Milwaukee-WI-53201]
Voice:[1-414-229-2257], FAX: [Add FAX number], E-Mail:[mitter@uwm.edu]
Re: [Empirical Study for Co-existence of 802.11 b and Bluetooth : IEEE802.15-00/00148 TG2 ]
Abstract: [Results of Empirical Study for evaluating coexistence of 802.11b and Bluetooth]
Purpose: [To help in coexistence modeling and validate simulated results for specific scenarios ]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)

## Slide 2: Empirical Study for IEEE802.11 b WLAN & Bluetooth Coexistence in UL Band*
Vinay Mitter1,Ivan Howitt2,Jose Gutierrez3
1,2 Wireless & Signal Processing Laboratory
Electrical Engineering & Computer Science Department
University of Wisconsin - Milwaukee PO Box 784 Milwaukee, WI 53201
3 Eaton Corporation - Innovation Center
Phone: (414) 229-2247 Fax: (414) 229-2769 Email: mitter@uwm.edu, howitt@ee.uwm.edu
URL: www.uwm.edu/~howitt
* The work was sponsored by Eaton Corporation

## Slide 3: UWM Co-existence Research Goals
Insight into operation of Bluetooth and WLAN
Analytical Model for
BT’s Impact on 802.11b
802.11b’s Impact on BT
“Arbitrary” Coexistence Scenario
Examine Coexistence Under Specific Scenario vs. Identify Scenarios Where Coexistence is Impacted
Empirical Study
  Find key Parameters
  Validate Coexistence Model
General Test Bed – For evaluating Coexistence between WPANs & WLANs
Focus of
Presentation

## Slide 4: Issues -Addressed : 802.11b & BT
Impact on Network Performance
Pr[C] - Collision Probability, i.e, event resulting in packet retransmission
  Time
  Frequency
  Relative Power
1 MHz
Frequency
time
20 MHz
802.11b Packets
BT Packets
Collision

## Slide 5: Empirical Study - Outline
Insight 802.11 & BT Operations
Evaluating key parameters
Issue Addressed - Effect of co channel & adjacent channel interference (BT on 802.11)
To evaluate co-existence for Specific Scenarios
To evaluate Measures of performances
for One on One TG2 scenarios

## Slide 6
Test Bed - Block Diagram
802.11b Rx
BT Rx
802.11b Tx
BT Tx
Variable Attenuator (0-80 dB,1dB)
Ericsson ROK 101 007
Bluetooth Modules
3dB Power
Adder & Splitters
Tx/Rx Intersil HWB3163
PRISM II IEEE802.11b

## Slide 7: Empirical Study - BT Impact on 802.11
AP
BT
STA
Frequency
time
J/S required to
cause packet
retransmission
J/S = -10 dB

## Slide 8: Analytical & Empirical - Jamming Suppression
Analytical Model
  802.11 DS/SS
  CW Interference
Empirical
  CW Interference
  HP - BT Signal Generator
  Estimated expected packet error rate exceeded 8%

## Slide 9: S/J Threshold for E[PER] > 8 %
Empirical Results for S/J
Vs Frequency offset
Vs 802.11b data rates
for E[PER]> 8%
“ E[PER] : Expected
Packet Error Rate”

## Slide 10
Threshold S/J(max) versus f offset for the BT DH1 packet with
802.11 b interference
0
5
10
15
20
-25
-20
-15
-10
-5
0
5
10
15
f
offset
MHz
S/J ( f
offset
) dB
E[PER]>20%
E[PER]>8%
E[PER] Residual
Frequency
Maximum measured S/J
for expected packet
Packet error rate
Power
I (802.11 b)
S (BT)
Empirical Study – 802.11 b Impact on BT

## Slide 11
0
5
10
15
20
-50
-45
-40
-35
-30
-25
-20
-15
-10
-5
0
5
J
S
(f)
f
offset
MHz
Empirical
Numerical
Analytical & Empirical – Jamming Suppression
JS(f) : Jamming Suppression
for BT Receiver for
802.11 b Interference
as a function of foffset
Non Hopping

## Slide 12
6
8
10
12
14
16
0
10
20
30
40
50
60
70
80
90
100
S/J ( at f
offset
=0 ) dB
E[PER] %
dh3
dm5
dh1
dm3
dm1
foffset
S (Bluetooth) in dBm at foffset = 0
I ( 802.11 b) in dBm
11 Mbps
E [ PER ] for Various BT ACL Types
E [PER] : Expected Packet Error Rate

## Slide 13
6
8
10
12
14
16
0
0.5
1
1.5
S/J ( f
offset
) dB
Residual BER %
dh3
dm5
dh1
dm3
dm1
foffset
S (Bluetooth) in dBm at foffset = 0
I ( 802.11 b) in dBm
11 Mbps
Residual BER for Various BT ACL types

## Slide 14
Empirical Study for Specific Scenarios
Goals :
Evaluate co-existence for :-
IEEE 802.11b Interference on Bluetooth
Blue tooth Interference on 802.11 b
Validate Simulated and Analytical Models
Outline :
Empirical Test Methodology
Scenario Test Overview
802.11b on BT
BT on 802.11b
Results
Scope of tests

## Slide 15
Test Methodology - Specific Scenarios
802.11b Rx
BT Rx
802.11b Tx
BT Tx
Inputs :
Packet size
Packet Delay
Data Rate
Outputs :
PER
Throughput
Inputs :
Packet Type
Packet Delay
Nos of Packets
Output :
Residual BER
Nos of Packets lost
Residual PER
Total PER
Variable Attenuator (0-80 dB,1dB)
x dB = Path Loss in dB

## Slide 16
Scenarios Test Overview for BT on 802.11b
Bluetooth ( FH ‘Interfere I’ )
HV1 Packets
802.11 b ( DSSS Desired Signal ‘S’)
Packet Payload 1000 Bytes
Pkt Delay 1
No RTS / CTS , No Retransmissions, Fixed Transmitted
Data Rate (11 Mbps), Number of Trials / Packets : 1 X 106 numbers
Measure of Performance :
Probability of Packet Loss : represents the number of packets lost/in error divided by the total number of packets sent

## Slide 17
Packet Loss : BT on 802.11 b
0
0.5
1
1.5
2
2.5
3
3.5
4
4.5
5
5.5
6
0
5
10
15
20
25
30
35
40
45
50
Total Packet Loss for 802.11 b with BT Interference
Distance of WLAN station from BT slave in mtrs
PER %
BT HV1
BT Slave(0,0)
Tx Power 0 dBm
802.11 Access Point (0,15)
BT Master(1,0)
Tx power 0 dBm
WLAN Station
25 mw
(0,d)
Using propagation model as suggested by TG2
“Kammerman Model(IEEE 802.11 00/162)”

## Slide 18
Scenarios Test Overview for 802.11b on BT
802.11 b ‘DSSS’
Packet Payload ( 1000 Bytes )
Pkt Delay 1
No RTS/CTS , No Retransmissions, Fixed Transmitted Data Rate (11 Mbps),No ACK
Bluetooth (Frequency Hopping)
Different ACL packets DM1, DM3, DM5 & DH1
Measures of Performance :-
Probability of Packet loss : Represents the number of packets lost divided by the total
number of packets sent ‘or’ It represents scenario where packet has to be
retransmitted. Packet Loss is sum of Packets with errors in CAC or header &
packets where bits are in error after applying error correction if applicable
Residual BER : % age Bits in error in received packets

## Slide 19
Packet Loss : 802.11 b on Bluetooth
BT Master 0 dBm
(0,7)
BT Slave
Receiver
802.11 Interferer
(0,d) 25 mw
7 meters
(0,0)
Using propagation model as suggested by TG2
“Kammerman Model(IEEE 802.11 00/162)”
1
1.5
2
2.5
3
3.5
4
4.5
5
5.5
0.15
0.20
0.25
0.30
0.35
0.40
0.45
0.50
0.55
0.60
0.65
Total Packet Loss for BT with 802.11 b Interference
Distance of BT slave from WLAN source in mtrs
Probability of Packet Loss
DM1
DM5
DM3
DH1

## Slide 20
BT Slave (0,0)
802.11 Interferer
(0,d)
7 meters
Residual BER : 802.11b on Bluetooth
BT Master
(0,7)
1
1.5
2
2.5
3
3.5
4
4.5
5
5.5
0
0.5
1
1.5
2
2.5
3
3.5
4
4.5
5
5.5
6
6.5
7
Res. BER for BT in Presence of 802.11b
Distance of Bluetooth Slave from WLAN source
Residual BER %
DM1
DM5
DM3

## Slide 21: Relating Empirical Results to Scenarios
Fixed RF Environment
  Single Scenario
  Scenario Variations
Variations in RF Environment
  Shadowing
  Shadowing Impact on Scenario
  Key Issue - “S/I at the System Under Test”
  “SIR provides link for evaluating performance - Independent of Specific Scenario”
BT Tx
@ (0,x)
802.11 Interferer
5 m

## Slide 22
Coexistence for Multiple Topologies
Residual BER %
0
0.2
0.4
0.6
0.8
1
1.2
2
4
6
8
10
12
14
1
1.5
2
2.5
3
3.5
4
4.5
5
Distance of 802.11 interfere from BT Receiver (m)
Distance of BT transmitter from BT receiver (m)
Res BER < 0.1
Res BER>0.3
Res BER for BT DM1 in presence of 802.11 b
BT Transmitter (0,x)
802.11 Interferer
5 m

## Slide 23: RF Propagation
Expected Path Loss
  Attenuation for Tx to Rx separation, d
  Installation dependent
Shadowing
  Attenuation variation, independent of, d
  Installation dependent
Coexistence
  Desired Rx & Interference Rx Scenario Dependent

## Slide 24: Empirical Results Summary
Empirical Measurements
  Key Parameters
    Jamming Suppressing Vs Frequency Offset
    802.11b on BT & BT on 802.11b
  One on One Scenarios
    802.11b on BT
    BT on 802.11b
Mapping Empirical Results into Arbitrary one on one scenario
  SIR for desired MOP

## Slide 25: Additional References
Ivan Howitt, “WLAN and WPAN Coexistence in UL Band,” In Review, Transactions on Vehicular Technology.
Ivan Howitt, “Bluetooth Performance in the Presence of 802.11b WLAN,” In Review, JSAC.
Ivan Howitt, Vinay Mitter, Jose Gutierrez, “Empirical Study for IEEE 802.11 and Bluetooth Interoperability,” IEEE Fall,Rhodes’2001.
Ivan Howitt, “IEEE 802.11 and Bluetooth Coexistence Analysis Methodology,” IEEE VTC Fall,Rhodes 2001.
Vinay Mitter,Ivan Howitt ,Jose Gutierrez,” Empirical Study for performance analysis of Blue tooth in presence of WLAN Interference,”In Review IEEE VTC Spring 2001
Ivan Howitt,Vinay Mitter “ Analytical Tools for Evaluating Co-existence in UL Band ” IEEE802.15-01/032r0