## Slide 1: Proposal for Non-Collaborative BT and 802.11b MAC Mechanisms for Enhanced Coexistence
Jie Liang
Texas Instruments Incorporated
12500 TI Blvd.
Dallas, Texas 75243
(ph) 214-480-4105
(email) liang@ti.com

## Slide 2: Outline
Summary of our ACL proposal
Focus on updated proposal to improve the BT voice link quality while improving 802.11b throughput
Proposals for improving BT voice links:
  Selecting HV3 packet as default packet type for SCO link
  Enhanced voice link: allow Master flexibility to search for best TX slots given delay requirement
Simulation results that confirm significant improvement in throughput for both BT and 802.11b

## Slide 3: Summary of ACL Proposals
Adaptive packet type selection considering slot time,
FEC, CRC based on channel condition and QoS:
DM1, DM3, DM5, DH1, DH3, DH5,AUX1
Adaptive packet payload length selection: fragmentation
Adaptive link configuration: flow control, rate control

## Slide 4: SCO Link Coexistence Problems

## Slide 5: SCO Link Coexistence Problem and Scenarios
A serious problem that needs urgent solutions
  Voice applications are among the most important applications for BT
  Significant packet losses for BT SCO links under 802.11b interference
  Significant throughput drop for 802.11b network
Scenarios
  Separated > 10 feet: minor problem
  Problem when <10 feet distance
  Also dependent on 802.11b duty cycle

## Slide 6: Key Ideas
HV3 packet type is the most coexistence friendly compared with HV1 and HV2 packets
Allow the master to search for the best TX slots given a delay requirement

## Slide 7: Voice Payload and SCO Packets
QoS requirement of voice payload:
  PCM coding: 10-4 (random errors) good quality is retained
    10-3 start to notice artifacts, but still acceptable
  CVSD coding: 10-3 good quality is retained
    10-2 start to notice artifacts, but still acceptable
  Perceptible errors mostly come from collisions (really high BER or fail to decode the BT packet header)
HV1 vs. HV2 vs. HV3
  Packet payload length: 80, 160, 240 bits (1.25ms, 2.5ms, 3.75ms)
  Tsco = 2, 4, 6
  FEC 1/3, 2/3, none

## Slide 8: 802.11b Channel Access Timing
Busy Medium
DIFS
Back-off Window
Medium Idle
New Frame
ACK
Frame Exchange Sequences
Tcp
SIFS
Tbf
SIF= 10us DIF = 50us aSlot_time = 20us
Tbf = N x aSlot
Tf=PLCP Preamble + Header = 192us
Minimum Time Needed (no back-off and payload):
Tm= DIFS+Tf+SIFS+Tf=50+192+10+192=444us
500bytes Payload (add back-off and Payload at 11Mbps):
T=16xaSlot+Tm+400=1164us
Note: needs about 2 BT Slot time for transmitting one average packet
for 11Mbps 802.11b (a block of time is needed by 802.11b)

## Slide 9: Adaptive SCO Link Configuration
Proposal: Use HV3 packet as default (more co-existence friendly)
Leave more time for 802.11 transmissions
Lack of FEC in HV3 is not problem
  high tolerance of random BER
  FEC does not help during collision
Transmit less often – good for saving power
HV1 Traffic
HV3 Traffic

## Slide 10: Enhanced Voice Link (1)
New SCO packet type – EV3:
  no FEC
  240 bits payload
  One EV3 packet for every 6 slots (delay<3.75ms)
  Slave will only transmit when addressed by master
    Only master needs to do the scheduling
    Make sure only one pair of slots are used
  CRC: could be another option, which accommodate applications that want data integrity on voice data
Why:
  Flexible in traffic scheduling to avoid collisions (no fixed intervals)

## Slide 11: Enhanced Voice Link (2)
Enhanced Voice Link Setup:
new EV3 packet type, payload size: 240 bits
Npoll: <6 slots
Adaptive selection of transmitting slots based on channel conditions
Delay < 3.75ms
EV3 Traffic
HV3 Traffic
B
B
G
G
G
G
B
G
B
B
G
G
G
G
B
G

## Slide 12: Algorithm for Selecting TX Slots
  Score(n) = 0, if hop(2*n) and hop(2*n+1) are both bad channels
  1, if hop(2*n) is bad and hop(2*n+1) is good
  2, if hop(2*n) is good and hop(2*n+1) is bad
  3, if both are good channels
  TxSlot=0; MaxScore=0;
  For(n=0;n<3;n++)
  if(Score(n)>MaxScore)
  TxSlot=2*n;
  MaxScore = Score(n);
B
B
G
G
B
G
0
1
2
3
4
5
hop
score
0
3
1
Selecting a pair of slots
with the maxim score

## Slide 13: Simulation Results
OPNET models for 802.11b and BT baseband
Only considered collisions in radio link:
  In-band packets that overlap in time result in collision
  Collision meant packet loss
  Valid assumption for the considered scenario (<3 feet separation) and voice payload’s tolerance for random errors
Two 802.11b stations and two BT stations in simulations

## Slide 14: OPNET Scenario

## Slide 15: Simulation Results – Key Points
Note changes from first 15 sec (BT silence) to the second 15 sec
Note that the enhanced voice link always outperforms HV3 and HV1 links for both BT throughput and 802.11b throughput
Note that HV3 is better than HV1 for coexistence
Note that the changes in behavior when loads on 802.11b networks change (from 5Mbps ->2Mbps
->200k)

## Slide 16: HV1 Packet
WLAN Load:
5 Mbps

## Slide 17: HV3 Packets
WLAN Load:
5 Mbps

## Slide 18: Enhanced Voice Link
WLAN Load:
5 Mbps

## Slide 19: BT Master-Slave Throughput
WLAN Load:
5 Mbps

## Slide 20: 802.11b Throughput
WLAN Load:
5 Mbps

## Slide 21: BT Master-Slave Throughput
WLAN Load:
2 Mbps

## Slide 22: 802.11b Throughput
WLAN Load:
2 Mbps

## Slide 23: BT Master-Slave Throughput
WLAN Load:
200kbps

## Slide 24: 802.11b Throughput
WLAN Load:
200kbps

## Slide 25: Conclusions (1)
Proposals for enhancing voice links for BT:
  HV3 packet as default SCO packet type
  Enhanced voice link using new EV3 packet
Extensive simulation data demonstrates that the proposed methods significantly improve coexistence performance
No changes to the current BT specs, just new usages
Easy implementation through software upgrades

## Slide 26: Conclusions (2) Evaluation Questionnaires
Non-Collaborative
Impact on Standards:
  New SCO packet type
Regulatory Impact:
  None
Complexity:
  Software upgrade for most implementations
Interoperability with Non-coexistence Devices:
  Drop back to HV3 packet for non-coexistence devices

## Slide 27: Conclusions (3) Evaluation Questionnaires
Classes of Operations:
  Both PCF and DCF for 802.11b
  Voice payload for BT
Voice and Data Support:
  Voice
Impact on higher layer:
  Mostly none
Impact on Power Management:
  None