## Slide 1
NOTE: Update all red fields replacing with your information; they are required. This is a manual update in appropriate
fields. All Blue fields are informational and are to be deleted. Black stays. After updating delete this box/paragraph.
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: TG4 RFWaves MAC Proposal Overview
Date Submitted: 8 March, 2001
Source: Barry Volinskey, RFWaves, LTD
Address [Add address Street, City, PC, Province/State, Country]
Voice:+972-3-6344131 FAX: +972-3-6344130 , E-Mail: Volinskey@RFWaves.com
Re:
[If this is a response to a Call for Contributions, cite the name and date of the Call for Contributions to which this document responds, as well as the relevant item number in the Call for Contributions.]
[Note: Contributions that are not responsive to this section of the template, and contributions which do
not address the topic under which they are submitted, may be refused or consigned to the “General Contributions” area.]
Abstract: An overview of the MAC layer proposed by RFWaves for TG4
Purpose: Presentation to TG4 at the HH meeting
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: RFWaves Ltd.
TG4 RFWaves MAC Proposal Overview

## Slide 3: Introduction
RFWaves main interest is in the PHY
The MAC should utilize the PHY to the benefit of the applications
Application segments include:
  Home automation and security
  Industrial automation
  Toys and games
  Controllers and peripherals
  Internet connected appliances
Different requirements!
Market size >> 100M Units a year

## Slide 4: MAC Implementation Requirements
Software should be able to run on a 8bit microcontroller
  Low Power
  Low Cost
ASIC or FPGA can be used in some applications to perform MAC functions

## Slide 5: Suggested MAC Solutions
Low end Master-Slave CSMA – Most Common
  Master has a large power source
  All communication is through the master
Other applications may require different MAC layers:
  High bit-rate applications Master-Slave TDMA
  Symmetric, User initiated, Master-Slave
    Symmetric Power Consumption.
    Example - a network of handheld games

## Slide 6: CSMA, Master-Slave Based MAC
Great for various automation and security applications
One master node with large power source
Master is always in receiving mode
A slave device would burst and wait for ACK from the master
All communication is done through the master node
Do 650uSec between tries to avoid Bluetooth
128 bit packets – 32bit ACK

## Slide 7: Communication Format
Slave unit senses for carrier
If carrier exists – it waits for a random based time of P (other schemes possible) and try to sense again
If no carrier is detected packet is transmitted, going to receive mode immediately afterwards to receive ACK and any packets awaiting
Master sends an ACK immediately and signals the slave to remain in reception if more packets await it

## Slide 8: Communication Format cont.
Failures in receiving ACK result in retransmits with varying delays
Setup phase includes a specific packet with a “new device” address, resulting in a reply from the master containing the address for the device
The master can keep a translation table between real MAC addresses (32 bit) to their network address (8 bit) if needed
If a device does not get replied several times it will go back into the setup phase

## Slide 9: Packet Structure
Example packet structure – Long packets
  Preamble (8 bit)
  Source Address (2-4 byte)
  Destination Address (2-4 byte)
  Packet type (8 bit)
    IP, ACK, last packet in a buffer, control, etc.

## Slide 10: Packet Structure cont.
  Payload length (8 bit)
  Packet number (8 bit)
  Total length (8 bit)
  Spare (8 bit)
  Payload (up to 256 bit)
  CRC/Checksum (16 bit)
  End byte (8 bit)
Total overhead – 112-136 bit

## Slide 11: Packet Structure cont.
Example packet structure – Short packets
  Preamble (8 bit)
  Source Address (8 bit)
  Destination Address (8 bit)
  Packet type (4 bit)
  Spare (4 bit)
  Payload 0 or 64 bit
  CRC/Checksum (16 bit)
  Stop byte (8 bit)
Total overhead – 56 bit

## Slide 12: Reply to CFA
Applies to both sweet spots of applications
64K Devices
Master-Slave architecture with automatic network initiation and service discovery
Bi-Directional communication
Support both TDMA and CSMA types of communication
Latency for 128bit packet – Less than 1mSec – with retransmissions for errors

## Slide 13: Reply to CFA cont.
Star and Mesh topologies supported by PHY
Several networks can interact in the same area, due to high bandwidth
Battery life – Long – Depending on application
Size – Extremely small – going smaller …
2.4GHz Antenna benefits
No location awareness

## Slide 14: Reply to CFA cont.
10m Range with small, printed antenna and no coding – Longer range available with improved antenna and coding
Global 2.4GHz ISM band
Coexistence in the 2.4GHz ISM band
Technically Feasible (working technology)
Cost
Cost/Performance