## Slide 1: Proposal for Collaborative BT and 802.11b MAC Mechanisms for Enhanced Coexistence
Jie Liang
Texas Instruments Incorporated
12500 TI Blvd.
Dallas, Texas 75243
(ph) 214-480-4105
(email) liang@ti.com

## Slide 2: Outline
Collaborative 802.11b MAC Mechanisms
Collaborative Bluetooth Mechanisms
Coordinator Unit for Resolving 802.11b and BT collisions using statistical contention

## Slide 3: Key Ideas
802.11b and BT collocated devices can reserve TX/RX slots in the channel access timing of each other
Use of virtual contention to resolve conflicting reservation requests

## Slide 4: Key Issues and Goals
Optimize/improve combined throughput
  Minimize the gaps
Maintain fairness between BT and 802.11b devices
Avoid long delays for packet delivery
Adjust to traffic load adaptively:
  No or minimal penalty to throughput when collision probability is low
  Handle bursty data traffic from either 802.11 or BT
Flexibility in allocating throughput of BT and 802.11b
BT
802.11b
Medium idle
time

## Slide 5: Collaborative 802.11b MAC Mechanisms
Modification of 802.11b Channel Access mechanism to incorporate BT timing for collision avoidance
Reserved BT slots are treated the same as “busy medium” in 802.11b channel access
Throughput of 802.11b and BT can be regulated through a coordinator unit (CU) that utilizes statistical contention to resolve conflicts

## Slide 6: Collaborative 802.11b MAC Mechanisms
Channel access:
  jointly determined by 802.11b timing and BT in-band slot timing
Use of fragmentation to fit PSDU between BT in-band slots
Continuous updates from BT MAC regarding BT TX/RX timing
Continuous updates to BT MAC regarding 802.11b TX/RX timing

## Slide 7: Baseline 802.11b Channel Access
CP Channel Access
* Busy Medium: could be from CCA or NAV
DIFS
Busy Medium
DIFS
Back-off Window
Medium Idle
New Frame
ACK
Frame Exchange Sequences
CFP Channel Access
PIFS
D1+poll
SIFS
U1+ack
D2+ack+poll
Frame Exchange Sequences
SIFS
Minimum T for
One successful frame transmission (Tcf)
Tcp
SIFS

## Slide 8: Baseline Channel Access
Contention Period (CP)
    During CP, channel access is obtained mostly through contention (RTS/CTS sequence is another way)
    STA defers transmission when sensing medium busy (medium status determined by both CCA and NAV)
    Each frame must be acknowledged (ACK) – the minimum time for a successful frame transmission is Tcp (current frame+SIF+ACK frame)
Contention Free Period (CFP)
    During CFP, channel access is obtained by CF-POLL
    After receiving a CF-POLL frame, the addressed station transmits and waits for acknowledgement.
    The minimum time for successful transmission of a frame is Tcf (current frame+SIF+next frame with ACK)

## Slide 9: Coexistence 802.11b Channel Access (1)
DIFS
Busy Medium
DIFS
Back-off Window
Medium Idle
New Frame
ACK
Frame Exchange Sequences
BT Reserved
Tcp
PIFS
D1+poll
SIFS
U1+ack
D2+ack+poll
Frame Exchange Sequences
SIFS
Minimum T for
one frame (Tcf)
BT Reserved
CP Channel Access for coexistence
CFP Channel Access for coexistence
SIFS

## Slide 10: Coexistence 802.11b Channel Access (2)
BT In-band slot times (possible collisions) are known well ahead of time
SCO slots are pre-scheduled and known well ahead of time.
When co-located BT is master, all TX/RX timing is known
When co-located BT is slave, ACL TX slot is known about 625us ahead of time and 802.11b can be notified; ACL RX slot is known after decoding the BT packet header (this requires quick notification to 802.11b)
BT should notify 802.11b the TX/RX timing of the current frame after decoding packet header
802.11b should notify BT the TX/RX time of the current frame exchange immediately after known

## Slide 11: Coexistence 802.11b Channel Access (3)
Contention Period:
    When Tw<Tcp_min, the TXOP is too short, do not transmit
    When Tcp_min <Tw<Tn (Tn is the time needed), fragment the current packet to fit in the gap
    When Tw>=Tn, transmit the current frame w/o changes
Contention Free Period:
    When Tw<Tcfp_min, the TXOP is too short, do not transmit
    When Tcf_min <Tw<Tn (Tn is the time needed), fragment the current packet to fit in the gap
    When Tw>=Tn, transmit the current frame w/o changes
Note:
Tw– the transmission window size during CP and CFP

## Slide 12: Collaborative BT Mechanisms
Key Ideas:
    Allow co-located 802.11b device to reserve slot in BT timing
    BT slave can only transmit after receiving packet from BT master and the next slot is not reserved by 802.11b
    BT master should not initiate a packet exchange if the next two slots contain 802.11b reserved slot
    Note: when not restricted by other factors, move piconet master to the collocated BT device.
Features:
    Fully compatible with standard BT devices
    No changes to others parts of BT implementation

## Slide 13: Baseline BT Channel Access
M->S
S->M
M->S
S->M
Master TX in even slots, and slave TX in odd slots
Slave can access the channel only when addressed in the previous slot
Most ACL (except AUX1) packets must be acknowledged in the next
transmission

## Slide 14: Collaborative BT Mechanisms (1)
M->S
S->M
M->S
S->M
Slave should not transmit when its TX overlaps with reserved time slot
Master should not initiate a frame exchange with a slave when the
next two slots contains reserved slot
Slave should generate reservation signal to co-located 802.11b device for
the next S->M slot when it decodes master packet addressed to itself
Master should generate reservation signal to co-located 802.11b device for
the next two slots when it tries to schedule traffic to a BT slave
802.11b Reserved

## Slide 15: Collaborative BT Mechanisms (2)
BT shall update 802.11b device its packet timing immediately after decoding the packet header.
Many methods proposed in the non-collaborative BT proposal still apply here.

## Slide 16: Traffic Regulation through Timing Coordinator Unit
Wireless Medium
BT PHY
802.11b PHY
BT MAC
802.11b MAC
Coordinator
Unit (CU)
802.11b Timing
BT Timing
802.11b Timing
BT Timing

## Slide 17: Coordinator Unit
Regulates traffic of co-located 802.11b and BT devices
Conflicts of overlapping slot reservation from 802.11b and BT can be resolved using virtual statistical contention in CU:
      SCO link will take priority over both ACL and 802.11b traffic
      Dp: threshold between [0,1], D: uniform random variable in [0,1)
        D >= Dp, block 802.11b timing and feed BT timing to 802.11b
        D < Dp, block BT timing and feed 802.11b timing to BT
      Dp can be used for adjust the throughput of 802.11b and BT
Features of Contention-based CU:
    Flexibility
    Fairness (both have opportunities to access the medium through the contention)

## Slide 18: Conclusions (1)
Fairness:
  BT or 802.11b can access medium based on contention
No excess long delays:
  Only a series of unsuccessful contention result in long delay (low probability)
CU can incorporate more intelligent contention criteria:
  Traffic classes, delay bounds, etc.
Easy to adjust throughput biases between BT and 802.11b by changing Dp
Handle bursty traffic:
  When load allows, proposed method automatically allocates more bandwidth to the bursty traffic source

## Slide 19: Conclusions (1) Evaluation Questionnaires
Collaborative
Impact on Standards:
  Channel access for 802.11b and BT to include reservation
  No changes in other parts
Regulatory Impact:
  None
Complexity:
  Simple modification to current channel access implementations
Interoperability with Non-coexistence Devices:
  Fully compatible

## Slide 20: Conclusions (2) Evaluation Questionnaires
Classes of Operations:
  Both PCF and DCF for 802.11b
  All profiles in BT
Voice and Data Support:
  Both
Impact on higher layer:
  None
Impact on Power Management:
  None