## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Media Access Control proposal for the 802.15.4 Low Rate WPAN Standard]
Date Submitted: [March 2001]
Source: [Carl R. Stevenson] Company: [Agere Systems]
Address: [555 Union Boulevard, Room 22W214EQ, Allentown, PA 18109]
Voice:[(610) 712-8514], FAX: [(610) 712-4508], E-Mail:[carlstevenson@agere.com]
Re: [ MAC layer proposal submission, in response of the Call for Proposals ]
Abstract: [This contribution is a flexible MAC proposal for a Low Rate WPAN intended to be compliant with the P802.115.4 PAR. It is intended to support both master-slave and peer-to-peer communications. It can also optionally support node-to-node relay capabilities to provide robust communications in a variety of propagation environments to meet the needs of a wide range of low data rate applications. In its basic form, it can support up to 255 nodes per PAN, but through address extension can be expanded to support a much larger number of nodes.]
Purpose: [Response to IEEE 802.15.4 TG Call for Proposals]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
MAC Layer Proposal Submission to the IEEE P802.15.4 Low Rate WPAN Task Group

## Slide 3
Who is ?
Formerly Lucent Technologies Microelectronics Group
In the process of spinning off as an independent semiconductor company
Extensive experience in communications IC design, DSPs, and wireless systems design

## Slide 4: Description of MAC Layer Proposal (actually a MAC + LLC + at this point)
System Operation
  Half-duplex TDMA/CSMA-CA DAMA/Contention Based Protocol
    Network(s) controlled by master unit(s)
    Beacon from master defines TDMA frame structure
    p-persistent slotted aloha CSMA-CA reservation request slots
    Dynamic bandwidth allocations for time-sensitive traffic
    p-persistent slotted aloha CSMA-CA contention access slots
    Supports time-sensitive and asynchronous traffic through mix of assigned bandwidth and contention access
    Supports master-slave and peer-peer communications
    Possible for slaves to participate in < 1 network
    Possible to have gateways/portals to other dissimilar networks
    Promotes power efficiency through sleep modes

## Slide 5: HDLC-like Packet Structure Supports Protocols
Based on existing ISO/IEEE/other standards
Some SDL exists for similar protocols, which may be reusable with little modification
Transparent to data content
  Allows encapsulation of higher layer protocols between link layer DSAPs
  Does not impose data type dependencies
  Can transport encrypted payloads, if desirable
Small code size and CPU load possible
  Amateur Packet Radio implementations with nearly comparable complexity use 8-bit CPUs & 32k bytes of code
  Additional complexity for TDMA and other features should not be excessive

## Slide 6: Variable Length Packets

## Slide 7: Dynamically-assigned Frame Structure

## Slide 8: Frame Structure Can Vary Frame to Frame to Efficiently Handle a Mix of Traffic Types

## Slide 9: Slaves Can Be Moved to Other Channels Temporarily if Traffic Makes it Desirable

## Slide 10: MAC Implementation Concept (actually a MAC + LLC + at this point)
Substantially “Soft” MAC/LLC Implementation
  Proposal estimates based on synthesizable ARM7 core
  Frame buffers included in PHY size/power estimates
  4k Bytes RAM estimated for data
  128k bytes ROM estimated for MAC/LLC/Application code
  RAM and ROM sizes can be optimized as requirements become more clear
  Peripherals include 16 bits of GPIO & RTC (other options)
  Clock circuitry for scaleable clock rates including very low power ring oscillator for use during deep sleep modes
  Ring oscillator calibrated to master crystal oscillator to minimize clock drift during sleep modes
  Minimal additional support logic
  Application code space and CPU cycles available

## Slide 11: Power Mangement and Battery Life
Masters should generally be line-powered or have << battery capacity than slaves
  Facilitates efficient, reliable network control
  Assures beacons are available regularly for slaves
  Power drain due to processing load becomes insignificant
Slaves can have extended operating life on modest batteries
  Slave devices make use of low power modes
  Master can command slaves into deep sleep mode for multiple superframe intervals to conserve battery power in slave devices which can tolerate latency
  RSSI & link quality based TX power management possible
  Battery requirements/battery life depend on traffic load, TX power, and latency tolerance of a device

## Slide 12: Die Size Estimate - Total Solution (PHY + MAC + Misc)

## Slide 13: Power Consumption Estimate - Total Solution (PHY + MAC + Misc)

## Slide 14: Self-ranking in Comparison to Criteria
Awaiting completion of Criteria Document
Will complete self-ranking matrix in a timely manner when Criteria Document and matrix worksheet become available

## Slide 15: Thank you for your attention.
Any questions?