## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [PHY proposal for the Low Rate 802.15.4 Standard]
Date Submitted: [10 March, 2001]
Source: [Ed Callaway] Company: [Motorola]
Address: [8000 W. Sunrise Blvd., M/S 2141, Plantation, FL 33322]
Voice:[(954) 723-8341], FAX: [(954) 723-3712], E-Mail:[ed.callaway@motorola.com]
Re: [WPAN-802.15.4 Call for Proposals]
Abstract: [This presentation represents Motorola’s proposal for the P802.15.4 PHY standard, emphasizing the need for a low cost system having excellent battery life.]
Purpose: [Response to WPAN-802.15.4 Call for Proposals]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: PHY Proposal for the Low Rate 802.15.4 Standard
Ed Callaway, Member of the Technical Staff
Motorola Labs
Phone: +1-954-723-8341
Fax: +1-954-723-3712
ed.callaway@motorola.com

## Slide 3: Goal
Significantly lower hardware cost and current drain than 15.1.
Hardware cost reduced by:
  Use of Direct Sequence Spread Spectrum (DSSS)
  10 MHz channel separation, to ease channel filter requirements
Current drain reduced by:
  Short synchronization time
  Short message times

## Slide 4: Channelization
2.4 GHz band; 8 channels; 10 MHz channel separation:
f = 2405 + 10k MHz, k = 0, 1, … 7
Fixed channelization chosen by dedicated device at network initiation
10 MHz channel spacing sufficient for location determination using DSSS TDOA methods

## Slide 5: Spreading
1 Mc/s chip rate, 15.625 kS/s (64-chip pn sequences)
Offset-QPSK, with half-sine shaping
I-channel pn sequence CP = 103, with trailing zero
Q-channel pn sequence CP = 147, with trailing zero
I
Q
CP = 103
CP = 103
CP = 147
CP = 147
CP = 147
CP = 103

## Slide 6: Modulation
I-channel is used for symbol synchronization and service discovery (scanning node must correlate only one PN sequence)
Q-channel utilizes code position modulation to transmit information. The 147 sequence is cyclically shifted with transmitted data to one of 16 Gray-coded positions, each representing a 4-bit symbol.
Resulting bit rate is 62.5 kb/s
I
Q
c0
c1
…
c62
c63
…
c4
c5
c63
c0
…
c3
Symbol 0000
Symbol 0001

## Slide 7: CPM Performance

## Slide 8: Simple Packet
18 symbols
Transmission time = 1.024 ms
PHY preamble
SOP
PT
Source Addr
CRC
8 Symbols 3 S 2 S 4 S 1 S
(32 bits) (12 b) (8 b) (16 b) (4 b)

## Slide 9: Battery Life
The proposed PHY has a duty cycle of 0.1%. For a 10 mW transceiver with 10 uW standby power, this results in an average power drain of
0.001*10 mW + 0.999 *10uW = 19.99 uW.
If this node is supplied by a 750 mAh AAA battery, linearly regulated to 1 V, it has a battery life of
750 mAh/19.99 uA = 37,500 h,
or more than four years.

## Slide 10: Conclusion
Because of the cost and power drain requirements unique to P802.15.4, the PHY layer design must also be unique.
The combination of:
  wide channel separation
  low duty cycle DSSS
  code position modulation
produces a low cost, low power PHY solution optimized for 15.4 applications.

## Slide 11: Questions?