## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [PHY proposal for the Low Rate 802.15.4 Standard]
Date Submitted: [7 May, 2001]
Source: [Ed Callaway] Company: [Motorola]
Address: [8000 W. Sunrise Blvd., M/S 2141, Plantation, FL 33322]
Voice:[(954) 723-8341], FAX: [(954) 723-3712], E-Mail:[ed.callaway@motorola.com]
Re: [WPAN-802.15.4 Call for Proposals; Doc. IEEE 802.15-01/136r1]
Abstract: [This presentation represents Motorola’s proposal for the P802.15.4 PHY standard, emphasizing the need for a low cost system having excellent battery life.]
Purpose: [Response to WPAN-802.15.4 Call for Proposals]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: PHY Proposal for the Low Rate 802.15.4 Standard
Ed Callaway, Member of the Technical Staff
Motorola Labs
Phone: +1-954-723-8341
Fax: +1-954-723-3712
ed.callaway@motorola.com

## Slide 3: Proposed PHY
Combines
  wide channel separation (10 MHz)
  low duty cycle Direct Sequence Spread Spectrum (DSSS)
  Code Position Modulation
to produce a low cost, low power PHY solution optimized
for 15.4 applications.

## Slide 4: Highlights
Significantly lower hardware cost and current drain than 15.1.
  Hardware cost reduced by
    Use of DSSS
    10 MHz channel separation to ease channel filter requirements
  Current drain reduced by
    Short synchronization time
    Short message times

## Slide 5: Channelization
2.4 GHz band; 8 channels; 10 MHz channel separation
f = 2405 + 10k MHz, k = 0, 1, … 7
Fixed channelization chosen by dedicated device at network initiation
8 channels allow for 8 simultaneous operating WPANs
10 MHz channel spacing sufficient for location determination using DSSS TDOA methods

## Slide 6: Transceiver Specifications
BER ~ 10e-3
PER ~ 2%
(Assuming 6 bytes preamble + 10 bytes data)
Sensitivity ~ -90 dBm using differential decoding
(-103 dBm using conventional DSSS decoding)
Selectivity ~ -45 dBm adjacent channel (10 MHz offset)
Signal acquisition using DSSS with correlator
(4-5 symbols needed to sync using AGC)

## Slide 7: Spreading and Modulation
1 Mc/s chip rate, 15.625 kS/s (64-chip pn sequences)
I-channel pn sequence CP = 103, with trailing zero
Q-channel pn sequence CP = 147, with trailing zero
Offset-QPSK, with half-sine shaping
I-channel is used for symbol synchronization and service discovery (receiving node must correlate only one PN sequence)
Q-channel utilizes Code Position Modulation (CPM) to transmit information. The 147 pn sequence is cyclically shifted with transmitted data to one of 16 Gray-coded positions, each representing a 4-bit symbol.
Resulting bit rate is 62.5 kb/s

## Slide 8
BER Curve
n = # bits / Symbol

## Slide 9: System Considerations
Multipath
  10m range (indoors) implies worst case path length = 2x10m = 60nS. Proposed system can tolerate a delay spread of 100 ns, so there should be no problem in most applications
Interference and Jamming resistance Implementation dependent, can be designed to tolerate:
  +20 dBm 802.11b 10m away
  0 dBm 802.15.1 1m away
  Microwave ovens in quiet half-cycle
Intermodulation resistance – -20 dBm IIP3 required
Coexistence and throughput with co-located systems (multiple access)
  Low duty cycle systems, interference should be low

## Slide 10: Power / Range
Power:
Duty cycle = 0.1%
Transceiver active mode = 10 mW
Transceiver sleep mode = 20 uW
Average power drain is
0.001*10 mW + 0.999 *20uW = 30 uW
If this node is supplied by a 750 mAh AAA battery, linearly regulated to 1 V, it has a battery life of 2.8 years (25,000 h).
Range:
Range outdoors, LOS = 100m
Range indoors = 10m
Also based on –90 dBm Rx sensitivity

## Slide 11: Scalability
Power consumption greatly reduced in sleep mode
(20 uW vs. 10 mW)
Data rate increase possible, by sending 6b/S instead of 4b/S
Functionality of nodes varies with role, topology
(Designated Device, Designated MD, Distributed MD)
Cost per device varies according to functionality of a given node
Network size is scalable due to ad hoc nature of the network and large number of possible clusters

## Slide 12: Bottom Line
Cost estimate is $2 for quantity of 10M
(Includes everything from antenna port to bits)
Implementation size (active area)
  In 0.18 um, it is 6.3 mm2
  (Total active area = RF/analog + Baseband [60K gates] + MAC)
Technical feasibility & Manufacturability
  MD demonstration and network simulations available
  SPW and Matlab simulations of Code Position Modulation concept
  At present, developing single chip solution
  Samples available Q1 2002

## Slide 13: General Solution Criteria
Criteria | Ref | Value
Unit Manufacturing Cost ($) | 2.1 | $2 for 10M units
Interference and Susceptibility | 2.2.2 | 30-2350 and 2.530-13 GHz, -50 dBm; Adj. Channel (10 MHz), 2400-2483 MHz, -45 dBm
Intermodulation Resistance | 2.2.3 | -20 dBm IIP3
Jamming Resistance | 2.2.4 | Can tolerate – +20 dBm 802.11b 10m away 0 dBm 802.15.1 1m away Microwave ovens in quiet half-cycle
Multiple Access | 2.2.5 | 
Coexistence | 2.2.6 | Low duty cycle systems, interference should be low

## Slide 14: General Solution Criteria
Criteria | Ref | Value
Interoperability | 2.3 | True
Manufacturability | 2.4.1 | Single chip solution in development
Time to Market | 2.4.2 | Samples available Q1 2002
Regulatory Impact | 2.4.3 | True
Maturity of Solution | 2.4.4 | MD demo and network simulations available SPW and Matlab simulations of CPM
Scalability | 2.5 | 4 of 5 areas listed + network size
Location Awareness | 2.6 | True

## Slide 15: PHY Protocol Criteria
Criteria | Ref | Value
Size and Form Factor | 4.1 | Total active area in 0.18um = 6.3 mm2
Frequency Band | 4.2 | 2.4 GHz
# of Simultaneously Operating Full-Throughput PANs | 4.3 | 8
Signal Acquisition Method | 4.4 | DSSS with correlator
Range | 4.5 | Range outdoors, LOS = 100m Range indoors = 10m
Sensitivity | 4.6 | -90 dBm (differential decoding); -103 dBm (conventional DSSS decoding)
Delay Spread Tolerance | 4.7.2 | 100 ns
Power Consumption | 4.8 | Active mode = 10 mW Sleep mode = 20 uW