## Slide 1: Bluetooth Technology and Applications
Sponsored by IEEE Boston Chapter
At Analog Devices, Inc.
Wilmington, MA
April/May 2001
introduction:
Dr. James F. Mollenauer
Technical Strategy Associates
Newton, MA 02468 USA
617-244-0077
jmollenauer@TechnicalStrategy.com

## Slide 2: IEEE Boston Chapter
Course on Bluetooth technology and applications
Presented by a stellar cast...
Session 1: April 18 -- Overview of Bluetooth
  Jim Mollenauer - Technical Strategy Associates
  Ian Gifford- Chair, IEEE 802.15.1 WPAN Committee
Session 2: April 25 -- RF section
  Lane Bruns (& Mark Lane) - Silicon Wave
  Ashish Shah - Analog Devices
Session 3: May 2 -- Baseband processing
  Phillip Corrigan - Cambridge Silicon Radio
  Jerry O'Brien - Parthus Technologies
Session 4: May 9 -- Software considerations
  Lars Eriksson - Cetecom
Session 5: May 16 -- Applying Bluetooth in real systems
  Martin Bodley - GN Netcom
  Moshe Doron - Brightcom

## Slide 3: Session 1: Introduction
Introduction - Jim Mollenauer
  Course schedule and logistics
  What is Bluetooth?
  What problems is it intended to solve?
  Specifications vs. standards
History and technical overview - Ian Gifford
  Bluetooth at a glance
  History & current organization
  What does Bluetooth do - technically?
  The Bluetooth protocols
  Interoperability & profiles
  IEEE 802.15.1
  Summary
Compatibility issues - Jim Mollenauer
The BLUETOOTH trademarks are owned by Bluetooth SIG, Inc. U.S.A.

## Slide 4: What is Bluetooth?
A short-range wireless technology
Designed for several needs
  Interconnecting a computer and peripherals
    Clear the snake’s nest behind the desk!
  Interconnecting various handheld devices
    Laptop computer, cell phone, palmtop
    Preplanning of network is impractical
  Any short-range application where low cost is essential
    Goal: $5 parts cost
  Intended to be embedded in other devices
What it is not
  Another wireless LAN

## Slide 5: What does Bluetooth do for me?
Personal Ad-hoc Connectivity
Cable Replacement
Landline
Data/Voice Access Points
Slide courtesy of Tom Siep, TI, and Chatschik Bisdikian, IBM

## Slide 6: Usage scenarios: Headset
Wireless Freedom…
User benefits
Multiple device access
Cordless phone benefits
Hand’s free operation
Slide courtesy of Tom Siep, TI, and Chatschik Bisdikian, IBM

## Slide 7: Usage scenarios: Synchronization
Sharing Common Data…
User benefits
Proximity synchronization
Easily maintained database
Common information database
Slide courtesy of Tom Siep, TI, and Chatschik Bisdikian, IBM

## Slide 8: Usage scenarios: Data access points
PSTN, ISDN, LAN, WAN, xDSL
Remote Connections...
User benefits
No more connectors
Easy internet access
Common connection experience
Slide courtesy of Tom Siep, TI, and Chatschik Bisdikian, IBM

## Slide 9: Wireless Positioning
Cellular
Off-Campus Global Coverage
Wireless LAN
On-campus: Office, School, Airport, Hotel, Home
Bluetooth
Person Space: Office, Room, Briefcase, Pocket, Car
Short Range/Low Power
Voice AND Data
Low-cost
Small form factor
Many Co-located Nets
Universal Bridge
Slide courtesy of Tom Siep, TI, and Chatschik Bisdikian, IBM

## Slide 10: Deja Vu: Remember Infra-Red?
A short-range wireless technology
Low-cost, reasonable data rate
Pushed by Hewlett-Packard
Most laptops adopted it
Lots of cellphones and most palmtops have it
But no software for general connectivity
Even HP printers don’t have IR ports!
MORAL: a very nonlinear process
  Value is low until most devices have it (cf. adoption of fax)
  People won’t bother with it until probability of benefit is high

## Slide 11: Will Bluetooth Be Universal?
YES, if the size of the organization behind it means anything
Original work at Ericsson in 1994: Sven Mattison and Jaap Haartsen
Bluetooth SIG (Special Interest Group)
  Original founding members: Ericsson, IBM, Intel, Nokia, Toshiba
    “Promoter” group adds: 3Com, Lucent, Microsoft, Motorola
  Now over 2100 members
    Everyone you can think of
    Lots of companies you never heard of
  Very modest cost to join, unlike some other consortia
  Intellectual property pool
    Members agree to make their IP available to other members
    (if necessary to implement spec)

## Slide 12: Where Did the Name Come From?
A medieval Danish king, Harald Blaatand II or Bluetooth (940-981)
Noted for unifying Denmark and Sweden
Don’t ask: would the methods that the Vikings used to achieve consensus be admissible in the standards process today?

## Slide 13: From Specification to Standard
Initial work in the Bluetooth SIG
Specification version 1.1 approved (replacing 1.0B)
Foundation work joined by IEEE Project 802
  Generate official standard
  Deliberation and due process
  Bluetooth SIG continues on
802.15 group already chartered for PANs (personal area networks)
  SIG responded to call for proposals
Agreement not to change the first version(s) of Bluetooth
  Even if overall Project 802 requirements were not met
  Avoided incompatible developments in Project 802 and SIG
  Some contention with 802.11 (wireless LAN) group) which considered PANs to be within its charter
Future technology: an issue
  Both groups looking at faster rates: Radio 2 and 802.15 TG3
  IP questions: IEEE doesn’t do patent pools

## Slide 14: Specifications and Standards
Specifications
Can be written by any company or organization
Used frequently as a purchasing document, to solicit bids
As “standards”:
Written by industry consortia
Subject only to their own review and rules of procedure
Can be generated quickly, can be flawed
Standards
Written by groups chartered to do standards
In U.S., under ANSI (American National Standards Institute)
May cover only a part of full technology (IEEE 802 does layers 1 & 2)
Well-specified due process (which may be slow)
May be dictated by international treaties
What’s the difference?

## Slide 15: Win Some, Lose Some
Official standards don’t always make specifications obsolete--
    Ethernet
    Blue Book v. 2 by DEC, Intel, and Xerox preceded IEEE 802.3
    802.3 Physical layer changes accepted immediately
    802.3 MAC layer changes not always used, even 20 years later
    Compatibility issues have been handled well
    ATM
    ATM Forum became the driving force in ATM
    Standards groups ratified most of what the Forum did, after the fact
    Efficient process made it possible to generate specifications faster than customers could absorb them
    Abandoned by users in favor of high-speed Ethernet
    Except carriers, where ATM started
    Cable Modems
    Official group (IEEE 802.14) solicited cable operators to participate
    Operators finally did, but felt the IEEE process was too slow
    Did their own spec (DOCSIS), which they (not suppliers) controlled
    802.14 effort was ultimately abandoned

## Slide 16: Which Way Will Bluetooth Go?
Not like cable modems
  Buyers not concentrated in small group
    Millions of individuals will buy Bluetooth equipment
Not like ATM
  No established “legacy” technology like Ethernet
    Infra-red exists but is not well established
  Low cost will keep complexity bounded
Probably like Ethernet (my opinion)
  Coexistence of versions built to standard and original spec
  Compatibility mechanisms needed
    Issue now: version 1.0b vs. version 1.1, later 1.2
  Advanced versions (higher speed, longer range) from 802.15

## Slide 17: Bluetooth at a glance
Harald Blaatand “Bluetooth” II
  King of Denmark 940-981 AC
Specification for small-form factor, low-cost, low-power, short-range radio link between notebook PCs, cellular phones, PDAs and other portable devices.
  Radio frequency (RF) technology for Personal Connectivity
  Operates in the unlicensed 2.4GHz ISM band
  Hardware/Software description & application framework.
Source: Dr. Chatschik Bisdikian <bisdik@us.ibm.com>

## Slide 18: A little bit of history
The Bluetooth SIG (Special Interest Group) was formed in February 1998 by 5 promoter companies
  Ericsson,IBM, Intel, Nokia, Toshiba
The Bluetooth SIG went “public” in May 1998
The Bluetooth SIG work (the spec: 1,600+ pages) became public on July 26, 1999 (ver. 1.0A)
  ver. 1.0B was released on December 6, 1999
  ver. 1.1 was released on March 1, 2001
The promoter group increased in December 1999 to nine
  added: 3Com, Lucent, Microsoft, Motorola
There are 2,164 adopters (as of 3/15/2001)
  adopters enjoy royalty free use of the Bluetooth technology
Source: Dr. Chatschik Bisdikian <bisdik@us.ibm.com>

## Slide 19: Bluetooth a.k.a. MC Link multi-communicator link
“In 1994, Ericsson Mobile Communications AB in Lund, Sweden, initiated a study to investigate the feasibility of a low-power, low-cost radio interface between mobile phones and their accessories. The intention was to eliminate cables between phones and PC cards, wireless headsets, and so forth. The study was part of a larger project that investigated multi-communicators connected to the cellular network via cellular telephones. The last link in the connection between a communicator and the cellular network was a short-range radio link to the phone - thus, the link was called the multi-communicator link or MC link. As the MC link project progressed, it became clear that there was no limit to the kinds of application that could use a short-range radio link. Cheap, short-range radios would make wireless communication between portable devices economically feasible.” Jaap Haartsen, Ericcson Review No. 3, 1998

## Slide 20: Bluetooth SIG Structure
BQRB = Bluetooth Qualification Review Board
BTAB = Bluetooth Technical Advisor Board
BQA = Bluetooth Qualification Administrator
BQB = Bluetooth Qualification Body

## Slide 21: Bluetooth SIG - Key Groups
Policy Groups
Architecture Review Board (arch)
Measurement Initiative (mi)
Regulatory (gov)
Qualification Program (qp)
Qualification Review Board (bqrb)
Test Initiative (ti)
Working Groups
Radio 2.0 (radio)
Car Profile (car)
PAN Profile (pan)
Human Interface Device (hid)
Co-existence/Interoperability with 2.4 GHz ISM Devices (coexist)
Richer Audio/Voice/Video (av)
Printing Profile (printing)
Still Image Profile (imaging)
Extended Service Discovery Profile (esdp)
Local Positioning Profile (lp)
UDI for Japanese 3G Handsets (udi)
Expert Groups
Automotive Expert Group (car) (charter)
Security Expert Group (sec)
Study Groups
ATM Study Group (atm)
Host Controller Interface Study Group (hci)
Industrial Automation Study Group (ia)
ISDN Study Group (isdn)
Quality of Service Study Group (qos)

## Slide 22: What Does Bluetooth Do?
Cable Replacement

## Slide 23: Characteristics
Operates in the 2.4 GHz band at a data rate of 720Kb/s.
Uses Frequency Hopping (FH) spread spectrum, which divides the frequency band into a number of channels (2.402 - 2.480 GHz yielding 79 channels).
Radio transceivers hop from one channel to another in a pseudo-random fashion, determined by the master.
Supports up to 8 devices in a piconet (1 master and 7 slaves).
Piconets can combine to form scatternets.
Source: Dr. Chatschik Bisdikian <bisdik@us.ibm.com>

## Slide 24: What is a Piconet?
A collection of devices connected in an ad hoc fashion.
One unit will act as a master and the others as slaves for the duration of the piconet connection.
Master sets the clock and hopping pattern.
Each piconet has a unique hopping pattern/ID
Each master can connect to 7 simultaneous or 200+ inactive (parked) slaves per piconet
M
S
S
S
SB
P
P
M=Master
S=Slave
P=Parked
SB=Standby
Source: Dr. Chatschik Bisdikian <bisdik@us.ibm.com>

## Slide 25: What is a Scatternet?
A Scatternet is the linking of multiple co-located piconets through the sharing of common master or slave devices.
A device can be both a master and a slave.
Radios are symmetric (same radio can be master or slave)
High capacity system, each piconet has maximum capacity (720 Kbps)
M
M
S
S
S
S
P
SB
SB
P
P
M=Master
S=Slave
P=Parked
SB=Standby
Source: Dr. Chatschik Bisdikian <bisdik@us.ibm.com>

## Slide 26: The Bluetooth protocols
A hardware/software description
An application framework
Application Framework and Support
Link Manager and L2CAP
Radio & Baseband
Host Controller Interface
RF
Baseband
Audio
Link Manager
L2CAP
Other
TCS
RFCOMM
Data
SDP
Applications
Control
Source: Dr. Chatschik Bisdikian <bisdik@us.ibm.com>

## Slide 27: The transport protocols
middleware & data applications
audio apps
a: audio
d: data
c: control
radio
baseband
link
manager
L2CAP
control
audio
HCI
transport
protocol
group
middleware
protocol
group
application
group
(a)
(d)
(c)
Source: Dr. Chatschik Bisdikian <bisdik@us.ibm.com>

## Slide 28: The “lower” layer transports
Radio (RF)
  The Bluetooth radio front-end
    2.4GHz ISM band; 1Mbps
    1,600hops/sec; 0dBm (1mW) radio (up to 20dBm)
Baseband (BB)
  Piconet/Channel definition
  “Low-level” packet definition
  channel sharing
Link Management (LM)
  Definition of link properties
    encryption/authentication
    polling intervals set-up
    SCO link set-up
    low power mode set-up
Source: Dr. Chatschik Bisdikian <bisdik@us.ibm.com>

## Slide 29: The Bluetooth network topology
M
M
S
S
S
S
P
sb
sb
P
P
Radio designation
  Connected radios can be master or slave
  Radios are symmetric (same radio can be master or slave)
Piconet
  Master can connect to 7 simultaneous or 200+ inactive (parked) slaves per piconet
  Each piconet has maximum capacity (1 MSps)
  Unique hopping pattern/ID
Scatternet
  Piconets can coexist in time and space
Source: Dr. Chatschik Bisdikian <bisdik@us.ibm.com>

## Slide 30: The piconet
or
A
D
C
B
E
All devices in a piconet hop together
  To form a piconet: master gives slaves its clock and device ID
    Hopping pattern determined by device ID (48-bit)
    Phase in hopping pattern determined by Clock
Non-piconet devices are in standby
Piconet Addressing
  Active Member Address (AMA, 3-bits)
  Parked Member Address (PMA, 8-bits)
Source: Dr. Chatschik Bisdikian <bisdik@us.ibm.com>

## Slide 31: The baseband states
Standby
  do nothing
Inquire
  search for other devices in the vicinity
Page
  connect to a specific device
Connected
  participate in a piconet (master or slave)
standby
connected
page
inquiry
Source: Dr. Chatschik Bisdikian <bisdik@us.ibm.com>

## Slide 32: Baseband packet
header
payload
access code
LSB
MSB
(68|72) bits
54 bits
0-2745 bits
Source: Dr. Chatschik Bisdikian <bisdik@us.ibm.com>

## Slide 33: Paging sequence
625 µsec
312.5 µsec
68 µsec
ft[k]P
ft[k+1]P
ft[k+2]P
fr[k]P
fr[k+1]P
fr[k+2]P
master listens
master pages
master listens
master responds
IDi
IDi
IDi
FHSi
IDi
slave responds
slave responds
625 µsec
A: slave acquires half-slot synchronization
B: slave acquires full-slot synchronization
C: slave capable to join master’s piconet
D: piconet communications start with master Tx slot
(C)
(D)
(A)
(B)
ft[m]C
1.25 msec
625 µsec
Source: Dr. Chatschik Bisdikian <bisdik@us.ibm.com>

## Slide 34: Baseband link types
Polling-based (TDD) packet transmissions
  1 slot: 0.625msec (max 1600 slots/sec)
  master/slave slots (even-/odd-numbered slots)
  polling: master always “polls” slaves
Synchronous connection-oriented (SCO) link
  “circuit-switched”
    periodic single-slot packet assignment
  symmetric 64Kbps full-duplex
Asynchronous connection-less (ACL) link
  packet switching
  asymmetric bandwidth
    variable packet size (1-5 slots)
      max. 721 kbps (57.6 kbps return channel)
      108.8 - 432.6 kbps (symmetric)
ACL link
0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 19 20 21 22
SCO link
transmission from master
transmission from slave
Source: Dr. Chatschik Bisdikian <bisdik@us.ibm.com>

## Slide 35: Bluetooth security features
Authentication of remote device
  based on link key (128 bit)
  challenge/response
  may be performed in both directions
Encryption of payload data
  stream cipher algorithm ( 128 Bit)
    Safer+ (Massey and Rueppel)
  affects all traffic on a link
Initialization
  shared key
  PIN entry by user
Source: Dr. Chatschik Bisdikian <bisdik@us.ibm.com>

## Slide 36: Key generation and usage
PIN
E2
Link Key
Encryption Key
E3
Encryption
Authentication
PIN
E2
Link Key
Encryption Key
E3
User Input
(Initialization)
(possibly)
Permanent
Storage
Temporary
Storage
Source: Dr. Chatschik Bisdikian <bisdik@us.ibm.com>

## Slide 37
Dev_A
Dev_B
initial
authentication
temporary
link key
temporary
link key
temporary link key
generation algorithm
temporary link key
generation algorithm
user enters common PIN
(initialization)
trust device?
trust device?
trust is a mutual relation
in future authentications
use permanent link key
encrypt link?
encrypt link?
no
no
generate and store
permanent link key
generate and store
permanent link key
yes
yes
encryption
generate temporary
encryption link
generate temporary
encryption link
yes
yes
encryption is a
mutual operation
Source: Dr. Chatschik Bisdikian <bisdik@us.ibm.com>

## Slide 38: The “upper” layer transports
Host Controller Interface (HCI)
  provides a common interface between the Bluetooth host and a Bluetooth module
    Interfaces in spec 1.0: USB; UART; RS-232
Link Layer Control & Adaptation (L2CAP)
  A simple data link protocol on top of the baseband
    connection-oriented & connectionless
    protocol multiplexing
    segmentation & reassembly
    QoS flow specification per connection (channel)
    group abstraction
Source: Dr. Chatschik Bisdikian <bisdik@us.ibm.com>

## Slide 39: The middleware protocols
a: adopted protocol
b: Bluetooth specific protocol
transport
protocol
group
middleware
protocol
group
application
group
transport protocols
networking
apps
audio apps
IrDA
apps
OBEX
control
audio
RFCOMM
PPP
IP
TCP
UDP
SDP
telephony
control
based on
AT
commands
IrMC
TCS-BIN
(b)
(b)
(a)
(a)
(b)
telephony apps
Source: Dr. Chatschik Bisdikian <bisdik@us.ibm.com>

## Slide 40: Middleware protocols (1)
Service Discovery Protocol (SDP)
  Defines an inquiry/response protocol for discovering services
    Searching for and browsing services
  Defines a service record format
    Information about services provided by attributes
    Attributes composed of an ID (name) and a value
    IDs may be universally unique identifiers (UUIDs)
Source: Dr. Chatschik Bisdikian <bisdik@us.ibm.com>

## Slide 41: Middleware protocols (2)
RFCOMM (based on GSM TS07.10)
  emulates a serial-port to support a large base of legacy (serial-port-based) applications
  allows multiple “ports” over a single physical channel between two devices
Telephony Control Protocol Spec (TCS)
  call control (setup & release)
  group management for gateway serving multiple devices
Legacy protocol reuse
  reuse existing protocols, e.g., IrDA’s OBEX, or WAP for interacting with applications on phones
Source: Dr. Chatschik Bisdikian <bisdik@us.ibm.com>

## Slide 42: Interoperability & Profiles
Profiles
Protocols
Applications
Represents default solution for a usage model
Vertical slice through the protocol stack
Basis for interoperability and logo requirements
Each Bluetooth device supports one or more profiles
Source: Dr. Chatschik Bisdikian <bisdik@us.ibm.com>

## Slide 43: Profiles (spec v.1)
Generic Access Profile
  Service Discovery Application Profile
  Serial Port Profile
    Dial-up Networking Profile
    Fax Profile
    Headset Profile
    LAN Access Profile (using PPP)
    Generic Object Exchange Profile
      File Transfer Profile
      Object Push Profile
      Synchronization Profile
  TCS_BIN-based profiles
    Cordless Telephony Profile
    Intercom Profile
Source: Dr. Chatschik Bisdikian <bisdik@us.ibm.com>

## Slide 44: LAN access point profile
RFCOMM
ACL SCO
Bluetooth Baseband
LMP
L2CAP
PPP
Source: Dr. Chatschik Bisdikian <bisdik@us.ibm.com>

## Slide 45: Profiles (spec v.2)
Radio 2 (next generation radio)
  backward compatible
Car Profile
PAN Profile
Human Interface Device
Co-existence/Interoperability with 2.4 GHz ISM Devices
Richer Audio/Voice/Video
Printing Profile
Still Image Profile
Extended Service Discovery Profile
Local Positioning Profile
UDI for Japanese 3G Handsets
Source: Dr. Chatschik Bisdikian <bisdik@us.ibm.com>

## Slide 46: The 802.15.1 standard
Source: Dr. Chatschik Bisdikian <bisdik@us.ibm.com>

## Slide 47: Summary
Bluetooth is a global, RF-based (ISM band: 2.4 GHz), short-range, connectivity solution for portable, personal devices
  it is not just a radio, it is an end-to-end solution
The Bluetooth spec comprises
  a HW & SW protocol specification
  usage case scenario profiles and interoperability requirements
IEEE 802.15.1 is working on standardizing the PHY and MAC layers in Bluetooth
To learn more: http://www.bluetooth.org
Source: Dr. Chatschik Bisdikian <bisdik@us.ibm.com>

## Slide 48: More on Bluetooth?
More Info:
http://www.bluetooth.com/developer/specification/specification.asp
More Info:
http://internet.motlabs.com/books.htm

## Slide 49: More on Bluetooth? (cont)
Join the Bluetooth SIG and participate
  http://www.bluetooth.org
Join the IEEE WG for WPANs and participate
  http://ieee802.org/15
Join the IETF IP over Bluetooth (IPoBT) BoF
  http://internet.motlabs.com
Also visit the Bluetooth(TM) Weblog
  http://bluetooth.weblogs.com/

## Slide 50: More on IEEE 802.15.1?
Jul99
  Initial Discussion on Proposals.
Nov99
  Initial draft ready for WG ballot.
Jan00
  First Ballot complete, second ballot kicked off.
Mar01
  Draft ready for IEEE sponsor ballot.
Jul01
Sep01
  Approval by IEEE Standards Board
Nov01
Dec01
  Approval by IEEE Standards Board
802 Sponsor Expectation
802.15.1 Project Target

## Slide 51: IEEE 802.15.1 SDL Overview
What is SDL?
  Specification and Description Language
  Standardized by ITU-T in the Z-series Mainly ITU-T Recommendation Z.100
Why use SDL?
  Provides Clear and Unambiguous Description of … (e.g. Protocols, or Systems)
  Simulation, Validation, and Verification tools available for SDLs
  Conversion tools available to take SDL in and generate “useable code” or “TTCN tests”
When to create SDLs?
  In the beginning
  Not after the protocol is described by other means (e.g. English text)
  After English text to aid in protocol review, validation, and testing.
The IEEE Draft P802.15.1/D0.9.1 SDL is 579 pages
out of 1159 pages. Currently it is normative.

## Slide 52
Ian Gifford - IEEE 802.15.1 Chair
  giffordi@ieee.org
  Tel: +1 978 815 8182
Dr. Chatschik Bisdikian, IEEE 802.15.1 Vice Chair
  bisdik@us.ibm.com
  Tel: +1 914 784 7439
Thomas Siep, IEEE 802.15.1 Editor-in-Chief
  siep@ti.com
  Tel: +1 214 480 6786
Francis Truntzer, Bluetooth SIG Chair
  francis.l.truntzer@intel.com
  Tel: +1 408 765 5989
James Kardach, Bluetooth SIG Chair
  Jim.Kardach@intel.com
  Tel: +1 408 765 4469
Jim Carlo, IEEE802 LAN/MAN Standards Committee, Chair
  jcarlo@ti.com
  Tel: +1 214 693 1776 (Cellular)
  Susan Tatiner, IEEE-SA Director Standards Publishing Programs
  s.tatiner@ieee.org
  Tel: +1 732 562 3830
Contact Information

## Slide 53: Compatibility and Interference Issues
Compatibility: devices you want to communicate with
Interference: devices you don’t
Bluetooth is in an unlicensed band -- this is good and bad
  Good in that there’s no red tape, devices can go most anywhere
  Bad in that other simultaneous usage is unpredictable
ISM band: Industrial, Scientific, and Medical
  All sorts of uses, many predating data communication
    Examples: microwave ovens, RF plasma lighting
  FCC mandates spread spectrum to spread the pain of interference
    All users get some interference rather than some a lot and some none at all

## Slide 54: Frequency Hopping
One way to spread the spectrum
Used by Bluetooth, HomeRF, and the original (1 or 2 Mbps) version of 802.11
Frequency changes after many bits are sent
  Relatively easy to implement
Alternative: Direct Sequence
  Frequency changes faster than bit rate
  Efficient but complex; used by newer versions of 802.11
Unless spectrum is very crowded, probability of two users at same time at same frequency is low
Other wireless technologies use different hopping rate
  Bluetooth: 1600 hops per second
  HomeRF: 8 hops per second

## Slide 55: Microwave Ovens
Use RF induction heating, in the same frequency band as Bluetooth
Do their own version of spread spectrum, varying the frequency as the AC line voltage rises from zero to peak
Data from NTIA, courtesy of Intersil

## Slide 56: Microwave Lighting
The next big thing in lighting, but RF emissions could be a problem
  Argon plasma transfers energy to sulfur, which radiates light
ISM band is legitimate for such applications
Strong incentives for adopting microwave lighting
    Most efficient broad-spectrum light known
    (6x more than incandescent)
    Sunlight appearance
    High output
    Very compact
Emission limits established in Europe
FCC working on the issue
OLD
Fusion Lighting, Inc.
NEW

## Slide 57: The Radio Jam
Lots of different types of networks, all using the ISM band
How badly will they interfere with each other?
IEEE 802.11 wireless LAN
Bluetooth/802.15
HomeRF
  A consortium developing in-home wireless networks
  RF technology is simplified 802.11
  Based on assumption that full 802.11 is too costly
  Back in the game after 9/00 FCC decision for wideband FH
ETSI Hiperlan wireless LAN
IEEE 802.16.4 “Wireless HUMAN” -- just started up
  High-speed unlicensed metropolitan area network
  Wireless access network aimed at home Internet users
  Sentiment is in favor of using 802.11 physical layer
  Signals will be strong near antenna towers

## Slide 58: Interference Concerns
Two levels of interference
  Physical layer: interfering signal acts like noise
    Spread spectrum technology minimizes this
    Interference for a brief interval, then one or both systems move on
    Error-correcting code may correct garbled section
  MAC layer
    Interfering signal may look like a rogue member of the network
    For example, Bluetooth might confuse 802.11
BCN
Poll
A
B
D
E
F
G
coordinator
802.11 users
interference
Gap expected
TIME

## Slide 59: Working on Coexistence
Work in IEEE 802 to develop coexistence strategies: 802.15 TG 2
Methods include channel selection and adaptive hopping sequence
Source: Nada Golmie, NIST, presentation to IEEE 802.15

## Slide 60: Interoperability Problems
Two versions of Bluetooth now in the field
  1.0b and 1.1
  1.1 just approved, but many implementers started with that
  Lack of full interoperability was embarrassing at Consumer Electronics Show
  But not a real problem: numbers of units produced so far is miniscule compared to ultimate production