## Slide 1
NOTE: Update all red fields replacing with your information; they are required. This is a manual update in appropriate
fields. All Blue fields are informational and are to be deleted. Black stays. After updating delete this box/paragraph.
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: TG4 RFWaves PHY Proposal
Date Submitted: 14 May, 2001
Source: Barry Volinskey, RFWaves, LTD.
Address Yoni Netanyahu 5 Or-Yehuda 60376, Israel
Voice: +972-3-6344131 , FAX: +972-3-6344130, E-Mail:Volinskey@RFWaves.com
Re:0
[If this is a response to a Call for Contributions, cite the name and date of the Call for Contributions to which this document responds, as well as the relevant item number in the Call for Contributions.]
[Note: Contributions that are not responsive to this section of the template, and contributions which do
not address the topic under which they are submitted, may be refused or consigned to the “General Contributions” area.]
Abstract: RFWaves proposal of a PHY layer for TG4.
Purpose: Presentation at the Orlando meeting, May-2001.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: RFWaves – PHY Concepts

## Slide 3: The SAW Correlator
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4: The RFWaves Radio - Transmitter
Notes: <number>
<footer>
<header>
<date/time>

## Slide 5: The RFWaves Radio - Receiver
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6: The RFWaves Radio – Full Module
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: Main Characteristics
Uses 2.4GHz ISM band – FCC compliant
Direct Sequence Spread Spectrum
Half Duplex, Digital Transceiver (symmetric system)
Range of 10m with possible increase to 30m (indoor at BER of 10e-4) depending on antenna size and design
Low power consumption
Low cost
1Mbps raw bit-rate – enables robustness at low bit rates
Fixed channels – each device works on a single pre-set channel
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8: Radio PCB
Notes: <number>
<footer>
<header>
<date/time>

## Slide 9: Reply to Criteria Document

## Slide 10: Unit Manufacturing Cost (UMC)
Cost is based on available quotation for RFWaves by 3rd party foundries
Assumed costs will be significantly lower for in-house production or increased quantities
Result to 2.1.2

## Slide 11: Unit Manufacturing Cost (UMC)
 | 2002 – 10M units ($) | 2003 – 20M units ($) | Flip Chip packaging($)
RFIC 1.3mm^2 | .63 | .5 | .35
SAW correlator | .55 | .4 | .4
SAW resonator | .43 | .25 | .2
Passives | .1 | .1 | .1
PCB (10X10mm) | .05 | .05 | .05
Assembly & testing | .15 | .1 | .1
Yield | .9 | .96 | .96
Total | 2.1 | 1.35 | 1.25
Result to 2.1.2

## Slide 12: Unit Manufacturing Cost (UMC)
A 50cents, 8-bit micro controller / logic is enough to support a simple MAC layer
Flip Chip packaging technology is under development now for SAW devices.
We can give up the SAW resonator and exchange it with a reference frequency from the MAC and on-chip PLL.
Result to 2.1.2

## Slide 13: Signal Robustness – Interference and Susceptibility
P interferer=P signal - 6dB
Result to 2.2.2.2

## Slide 14: Signal Robustness – Interference and Susceptibility
IIP1 = -18dBm
Input filter Q=5
30 MHz – 1GHz: acceptable interferer power level < -10dBm
1GHz-2GHz : acceptable interferer power level < -20dBm
3GHz-13GHz : acceptable interferer power level < -20dBm
Result to 2.2.2.2

## Slide 15: Signal Robustness - Intermodulation Resistance
LO = 1952MHz
IF = 488MHz
IIP1 = -18dBm
Result to 2.2.2.2

## Slide 16: Signal Robustness - Intermodulation Resistance
Result to 2.2.3.2: (+)
Notes: Refers to Jamming as well

## Slide 17: Signal Robustness – Coexistence
Values 1&2 – 802.15.1
Result to 2.2.6.2

## Slide 18: Signal Robustness – Coexistence
Values 1&2 – 802.15.1
Path Loss1=60dB Path Loss2=56dB Path Loss3=50dB | Pt(A1,A2)<0dBm @ 1MHz band Pt(B1,B2)=20dBm @ 1MHz band
B1: Carrier=20dBm-60dB=-40dBm Interference<0dBm-50dB=-50dBm C/I>10dB | B2: Carrier=20dBm-60dB=-40dBm Interference<0dBm-56dB=-56dBm C/I>16dB
Conclusion: interference to 802.15.1 is negligible!
Result to 2.2.6.2

## Slide 19: Technical Feasibility - Manufacturability
Manufacturability of SAW Devices:
A well known & tested technology in the past 40 years
Based on piezo-electric qualities of crystals
Penetrated consumer applications in the past decade, as cellular markets evolved rapidly
A one-mask process – only one aluminum layer
SAW correlators have been used in military & radar applications for over 30 years
Result to 2.4.1.2

## Slide 20: Technical Feasibility - Manufacturability
Spreading function & pulse shaping – simulated
Result to 2.4.1.2

## Slide 21: Technical Feasibility - Manufacturability
Spreading function & pulse shaping – measured
Result to 2.4.1.2

## Slide 22: Technical Feasibility - Manufacturability
Autocorrelation function – simulated
Result to 2.4.1.2

## Slide 23: Technical Feasibility - Manufacturability
Autocorrelation function – measured
Result to 2.4.1.2

## Slide 24: Technical Feasibility - Time to Market
RFWaves Schedule
  SAW components have been manufactured and tested
  Functioning RFIC in Q3 2001
  Engineering samples available Q4 2001
  Mass production by RFWaves end of Q1 2002
Result to 2.4.2.2

## Slide 25: Technical Feasibility – Regulatory Impact
Complies with FCC part 15.247
Complies with ETSI ETS 300 328
Result to 2.4.3.2

## Slide 26: Technical Feasibility – Maturity of Solution
The SAW Correlator is functioning, and is very close to the simulated results
The SAW Resonator is functioning, and is very close to the simulated results
A functioning RFIC will be available by Q3 2001
A discrete prototype (based on the real SAW correlator) was built & tested for performance.
Result to 2.4.4.2

## Slide 27: Scalability
Power consumption
  Latency/Bit-rate can be linearly exchanged for power consumption
Coding can be used in the MAC layer to increase range, in exchange for bit-rate/power
Frequency bands
  The system can work in 5GHz and 915MHz ISM bands
Cost
  By supplying reference frequency from the MAC layer, the SAW resonator can be saved, and replaced by an on-chip PLL
Result to 2.5

## Slide 28: Location Awareness
No location awareness capability
The system supports RSSI (as part of the OOK receiver) – which allows distance estimation
Result to 2.6

## Slide 29: Size and Form Factor
 | Length | Width | Height
SAW resonator | 3.8 | 3.8 | 1
SAW correlator | 7 | 5 | 1.3
RFIC | 5 | 5 | 0.5
Passives (10X0402) | 2 | 4 | 0.5
Total size: 10X10mm
Result to 4.1.2

## Slide 30: Size and Form Factor - flip chip option
 | Length | Width | Height
SAW resonator | 1.5 | 2 | 0.8
SAW correlator | 5 | 1 | 0.8
RFIC - BiPOLAR | 5 | 5 | 0.5
Passives (10X0402) | 2 | 4 | 0.5
Total size: 7X7mm
Result to 4.1.2

## Slide 31: Frequency Band
Band width : 20MHz @ -20dBc
Result to 4.2.2

## Slide 32: Number of Simultaneously Operating Full Throughput PAN’s
FDMA:
3 frequency channels are offered: 2.4-2.44, 2.42-2.46, 2.44-2.48
Result to 4.3.2

## Slide 33: Number of Simultaneously Operating Full Throughput PAN’s
Blue – 13bit BPSK Green – Linear FM Red – 13 bit BFSK
Result to 4.3.2
CDMA:

## Slide 34: Number of Simultaneously Operating Full Throughput PAN’s
CDMA: 3 codes
FDMA: 3 frequencies
Total: 9 independent channels are possible
Result to 4.3.2

## Slide 35
9 independent 1Mbps throughput PANs are available
Each frequency/code combination can support:
  9 PANs of 100Kbps using TDMA
  3 PANs of 100Kbps using CSMA
  Many PANs of very low bit-rate/high latency
Number of Simultaneously Operating PAN’s
Result to 4.3.2

## Slide 36: Signal Robustness - Coexistence
High bit-rate bursts enable better robustness in the time-domain:
  128 bits are transmitted in 128 Sec
  Capable to receive an ACK and retransmit twice within a single Bluetooth hop (650 Sec)
Result to 2.2.6.2

## Slide 37: Signal Robustness – Multiple Channel Access
Cross correlation of two channels – 20MHz apart:
Green – auto correlation
Blue – cross correlation, 10dB higher interferer
Result to 2.2.5.2

## Slide 38: Signal Acquisition Method
A SAW correlator is a matched filter – hence locks on the 1st bit it detects. A preamble of 4-5 bits is enough to set up the link (one bit) and allow the MAC to synchronize (3-4 bits)
Greatly effects power consumption
Result to 4.4.2

## Slide 39: Signal Acquisition Method – 4 consecutive pulses
Result to 4.4.2

## Slide 40: 4 Consecutive Auto-Correlations
Result to 4.4.2

## Slide 41: Range
Output power = 10dBm
Sensitivity = -90dBm
Antenna gain = -5 dBi (Rx & Tx)
Path Loss = 10-(-90)+(-5)+(-5)=90dB
Range:
D=10^[(L-40)/33]=30meter
Result to 4.5.2

## Slide 42: Sensitivity
Modulation: On Off Keying
BER < 10^-4
(1+2): Eb/N0=11dB
Receiver data:
  Noise Figure = 10dB
  Thermal Noise: Pn=-114+10*log(20)=-101
  (4.1+4.2): N0=-101+10=-101dBm
(3+4): Sense=Ebmin=-101+11=-90dBm
Result to 4.6.2

## Slide 43: Power consumption
True measurement of power efficiency should be in Joule/bit – 60nJoule/bit
In low bit-rate - with small packets, the following become critical to total power consumption:
  Standby (sleep) power consumption - 1A
  Wake up time (and related power consumption) - 10Sec
  Acquisition time - 1Sec (1Bit)
Result to 4.8.2

## Slide 44: Power Consumption
Assumptions:
  Packet size = 20 byte = 180bits = 180Sec
  200 Packets / second (100Tx, 100Rx)
Peak current consumption (Vcc=3V)
  Tx=20mA
  Rx=20mA
  STDBY=1A
Result to 4.8.2

## Slide 45: Power Consumption
 | Peak | Average
Tx | 60mW | 4W
Rx | 60mW | 4W
Standby | 1W | 1W
Result to 4.8.2

## Slide 46: Thank You