## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Header error rate analysis for 802.15.3]
Date Submitted: [8 May 2001]
Source: [Stanley K. Ling and Keith Holt] Company [Intel Corporation]
Address [9750 Goethe Road, M/S LOC 3/8, Sacramento, CA 95827]
Voice:[(916) 855-5000], FAX: [(916) 854-2809], E-Mail:[stan.k.ling@intel.com, keith.holt@intel.com]
Re: []
Abstract: [This contribution presents analytical and simulation results for two proposed header modulations.]
Purpose: [For information only.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Frame Format
The frame header will be 18 bytes, consisting of:
  PLCP header + MAC header + HCS
The PLCP header will be ~4 bytes1
The MAC header will be 12 bytes2
The HCS for the PLCP + MAC header will be 2 bytes2
1 byte SIGNAL, 1 byte SERVICE, 2 bytes LENGTH from IEEE Std 802.11b-1999
IEEE 802.15-01/034r2

## Slide 3: Header Coding
Proposal 1: Send the header twice using (O)QPSK, retain the correct one
Proposal 2: Send the header once using BPSK

## Slide 4: Error Rate Analysis
Define: P(H) = prob. of correct header detection
= prob. of incorrect header detection
P(H1),P(H2) = prob. of correct detection of header #1 and #2
= prob. of incorrect detection of header #1 and #2
P(SymbolQPSK) = prob. of correct (O)QPSK symbol detection
= prob. of incorrect (O)QPSK symbol detection
P(SymbolBPSK) = prob. of correct BPSK symbol detection
= prob. of incorrect BPSK symbol detection

## Slide 5: Error Rate Analysis (Proposal 1)
The header is incorrectly detected when both Header #1
and Header #2 are incorrect:
Assuming 144 bits of data in the header:
Assuming AWGN, the probability of symbol error is [1]:

## Slide 6: Error Rate Analysis (Proposal 2)
Assuming 144 bits of data in the header:
Assuming AWGN, the probability of symbol error is [1]:

## Slide 7: Simulation Results
BPSK provides ~1dB modulation gain over (O)QPSKx2 at 10-4 header error rate

## Slide 8: Conclusions
Transmitting the header using BPSK is more robust than sending the header twice using (O)QPSK.
BPSK should be chosen as the header modulation for IEEE 802.15.3.

## Slide 9: References
Proakis, J. G., Digital Communications, New York, New York: McGraw-Hill, 1995.