## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [TG3 Publicity Presentation]
Date Submitted: [7May2001]
Source: [James D. Allen] Company: [Eastman Kodak Co.]
Address: [1669 Eastman Ave. Rochester, NY, 14650-2015]
Voice:[(716) 588-1906], FAX: [(716) 722-9053], E-Mail:[james.d.allen@kodak.com]
[Jeyhan Karaoguz] Company: [Broadcom Corporation]
Address: [16215 Alton Parkway, Irvine, CA 92619]
Voice: [949 585 6168 ] E-Mail: [jeyhan@broadcom.com]
[John Barr] Company: [Motorola}
Address: [1750 E. Golf Road, 6th Floor, Schaumburg, IL 60173]
Voice: [(847) 576-8706] E-mail: (john.barr@motorola.com]
Re: [ ]
Abstract: [This presentation highlights the form and status of TG3]
Purpose: [Allow TG3 members to communicate consistent information about TG3 efforts.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
<Name and Title>
<Company>
<Address>
<phone>
<email address>
IEEE 802.15.3 High Rate WPAN™

## Slide 3: Objectives of IEEE 802
To develop consensus standards that benefits the World Wide Networked Society.
Maintain the imperative principals of standards making:
  Due process
  Consensus
  Openness
  Balance
  Rights of appeal
Publish LAN/MAN Standards in electronic format

## Slide 4: IEEE 802 Architecture

## Slide 5: IEEE 802.15 Charter
Wireless Personal Area Networks (WPANsTM)
  Short-range
  Low Power
  Low Cost
  Small networks
  Ad hoc network formation
  Power management
  Communication of devices within a Personal Operating Space (10m sphere)

## Slide 6: IEEE 802.15 Working Groups
802.15.1 (Bluetooth Standardization Task Group)
  IEEE Standard of Bluetooth™ Specification
802.15.2 (Recommended Practice)
  Model and Facilitate Coexistence of WPAN & WLAN devices
802.15.3 (High Rate WPAN Standard Task Group)
  A High-Rate (> 20 Mbps) WPAN
802.15.4 (Low Rate WPAN Standard Task Group)
  Raw Data Rate = 2Kb/sec to 200Kb/sec

## Slide 7: IEEE 802.15 Org chart
You
are
Here

## Slide 8: Wireless Personal Area Networks “WPANs”
WPANs address communication needs within personal operating space < 10m
IEEE 802.15.3 is chartered with creating a high rate WPAN standard that provides
for low power, low cost, short range solutions targeted to consumer digital imaging
and multimedia applications
Games
Web Tablet
Printer
PDA
Laptop
Cell Phone
Digital
Camera
MP3 Player
Projector

## Slide 9: Application Summary
Multimedia and large file transfers between consumer devices.
Local video distribution and control
DCT-2000

## Slide 10: TG3 Application Needs
Consumer Market - Indoor/Outdoor
Simple to use
Cost is a KEY factor
Data rates well above 20 Mbps are needed for Multimedia applications
Standard has to happen quickly
Needs simple Quality of Service algorithm
Co-existence is important

## Slide 11: High Rate WPAN Applications
Multi megabyte “bulky” data transfers
  Image files: between digital cameras and PC/laptop or gateways
  Music files (MP3): between portable players and PC/laptop or gateways
  Targeted transfer time: 7 to 15 seconds
Video transmission
  High definition MPEG2 (19.2 Mbps): between HD displays and video player/gateways
  DVD (11 Mbps): home entertainment systems
High quality audio
  CD audio (1.5 Mbps), AC3 Dolby digital audio (384 Kbps) : between CD player and speakers, home entertainment systems
  Streaming MP3 (128 Kbps): between MP3 players and headsets/speakers

## Slide 12: High Rate WPAN Features
Physical Layer
Raw data rates commensurate with high definition video, high quality audio transmission, and rapid bulky data transfers (~ 50 Mbps)
RF front-end and baseband processors optimized for short range transmission
Low current drain (~ 80 mA) for extended battery life
Low cost and small form factor implementations for integration in consumer devices
MAC Layer
Support for multimedia QoS (guaranteed time slots)
Support for high rate asynchronous data transfer
‘Ad-hoc’ networking support (devices assume master or slave functionality based on existing network)
Power management (low current drain during idle periods)
Short connection time (ability to join an existing network rapidly, <<1 sec)

## Slide 13: IEEE 802.15.3 High Rate WPAN Standard
802.15.3 MAC layer designed to support:
  Multi-media QoS
    Guaranteed time slots for isochronous data transfers
    Slot width is assigned based on QoS rules
  “Ad-hoc” networking
    Any device may assume master or slave functionality (short connection time, <<1sec) based on existing network conditions
  Power management
    MAC protocol designed to significantly lower power consumption during idle or network scan periods
802.15.3 PHY layer designed to achieve….
  raw data rates up to 55 Mbps
  low cost, low complexity, and low power RF front-end and baseband processor implementations

## Slide 14: IEEE 802.15.3 MAC Layer Overview
Contention Access Period
(CAP)
Guaranteed Time Slots
(GTS)
BEACON
BEACON
...
...
Superframe
WPAN
Parameters
Small command/control functions
Duration can change depending on Isochronous demands
Pre-assigned start times allow Sleep modes
Isochronous data streams:
Standard definition MPEG2, 4.5 Mbps
High definition MPEG2, 19.2 Mbps
MPEG1, 1.5 Mbps
DVD, up to 9.8 Mbps
CD Audio, 1.5 Mbps
AC3 Dolby digital, 448 Kbps
MP3 streaming audio, 128 Kbps
Asynchronous data transfers:
Image files
MP3 music files
(All multi megabyte files)

## Slide 15: IEEE 802.15.3 PHY Layer Overview

## Slide 16: 802.11 Comparison
IEEE 802.11 “a,b,e, and g” Extensions
  802.11 MAC specification is unnecessarily burdened with LAN (Local Area Networks) functionality and applications such as roaming, WEP (Wired Equivalent Privacy) specific authentication and encryption, access point control functions (not ‘ad-hoc’), scheduling, etc., and little consideration given to power management
  Even though 802.11e MAC additions are projected to provide for multimedia QoS, legacy burden for LAN functionality renders the MAC implementations too complex and power inefficient for WPAN applications
  802.11b PHY layer supports data rates only up to 11 Mbps (not nearly sufficient for WPAN applications), support for higher data rates (currently under 802.11g) require FCC rule change in the 2.4 GHz band
  802.11a PHY layer supports data rates up to 54 Mbps, but OFDM baseband processor consumes too much power and requires too expensive RF front-end implementations for WPAN applications and devices

## Slide 17: Wireless M/M alternatives

## Slide 18: Status and Plans for TG3
November 2000 - Reduction of Proposals to 1PHY/1MAC
May 2001 - Complete Initial Draft (PHY and Data Link layers)
July 2001 –
  Prepare Initial Draft for Letter Balloting
  Consideration of alternate PHYs
November, 2001 - Sponsor Ballot
Standard by the end of 2001 or early 2002
Notes: <number>
<footer>
<header>
<date/time>

## Slide 19: Contact Data
Website: http://www.ieee802.org/15/pub/TG3.html
Chair: john.barr@motorola.com
Vice Chair: james.d.allen@kodak.com
Secretary: pat.kinney@invensys.com
PHY Comm. Chair: jgilb@mobilian.com
MAC Comm. Chair: aheberling@xtremespectrum.com
SYS Comm. Chair: rick@xtremespectrum.com
Public List Server: stds-802-wpan@ieee.org