## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [TG3-PHY-Committee-Monterey-Report]
Date Submitted: [14 May 2001]
Source: [James P. K. Gilb] Company [Mobilian]
Address [11031 Via Frontera, Suite C, San Diego, CA 92127]
Voice:[1-858-217-2201], FAX: [1-858-217-2301], E-Mail:[gilb@ieee.org]
Re: []
Abstract: [A summary of the work accomplished by the PHY committee in conference calls and via email since the last meeting in Hilton Head and a summary of the work accomplished in Orlando.]
Purpose: [Document the work accomplished by the PHY committee.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: PHY Decisions Reached
Agreed to 2048 byte packets
  caveat is that systems should scale back when the packet loss goes up (will be added for d05)
Resolved PHY layer management issues
  see system report for detail
Modified TX/RX turnaround definitions slightly
  TX to RX < 10 us
  10 us < RX to TX < 11 us (please review)
IFS definitions
  10 us for turnaround, 15 us to detect clear channel

## Slide 3: PHY Decisions Reached (cont.)
New suggestion for jamming test
  presented in later slide
Link quality indication (LQI)
  Adopt 802.11 DS RSSI specification
    See that document, please comment
  Add optional mean squared error (MSE)
    Jeyhan is working on suggestion
Header FEC
  Two possibilities, BPSK and twice repeated header+HCS - see 01/244 for analysis

## Slide 4: Jamming Test
Latest suggestion for alternate channel rejection, makes 802.15.3 comparable to 802.11a
New definitions of adjacent and alternate channel in d04
Suggest changing desired signal to 5 dB above reference sensitivity instead of 10 dB (for easier linearity requirements).
Data Rate (Mbit/s)
Minimum sensitivity
Adjacent channel rejection (dB)
Alternate channel rejection (dB)
22
-75 dBm
10 dB
26 dB
33
-74 dBm
6 dB
22 dB
44
-71 dBm
3 dB
19 dB
55
-68 dBm
0 dB
16 dB

## Slide 5: Outstanding issues
OQPSK vs. QPSK
CCA definition
Header FEC
TX clock/frequency synchronization
Review modulation accuracy requirements
  need to balance TX and RX complexity
Review jamming test desired signal power
RSSI – MSE definition
Whitener initialization
Coexistence – describe steps used
Add PHY description to the overview clause