## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Merged IPC and TI Adaptive Frequency Hopping Proposal
Date Submitted: May 14, 2001
Source: (1) KC Chen, HK Chen, CC Chao (2) Anuj Batra, Kofi Anim-Appiah, and Jin-Meng Ho
Company: (1) Integrated Programmable Communications, Inc. (2) Texas Instruments, Inc.
Address: (1)Taiwan Laboratories Address: P.O. Box 4-2, Chupei, Hsinchu, Taiwan 302
(2) 12500 TI Boulevural, Dallas, TX 75025
TEL(1) +886 3 553 9128, FAX: +886 3 553 9153, E-Mail: {kc,hkchen,ccc}@inprocomm.com
(2) +1 214 480 4220, E-Mail: batra@ti.com
Re: Submission of a Coexistence Mechanism in response to IEEE 802.15-00/009r4
Abstract: Submission to Task Group 2 for consideration as the coexistence mechanism for 802.15.2. It merges two prior submissions in the category of adaptive frequency hopping.
Purpose: Description of Proposal
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Merged IPC and TI Adaptive Frequency Hopping Proposal
KC Chen, HK Chen, CC Chao
Integrated Programmable Communications, Inc.
Anuj Batra, Kofi Anim-Appiah, and Jin-Meng Ho
Texas Instruments

## Slide 3: Outline
Present the unified framework for a merged adaptive frequency hopping proposal.
Also, we will present an enhancement (ESHA) for the SCO link from Selective Hopping for Hit Avoidance (SHA).
Finally, we will show the relationship of this merged proposal to other proposals presented in 802.15.2.

## Slide 4: Unified Framework for Merged Proposal

## Slide 5: Bluetooth Degradation
In an interference-limited environment, the throughput for a Bluetooth device is often degraded.
The throughput, however, can be improved by avoiding bad channels.
One way to avoid the bad channels is to rearrange the hopping sequence (introduce some structure).
The “Two Layer Structure” can be used to rearrange (modify) the original Bluetooth hopping sequence.

## Slide 6: Channel Quality Assessment (1)
Leave actual method for channel quality assessment undefined.
  Each manufacturer will have its own proprietary implementation
  Examples
    From the combination of RSSI and error detection (HEC, CRC, FEC)
    Listen to the channel during channel idle time
    Special hardware to detect some specific interference, such as 802.11b CCA
    Divide the band into N sub-bands for detection
      Small N for fast assessment, large N for better frequency resolution
      N=3 for 802.11b at channel 1, 6, 11
      N=79 for access each channel independently
      3<N<79 as a compromised solution
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 7: Channel Quality Assessment (2)
Regardless of the real implementation, the result can be mapped to the same format:
  A list of 79 items, one for each channel, indicating the corresponding channel is good/bad/unused, requiring 2*79=158 bits.
  Unused channels allow to use less than 79 channels.
The recommended practice:
  Should have standardized format and procedure to exchange the information of channel quality assessment
  May include suggested values for assessment time
    The requirement for assessment time is application specific.
    SCO link should demand shorter assessment time.
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 8: Two Layer Structure for HS
Frequency synthesizer
Partition mapping
Original hopping sequence generator
Hop clock
RF input signal
partition sequence

## Slide 9: Partitions
“Two Layer Structure” is based on partitions of the Bluetooth channels.
The partition sequences specify “when” to use “which” partition. They are designed for optimal coexistence performance.
The partition mapping
  It primary function is to select one channel in the given partition
  We maintain the pseudo-random property of the original Bluetooth hopping sequence.
Example of a frequency partition is given on the next slide.

## Slide 10: Example of Frequency Partition
Partition number
Corresponding Bluetooth channel number*
Total channels in this partition
Corresponding 802.11b
Channel number
1
0-22,75-77
26
1
2
23-47,74
26
6
3
48-72,73
26
11
*Channel 78 is not involved in any partitions to equalize the size of each partition.

## Slide 11: Example of HS from the Structure
23 | 22 | 53 | 40 | 57 | 42 | 21 | 36 | 25 | 38 | 27 | 63
2 | 1 | 3 | 2 | 3 | 2 | 1 | 2 | 2 | 2 | 2 | 3
1 | 1 | 2 | 2 | 3 | 3 | 1 | 1 | 3 | 3 | 2 | 2
75 | 22 | 27 | 40 | 57 | 69 | 21 | 10 | 52 | 65 | 27 | 37
Partition sequence
Corresponding partitions of original sequence
Original hopping sequence
Hopping sequence after mapping
P1 | P2 | P3
Colors

## Slide 12: Definition of Partitions
For an SCO link, use the three partitions described on previous slide.
For an ACL link, use two partitions:
  Partition 1 is composed of the good channels (length = NG).
  Partition 2 is composed of the bad channels (length = NB).
  Let Nmin = min. frequencies defined by FCC and min. needed for frequency diversity.
Nmin  NG + NB  79
  Note that it possible some of the channels are unused, i.e., there are not in either partition.
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 13: An Example of Partition Sequence for an SCO Link (1)
In this example:
  The partition sequence is repeating {1,2,3,1,3,2}.
    Each element represents a master slot and a slave slot.
  The traffic is an HV2 link with the parameters Tsco=4, Dsco=0,1
    The reserved slots for the SCO link is red
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Hop
SCO slots
1 | 2 | 3 | 1 | 3 | 2
Partition sequence

## Slide 14: An Example of Partition Sequence for an SCO Link (2)
In the this period of 12 hops, there are 6 M-S (Master-Slave) pairs.
  The HV2 link occupies 3 M-S pairs.
    Two of the M-S pairs are of partition 3
    The other one of the M-S pairs is of partition 1.
    Partition 2 is never used in this SCO link.
  We define the partition usage vector to show the relative frequency of the partitions in the reserved slots, given the traffic and the sequence.
    The partition usage vector in this example is
    U=( u1, u2, u3 ) = (1, 0 ,2)
This partition sequence is good to use when
  Partition 2 is severely interfered, the other partitions are clean.

## Slide 15: Primary Ideas of Partition Sequence for an SCO Link
Slots in SCO links are periodic and scheduled
  We can match the good partitions to the reserved slots, by designing the partition sequence
  A set of partitions sequences are designed to cover
    Which of the partitions are better?
    What is the traffic requirement?

## Slide 16: Partition Sequence for an SCO Link
For an SCO link, select a partition sequence from the table given on next slide.
  The selection is performed at the master only.
  A baseline selection algorithm is provided.
  A least part of the selection algorithm has to be standardized
    To guarantee the coexistence performance
      If one manufacturer implements this algorithm incorrectly, then all of Bluetooth manufacturers will suffer, esp. in the press.
    To keep interoperability
The partition sequences and necessary parameters are then sent to each slave in the piconet.

## Slide 17: Baseline Partition Sequence Selection Algorithm for an SCO link(1)
  Calculate a hit ratio for each partition as the ratio of the number of interference events to the number of total events
    For partitions with interference hit ratios below threshold, corresponding hit ratios are set to be zero.
  From the time slots reserved by the traffic requirements, calculate the partition usage vector for each of the partition sequences.
  Select the partition sequence with minimal H(p)

## Slide 18: Baseline Partition Sequence Selection Algorithm for an SCO Link(2)
Definition of H(p)
  H(p) is defined for each sequence p with given traffic requirement,
where Np is the number of partitions,
R(k) is the measured hit ratio of the k-th partition,
uk(p) is the k-th element of the partition usage vector of the partition
sequence p.
A sequence that utilizes better partitions (lower hit ratios) more frequently has lower H(p).

## Slide 19: Baseline Partition Sequence Selection Algorithm for an SCO Link(3)
Definition of partition usage vector
  The partition usage vector U(p) is calculated for a partition sequence p given the time slots reserved by traffic requirement.
  The k-th element of U(p), uk(p), is proportional to the relative frequency of partition k in the reserved time slots.

## Slide 20: A Set of Partition Sequences

## Slide 21: Partition Sequence for an ACL Link
Consider the following hopping sequence with fixed block lengths:
For an ACL link, the sequence is completely described by parameters RG and RB.
  The equations for selecting RG and RB are give in next 2 slides.
For this link, the partition sequence is binary (either 1 or 2).
This sequence and the necessary parameters are then sent to each slave within the piconet.

## Slide 22: Parameters for ACL Link (1)
Note:
  During blocks of good channels: 100% of packets are received.
  During blocks of bad channels: 0% packets are received.
  Define “Dead Time” = DT = 625 s · RB.
To comply with FCC regulations, need addition restriction:
Process for selecting:
  “Dead Time” requirement for application dictates value of RB.
  Given , RG must satisfy FCC constraint.
  If RG = 0, then must use a larger value of RB.

## Slide 23: Parameters for ACL Link (2)
Assume a fully-loaded link, where the master-to-slave packet is DM/H-M and where the slave-to-master packet is DM/H-S.
The optimal values for the block lengths are given by:
The aggregate throughput is then given by:

## Slide 24: Channel Mapping
Want to design a new hopping sequence that shares many of the same channels as the original hopping sequence.
This new sequence will have many advantages:
  It is backwards compatible, i.e., can support both the old and new sequences in the same piconet.
  It supports broadcast packets.
  Helps to maintain channel hop clock synchronization.
Channel in the original hopping sequence
Desired partition specified by the partition sequence
action
Good
Good
Keep the same
Good\Unused
Bad
Mapping
Bad \Unused
Good
Mapping
Bad
Bad
Keep the same
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 25: Pseudo-random mapping
Mod Nj
Size of partition
Good
Nj
Selected channel number of original hopping sequence (0~78)
Current partition = j
(from partition sequence)
shifter signal
Mapping table of this partition
Bad
Maintain the pseudo-random property of the original hopping sequence
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 26: Shifter Signal
If the input is uniformly distributed in the range [0, N – 1], then the output of MOD(Nj) will not be uniformly distributed, unless N is multiple of Nj.
To force a uniform output distribution, we add a “shifter signal” to the input.
A simple example of a shifter signal is given by:
  Two counters, one for each partition.
  Each counter has the range [0, Nj – 1].
  The counter of selected partition counts up by one each time.

## Slide 27: Enhancements to the SCO link

## Slide 28: Enhanced SHA (ESHA) for SCO Link
Enhancement:
  Takes full advantage of the possibility that good channels may reside in the bad partition.
  Most effective for narrowband interference sources and possibly narrowband 802.11b signals.

## Slide 29: Description of Enhancements
What stays the same:
  “Two layer structure” to modify hopping sequence.
  Pseudo-random mapping device.
  The idea of allocating good channels in the good partitions for the SCO link remains the same.
What is new:
  The partitioning is now dynamic, as was done for the ACL link.
  An algorithm to generate the new partition sequence.
    This algorithm replaces the “select one from the table” method.

## Slide 30: System Architecture
Frequency synthesizer
Multiplexer
Partition mapping re-mapping
Hopping sequence generation
Original/Mapped sequence selection
Partition sequence generation
Channel partitioning
Traffic requirement
Hop clock
RF input signal
Partition sequence change procedure
Packet target
Channel usage requirement
Channel interference measurement
Interference indicator from integrated / collocated devices
Modified blocks are red

## Slide 31: Partitioning for Enhanced SHA
Exactly the same as that for the ACL link.
The contents of the partitions are now dynamic:
  Partition 1 is composed of the good channels (length = NG).
  Partition 2 is composed of the bad channels (length = NB).
  Let Nmin = min. frequencies defined by FCC and min. needed for frequency diversity.
Nmin  NG + NB  79
  Note that it possible some of the channels are unused, i.e., there are not in either partition.
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 32: Partition Sequence for ESHA (1)
Focus on HV2 and HV3 links.
Let MAU be the minimal allocation unit.
  MAU = 2 hops  master and slave slots are in the same partition.
Let the Frame be matched to the period of the HV link.
  For HV2: one Frame = 2 MAUs = 4 hops.
  For HV3: one Frame = 3 MAUs = 6 hops.
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 33: Partition Sequence for ESHA (2)
Considering from an example:
  NG=5, NB=6, total channel =11.
  Note that the relative frequency of partitions in the partition sequence should be proportional to the partition size.
  In a HV3 frame, which has 3 MAUs
    Averagely we should have MG= 3*5/11 good MAUs, and MB= 3*6/11 bad MAUs.
    These numbers are not integers
      This is why we introduce superframe
  In a superframe cmposed of 11 frames
    Total MAUs = 11*3= 33
    Averagely we should have MG= 33*5/11=15 good MAUs, and MB= 33*6/11=18 bad MAUs.

## Slide 34: Partition Sequence for ESHA (2)
Structure of partition sequence:
  Let the Super-frame be the period of partition sequence.
  Each super-frame is composed of Ls frames, and each frame is composed of Lf MAU.
Super-frame
Super-frame
Super-frame
0
2
1
Lf -1
frame
0
2
1
Ls -1
frame
MAU
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 35: ESHA Partition Sequence Example (1)
Illustration of distributing the MG MAUs
P2
P2
P2
P2
P2
P2
P2
P2
P2
P2
P2
P1
P2
P2
P1
P2
P2
P1
P2
P2
P1
P2
P1
P1
P1
P1
P1
P1
P1
P1
P1
P1
P1
Frame
0
1
2
3
4
5
6
7
8
9
10
good
bad
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 36: ESHA Partition Sequence Example (2)
i=0
1
2
3
4
5
6
7
8
9
10
m(i,G)
2
1
1
2
1
1
2
1
1
2
1
m(i,B)
1
2
2
1
2
2
1
2
2
1
2
Hop clock%6
0
1
2
3
4
5
Reserved hop
Reserved
Reserved
MAU slot
0
1
2
Traffic priority sequence
1
0
1
Traffic requirement (one HV3, Dsco=2,3):
The number of MAUs in each frame:
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 37: ESHA Partition Sequence Example (3)
The resulting partition sequence:
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32
These good MAUs are for SCO link
These good MAUs can be used for ACL link
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 38: Partition Sequence for ESHA: Detail Algorithm and Equations (1)
Partition sequence generation procedure:
  Calculate MG, the number of good MAUs in a super-frame.
  Distribute these MG MAUs to the Ls frames.
    The i-th frame will have m(i,G) good MAUs.
  Arrange the order of MAUs within each frame according to the traffic requirement.
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 39: Partition Sequence for ESHA: Detail Algorithm and Equations (2)
Number of MAUs of the good/bad partition: MG/MB
Number of MAUs of the good/bad partition in the i-th frame: m(i,G) / m(i,B)
  The first term is the maximal integer number of good MAUs that each frame can have.
  The second term d(i) is in the set {0,1}, indicating the frames having one more good MAUs.
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 40: Partition Sequence for ESHA: Detail Algorithm and Equations (3)
Equations for d(i)
  The residue good MAUs need to distribute
  To minimize the max spacing ‘c’ between these residue good MAUs when spreading them into Ls frames

## Slide 41: Partition Sequence for ESHA: Detail Algorithm and Equations (4)
The order of MAUs within each frame according to the traffic requirement
  Traffic priority sequence:
    A SCO slot will have a priority of 0 and it is the higher priority traffic
    a non-SCO slot will have a priority of 1 and it is the lower priority traffic.
  Rules:
    A slot with priority 0 has higher preference for the good MAU
    If there are two slots with the same priority number, the first slot in time has higher preference for the good MAU

## Slide 42: Relationship to Other Proposals

## Slide 43: Relationship to other proposals (1)
If the number of good channels in the band is greater than Nmin, then:
  We can choose NB = 0.
  Recall the restriction: Nmin  NG + NB.
  The adaptive frequency hopping algorithm therefore reduces to using only the good channels.
  Note that in this case, the partition sequence becomes a constant signal.
For this case, the merged proposal is very similar to the one proposed by Bandspeed.

## Slide 44: Relationship to other proposals (2)
Relationship to Bandspeed’s proposal
  The merged proposal degenerates to use a single good parition when there are enough good channels
  The same nice property: design a new hopping sequence that shares many of the same channels as the original hopping sequence.
  The only difference left is the mapping device, periodic or pseudo-random.

## Slide 45: Relationship to other proposals (3)
Relationship to Eliezer’s proposal
  The size of the good paritition is fixed as 23 (or other prime number) channels
  Use the good partition only
  The mapping device is periodic.

## Slide 46: Relationship to other proposals (4)
Benefit of the merged proposal
  Treat the proposals of “using good channels only” as a special case
  Provide the unified structure of high power/ low power devices
  Provide the smooth way for the possibly regulation changes

## Slide 47: Conclusions
New algorithm effectively support both SCO and ACL links.
  Guarantees services under certain traffic conditions.
  Performs well even in the presence of interference.
The algorithm is simple and backwards compatible:
  Can be implemented as a stand-alone module.
  Sequence is generated at master to prevent complicated two-way exchange of information (avoid delay).
Works with existing FCC rules. Also flexible to work with new FCC rules.

## Slide 48: References
K. C. Chen, H. K. Chen, C. C. Chao, Selective Hopping for Hit Avoidance [01/057r2]
A. Batra, K. Anim-Appiah, J.-M. Ho, An Intelligent Frequency Hopping Scheme for Improved Bluetooth Throughput in an Interference-Limited Environment [01/082r1]
H. B. Gan et al., Adaptive Frequency Hopping [00/367r1]

## Slide 49: Merged Proposal Response to Evaluation Criteria (I)
Collaborative or Non-collaborative:
  Its default setup is non-collaborative but collaborative is also defined.
Improved WLAN and WPAN Performance:
  WPAN throughput increases.
  WLAN BER/throughput improves.
Impacts on Standards:
  Minimum changes (ACL/SCO) in WPAN.
Regulatory Impact
  None and future changes are allowed.
Complexity:
  One extra implementation module in link-layer.

## Slide 50: Merged Proposal Response to Evaluation Criteria (II)
Interoperability with systems that do not include co-existence mechanism:
  Yes.
Impact on Interface to Higher Layers:
  None.
Applicability to Classes of Operation:
  Yes.
Voice and Data Support in Bluetooth:
  Yes.
Impact on Power Management:
  Increases life of battery because devices will not transmit on bad channels.