## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: IEEE802.15.3: A proposal to modify the frame types and commands.
Date Submitted: 15May, 2001
Source: Dr. William Shvodian Company: XtremeSpectrum
Address: 8133 Leesburg Pike, Suite 700, Vienna, Virginia 22182
Voice: +1.703.749-0230 X7129, FAX: +1.703.749.0249, E-Mail: bshvodian@xtremespectrum.com
Re: [ ]
Abstract: This proposal presents modified frame type definitions that provide a coherent organization of frame types.
Purpose: To provide an improvement to the current version of the 802.15.2 MAC CFP
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that these viewgraphs becomes the property of IEEE and may be made publicly available by P802.15, however, the substance of the subject matter contained in the viewgraphs remains the property of XtremeSpectrum Inc

## Slide 2: Overview
New Frame Types, Command frames convertede to unique frames
New ACK policy – Piggybacked ACK
2 Station Addresses for the Coordinator station
Rate in CTA and Channel time request to support multiple preamble lengths
Coordinator Challenge Frame
Simplified Coordinator Selection Fields
Replace TSF with Beacon number
Modify the Association Response so that it contains the entire Table MAP
New capability field: MAX GTS slots assigned to a station
Shared GTS slots

## Slide 3: Overview
The current Frame Types and Commands are not organized in a consistent manner. Some items are unique frames, while others are commands. It is not clear what the criterion was for assigning a primitive to have a unique frame format versus being a command type frame.
A recommended change allows all commands to be represented as unique frame types.

## Slide 4: Proposals
Option 1: If we delete Frame Position Field or use two reserved bits, we can use 6 bits for the frame type
Option 2: If we only don’t want to use 6 bits, we can separate primitives into management or control.

## Slide 5: Option 1: Management Frame Types

## Slide 6: Option 1: Control and Data frame types

## Slide 7: Option 2: Separate Management frames and Command Frames

## Slide 8: Command Primitives
Immediate Acknowledgment
Remain Quiet
Retransmission Request
Retransmission Sequence Resync
Beacon

## Slide 9: Management Primitives
Channel Time Request
Channel Time Grant
Probe Information
Repeater Service Request
Repeater Service Grant
Repeater Service Reject
Channel status Request
Channel status Response (new)
Coordinator Selection
Coordinator Hand-over
Device Information Request
Device Information Table (Response)
Stream Management Request
Stream Management Indication
Stream Management Response
Stream Management Confirm
Association Request
Association Response
Disassociation Request

## Slide 10: Recommended Frame Types
Use 6 bits for the frame type field.

## Slide 11: Current ACK Policy
Current ACK Policies:
  0 - No ACK
  1 – Immediate ACK
  2 – Delayed ACK
  3 – Reserved

## Slide 12: New ACK Policy
Current ACK Policies:
  0 - No ACK
  1 – Immediate ACK
  2 – Delayed ACK
  3 – Piggyback ACK. Piggyback ACK policy allows the receiving stations to send either an immediate ACK frame, or any other frame where the destination address is the same as the source address of the frame with the piggyback ACK policy set. The stream index and sequence control field are set based on the frame that is being transmitted, not the one that is being ACKed

## Slide 13: Dual Station Address for the Coordinator
In the baseline, the coordinator station is assigned a single 8 bit station address, address ’00’. This makes coordinator handoff challenging because each station now has to switch the address for the non-coordinator traffic bound for the station that was the coordinator.
We recommend assigning two station addresses to the coordinator station: Address ’00’ for all coordinator traffic, and a regular 8 bit address for all of the non-coordinator traffic bound for that station.

## Slide 14: Variable Length Preamble/Header
In 802.11 stations use the same preamble and header because in a CSMA/CA system all stations need to hear the preamble and Header.
In 802.15.3 if the header is always at the lowest rate, this can result in significant overhead
In 802.15.3, because GTS slots are assigned to specific SA/DA pairs, the slot can be assigned to use a particular
Since the CTA has been reduced from 12 bytes to 4, we recommend adding a byte to the CTA to specify the preamble/header length/rate. CTAs will now be 5 bytes long. Also, preamble/header length/rate field needs to be added to Channel Time Request

## Slide 15: Coordinator Challenge Frame
Currently there is no mechanism for a station to challenge the coordinator of a currently established piconet. It may be desirable for a number of reasons to enable a station to initiate a challenge to be coordinator of the piconet.
We recommend the creation of a Coordinator Challenge frame.

## Slide 16: Baseline Coordinator Selection Fields
Field Value Comment
RTC bit in capability field RTC=1 is preferred What does this mean? Delete
SEC bit in capability field SEC=1 is preferred
PS bit in capability field PS=0 is preferred PS is currently undefined
Storage Type sub-field in capability field
Higher value is preferred Remove
Total Ext connections Higher value is preferred What does this mean?
Active Ext connections Higher value is preferred What does this mean?
Total System Memory Higher value is preferred Depends on implementation
Avail System Memory Higher value is preferred Available for what?
Max PHY Range Higher value is preferred related to rate
Max PHY Rate Higher value is preferred related to range
Device ID Higher value is preferred

## Slide 17: Recommended Coordinator Selection Fields
Designated Coordinator bit in capability field. This enables a user to select which device should be coordinator, and override the coordinator selection capabilities comparison.
Coordinator designation is preferred
SEC bit in capability field SEC=1 is preferred
Battery/AC Power AC power is preferred
PS bit in capability field PS=0 is preferred
MAX GTS slots Higher value is preferred
Repeater Memory (>0 indicates repeater capable)
Higher value is preferred
Max Repeater Rate supported Higher value is preferred
Device ID Higher value is preferred

## Slide 18: Replace TSF with Beacon Number
TSF function is overkill for 802.15.3
This is needed in 802.11 to support negotiation timing in ad hoc mode. It is also needed in a frequency hopping system. It is not needed in 802.15.3
Replace the TSF field with a beacon number. All times in the superframe are relative to the beacon time.

## Slide 19: Modified Association Response
Baseline Association Response: only contains the information for the new station.
Modified Association Response: In addition to the association response frame, a Device Information Table frame is broadcast so that the new station and all of thee stations in the piconet have the most up to date piconet information

## Slide 20: Add MAX GTS Slots to capability Field
In order to limit the complexity of a station, it is desirable to limit the number of GTS slots assigned to a station
Adding a Max GTS slots field to the capabilities field allows implementers to bound the number of GTS slots that they support.

## Slide 21: Assigning GTS Slots to Multiple Destination Addresses
Review the assignment mechanism for GTS
Introduce the concept of multiple destination addresses for GTS slot assignments
Show how Multiple Destination Addresses can be used to efficiently share bandwidth between variable bit rate streams

## Slide 22
GTS with Source-Destination Assignments
Guaranteed Time Slots
Contention
Access
Period
Beacon
Contention Free Period
Guaranteed Time Slots (GTS) are fixed assignment times
Beacons contain the assignments
Slots assigned to source/destination (SA->DA) pair to enable power savings for transmitting and receiving terminals
Unassigned Slot
1 4
1 3
1 2
2 1
3 1
4 1

## Slide 23
GTS with Multiple Destination Assignments
Guaranteed Time Slots
Contention
Access
Period
Beacon
Contention Free Period
Guaranteed Time Slots (GTS) are fixed assignment times
Beacons contain the assignments
Slots assigned to source/destination (SA->DA) pair.
Destination assignments can be assigned to multiple destination stations, so that station number 1 can dynamically allocate bandwidth to several variable bit rate streams. Alternatively, a slot can be assigned to a group address (G99 here)
Unassigned Slot
1 3
2 1
3 1
4 1
1 2
1 4
Contention
Access
Period
Beacon
Contention Free Period
1 G99
2 1
3 1
4 1

## Slide 24
Set Top Box – Video Distribution Example
Station 4
Coordinator
Station 1
Station 3
Station 5
Station 2

## Slide 25
GTS Multiple Destination Slot Details
Source/Destination Slot Assignment
GTS assigned to source 1, Group destination 99 (2, 3 and 4) in the Beacon CTA assignments
Source 1 can use group assigned GTS to transmit to any station in the group
The transmitted packets contain the source address (1) and the destination address (2, 3 or 4) for the particular stream
Stations 2, 3 and 4 listen during the destination assigned slot, and discard packets whose destination address does not match their own.
Source/Destination Packets
1 2
1 3
1 4
1 2
1 3
1 2
1 3
1 5
1 G99

## Slide 26
Shared GTS Slot Summary
Enable the use of multiple destination addresses so that a slot can be assigned to a particular source terminal that is able to send traffic bound for one of several destination addresses
This approach enables a source like a video distribution box to be able to dynamically re-allocate bandwidth for variable bit rate streams.
Needs work to define the mechanism for requesting and assigning shared GTS slots

## Slide 27: Overall Summary
Add New Frame Types - Command frames converted to unique frames
New ACK policy – Piggybacked ACK
2 Station Addresses for the Coordinator station
Rate in CTA and Channel time request to support multiple preamble lengths
Coordinator Challenge Frame
Simplified Coordinator Selection Fields
Replace TSF with Beacon number
Modify the Association Response so that it contains the entire Table MAP
New capability field: MAX GTS slots assigned to a station
Shared GTS slots – More work needed