## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Media Access Control proposal for the 802.15.4 Low Rate WPAN Standard]
Date Submitted: [May 2001]
Source: [Carl R. Stevenson] Company: [Agere Systems]
Address: [555 Union Boulevard, Room 22W214EQ, Allentown, PA 18109]
Voice:[(610) 712-8514], FAX: [(610) 712-4508], E-Mail:[carlstevenson@agere.com]
Re: [ MAC layer proposal submission, in response of the Call for Proposals ]
Abstract: [This contribution is a flexible MAC proposal for a Low Rate WPAN intended to be compliant with the P802.115.4 PAR. It is intended to support both master-slave and peer-to-peer communications. It can also optionally support node-to-node relay capabilities to provide robust communications in a variety of propagation environments to meet the needs of a wide range of low data rate applications. In its basic form, it can support up to 255 nodes per PAN, but through address extension can be expanded to support a much larger number of nodes.]
Purpose: [Response to IEEE 802.15.4 TG Call for Proposals]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
MAC Layer Proposal Submission to the IEEE P802.15.4 Low Rate WPAN Task Group

## Slide 3
Who is ?
Formerly Lucent Technologies Microelectronics Group
In the process of spinning off as an independent semiconductor company
Extensive experience in communications IC design, DSPs, and wireless systems design

## Slide 4: Description of MAC Layer Proposal (actually a MAC + LLC + at this point)
System Operation
  Half-duplex TDMA/CSMA-CA DAMA/contention based Protocol
    Network(s) controlled by “coordinator” unit(s)
    Beacon from coordinator defines TDMA frame structure
      p-persistent slotted aloha CSMA-CA reservation request slots
      Dynamic bandwidth allocations for time-sensitive traffic
      p-persistent slotted aloha CSMA-CA contention access slots
    Supports time-sensitive and asynchronous traffic through mix of assigned bandwidth and contention access
    Supports master-slave and peer-peer communications
    Possible for slaves to participate in > 1 network
    Possible to have gateways/portals to other dissimilar networks
    Promotes power efficiency through sleep modes

## Slide 5: HDLC-like Packet Structure Supports Protocols
Based on existing ISO/IEEE/other standards
Some SDL exists for similar protocols, which may be reusable with little modification
Transparent to data content
  Allows encapsulation of higher layer protocols between link layer DSAPs
  Does not impose data type dependencies
  Can transport encrypted payloads, if desirable
Small code size and CPU load possible
  Amateur packet radio implementations with nearly comparable complexity use 8-bit CPUs & 32k bytes of code
  Additional complexity for TDMA and other features should not be excessive

## Slide 6: Variable Length Packets

## Slide 7: Dynamically-assigned Frame Structure

## Slide 8: Frame Structure Can Vary Frame to Frame to Efficiently Handle a Mix of Traffic Types

## Slide 9: Slaves Can Be Moved to Other Channels Temporarily if Traffic Makes it Desirable

## Slide 10: MAC Implementation Concept (actually a MAC + LLC + at this point)
Substantially “Soft” MAC/LLC Implementation
  Proposal estimates based on synthesizable ARM7 core
  Frame buffers included in PHY size/power estimates
  4k Bytes RAM estimated for data
  128k bytes ROM estimated for MAC/LLC/Application code
  RAM and ROM sizes can be optimized as requirements become more clear (128k bytes of ROM is generous)
  Peripherals include 16 bits of GPIO & RTC (other options)
  Clock circuitry for scaleable clock rates including very low power ring oscillator for use during deep sleep modes
  Ring oscillator calibrated to master crystal oscillator to minimize clock drift during sleep modes
  Minimal additional support logic
  Application code space and CPU cycles available

## Slide 11: Power Mangement and Battery Life
Coordinators should generally be line-powered or have >> battery capacity than slaves
  Facilitates efficient, reliable network control
  Assures beacons are available regularly for slaves
  Power drain due to processing load becomes insignificant
Slaves can have extended operating life on modest batteries
  Slave devices make use of low power modes
  Coordinator can command slaves into deep sleep mode for multiple superframe intervals to conserve battery power in slave devices which can tolerate latency
  RSSI & link quality based TX power management possible
  Battery requirements/battery life depend on traffic load, TX power, and latency tolerance of a device

## Slide 12: Die Size Estimate - Total Solution (PHY + MAC + Misc)

## Slide 13: Power Consumption Estimate - Total Solution (PHY + MAC + Misc)

## Slide 14: General Solution Criteria
CRITERIA
REF.
VALUE
Unit Manufacturing Cost ($)
2.1
Based on area estimates + SOC mplementation, total system cost, including PHY, MAC, LLC & simple application est. to be ~ $1.00-$1.50
Interference and Susceptibility
2.2.2
Intermodulation Resistance
2.2.3
Jamming Resistance
2.2.4
Source 1: TBD- simulations under way
Source 2: TBD- simulations under way
Source 3: TBD- simulations under way
Source 4: TBD- simulations under way
Multiple Access
2.2.5
Scenario 1: TBD- simulations under way
Scenario 2: TBD- simulations under way
Scenario 3: TBD- simulations under way
Coexistence
2.2.6
Source 1: TBD- simulations under way
Source 2: TBD- simulations under way
Source 3: TBD- simulations under way
Source 4: TBD- simulations under way
Source 5: TBD- simulations under way
TBD – simulations under way
TBD- simulations under way

## Slide 15: General Solution Criteria (cont.)
CRITERIA
REF.
VALUE
Interoperability
2.3
TRUE
FALSE
Manufactureability
2.4.1
Time to Market
2.4.2
Regulatory Impact
2.4.3
TRUE
FALSE
Maturity of Solution
2.4.4
Scalability
2.5
Location Awareness
2.6
Not supported in terms of measuring relative locations in cm … RSSI and time of arrival techniques cannot readily provide much info
Yes – proposed system is based on substantial reuse of existing, proven technology which has been in high volume production for several years
Dependent on finalization of specification – could be as soon as ~ 6 months after final specification
Proposed system is based on substantial reuse of existing, proven technology which has been in high volume production for several years
Baasic concept can be scaled to other data rates, frequency bands, number of channels, etc.

## Slide 16: MAC Protocol Criteria
CRITERIA
REF.
VALUE
Transparent to Upper Layer Protocols (TCP/IP)
3.1
TRUE FALSE
Unique 48-bit Address
3.2.1
Subject to debate – needs further discussion
TRUE FALSE – gateway devices only
Simple Network Join/UnJoin Procedures for RF enabled devices
3.2.2
Network join/unjoin can be either automatic or manual.
Once network connection is established, sync is inherent.
Device Registration
3.2.3
Delivered data throughput
3.3.2
Traffic Types
3.4
(Breakdown of Application Requirements3.3.3)
Continuos Data - TBD
Periodic Data - TBD
Intermittent Data - TBD
Topology
3.5.1
Application dependent. Some apps need security of user intervention, some can be more promiscuous.
Raw data rate 160 kbps, scalable. Net throughput TBD pending sim results for various cases.
Mesh or star, master/slave, peer-peer, with relays to extend range

## Slide 17: MAC Protocol Criteria (cont.)
CRITERIA
REF.
VALUE
Max. # of devices
3.5.2
1. Address Space: 255, extendable 2a. Continuos Data: TBD rqmt. ill-defined 2b. Periodic Data: TBD rqmt. ill-defined 2c. Intermittent Data: TBD rqmt. ill-defined 3. Combination: TBD rqmt. ill-defined
Ad-Hoc Network
3.5.3
TRUE FALSE
Access to a Gateway
3.5.4
TRUE FALSE
Master Redundancy
3.6.2
TRUE – coordinator, not master, per se
FALSE
NOT APPLICABLE
Loss of Connection
3.6.3
TRUE – detect no beacon, new coordinator
FALSE
Power Management Types
3.7
Power Consumption of MAC controller
3.8
TX and RX: ~6.25mW (MAC @ 100 % d/c)
~68.75 mW (PMLA 100 % d/c)
Sleep: ~0.099 mW (P+M+L+A @ 0.1% d/c)
Deep Sleep: <0.030 mW
Proposed system includes extensive power management modes, including “deep sleep”

## Slide 18: MAC Protocol Criteria (cont.)
CRITERIA
REF.
VALUE
Authentication
3.9.1
Privacy
3.9.2
Proposal could support authentication at MAC layer, but we believe that authentication should be implemented in the application, as the requirement may be highly application depenent
Simple packet encryption can be provided at the MAC layer, but again, it may be more cost-effective to implement encryption of payloads at the application layer, due to application dependence of requirements

## Slide 19: Pugh Matrix Comparison Values General Solution Criteria Comparison Values
CRITERIA
REF.
Comparison Values
-
Same
+
Unit Manufacturing Cost ($) as a function of time (when product delivers) and volume
2.1
> ¼ x equivalent Bluetooth 1
1/20- x equivalent Bluetooth 1 value as indicated in Note #1
Notes:
1. Bluetooth 1 value is assumed to be $20 in 2H2000.
< 1/20 x equivalent Bluetooth 1
Interference and Susceptibility
2.2.2
Out of the proposed band: Worse performance than same criteria
In band: -: Interference protection is less than 25dB (excluding co-channel and adjacent channel)
Out of the proposed band: based on Bluetooth 1.0b (section A.4.3)
In band: Interference protection is less than 30dB (excluding co-channel and adjacent and first channel)
Out of the proposed band: Better performance than same criteria
In band: Interference protection is less greater than 35dB (excluding co-channel and adjacent channel)

## Slide 20: Pugh Matrix Comparison Values General Solution Criteria Comparison Values (cont.)
CRITERIA
REF.
Comparison Values
-
Same
+
Intermodulation
Resistance
2.2.3
Value 1)
< -45dBm
-35dBm to –45dBm
Needs clarification in Criteria Document
> -35dBm
Intermodulation above (sensitivity +3 dB) for minimum required data rate
2.2.3
Value 2)
< 25 dB
25 to 35 dB
Needs clarification in Criteria Document
> 35 dB
Jamming Resistance
Needs Simplification
2.2.4
Any 3 or more sources listed jam
2 sources jam
No more than 1 sources jams
Multiple Access
2.2.5
No Scenarios work
Handles Scenario 2
One or more of the other 2 scenarios work
Coexistence
(Evaluation for each of the 5 sources and the create a total value using the formula shown in note #3)
2.2.6
Individual Sources: less than 40%
(IC = -1)
Total: < 3
Individual Sources: 40% - 60%
(IC = 0)
Total: 3
Individual Sources: greater than 60% (IC = 1)
Total: > 3
Interoperability
2.3
False
True
N/A

## Slide 21: Pugh Matrix Comparison Values General Solution Criteria Comparison Values (cont.)
CRITERIA
REF.
Comparison Values
-
Same
+
Manufactureability
2.4.1
Expert opinion, models
Experiments
Pre-existence examples, demo
Time to Market
When Spec Final?
2.4.2
Available after 1Q2002
Available in 1Q2002
Available earlier than 1Q2002
Regulatory Impact
2.4.3
False
True
N/A
Maturity of Solution
2.4.4
Expert opinion, models
Experiments
Pre-existence examples, demo
Scalability
2.5
Scalability in 1 or less than of the 5 areas listed
Scalability in 2 areas of the 5 listed
Scalability in 3 or more of the 5 areas listed
Location Awareness
2.6
N/A
FALSE
TRUE
Note 3: Total equation for coexistence value calculation. Individual comparison values (-, same, +) are represented by the following numbers: - equals –1, same equals 0, + equals +1. The individual comparison values will be represented as IC in the equation below, with the subscript representing the source number referenced.
Total = 2 * IC1 + 2 * IC2 + IC3 + IC4 + IC5

## Slide 22: Pugh Matrix Comparison Values MAC Protocol Criteria Criteria Comparison Values
CRITERIA
REF.
Comparison Values
-
Same
+
Transparent to Upper Layer Protocols (TCP/IP)
3.1
FALSE
TRUE
N/A
Unique 48-bit Address
Subject to debate
3.2.1
Not Qualified (required by 802)
Essential
Subject to debate
N/A
Simple Network Join/UnJoin Procedures for RF enabled devices
3.2.2
Extended procedure for joining network
802.15.1 style join
Enhanced self-configuration of network
Device Registration
Application-dependent
Needs further discussion
3.2.3
Requires manual configuration
802.15.1 style registration as specified in sections 8.10.7 and 11.6.5.1-4.
Auto registration based on profile
Delivered data throughput
3.3.2
Does not provide data throughput between 10kkbps and 200kbps
One data rate between 10kbps and 200kbps
Can be scaled, however.
2 or more data rates one between 10kbps and 100kbps and 1 <> 100kbps and 200kbps
Traffic Types
3.4
Supports 1 or 2 traffic types
Support for all 3 traffic types
Topology
3.5.1
Point-to-Multipoint only
Point-to-Multipoint &
Point-to-Point (with no Peer-to-Peer)
Point-to-Multipoint,
Point-to-Point &
Peer-to-Peer

## Slide 23: Pugh Matrix Comparison Values MAC Protocol Criteria Criteria Comparison Values (cont.)
CRITERIA
REF.
Comparison Values
-
Same
+
Max. # Devices
3.5.2
< 7
7
7
(255 with ext. possible)
Ad-Hoc Network
3.5.3
FALSE
TRUE
N/A
Access to a Gateway
3.5.4
FALSE
TRUE
N/A
Master Redundancy
3.6.2
FALSE
TRUE
N/A
Loss of Connection
3.6.3
FALSE
TRUE
N/A
Power Management Types
3.7
Does not provide power management
Provides power savings mechanisms
Uses power harvesting
Power Consumption of MAC controller (the peak power of the MAC combined with an appropriate PHY)
3.8
30mW (PMLA)
(average under real duty cycles will be MUCH less)
Between 5mW and 30mW
< 5mW
Authentication
3.9.1
N/A
No Authentication
(can support optional)
Enhanced authentication at MAC layer
Privacy
3.9.2
No encryption
No encryption
(can support optional)
Packet encryption