## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Peak-to-Average Ratio Analysis of QPSK, OQPSK, and 64-QAM for 802.15.3]
Date Submitted: [25 April 2001]
Source: [Stanley K. Ling and Susumu Hara] Company [Intel Corporation]
Address [9750 Goethe Road, M/S LOC 3/8, Sacramento, CA 95827]
Voice:[(916) 855-5000], FAX: [(916) 854-2809], E-Mail:[stan.k.ling@intel.com and susumu.hara@intel.com]
Re: []
Abstract: [This contribution presents simulation results of OQPSK vs. QPSK for 802.15.3 PHY. QPSK is supported because it retains the CAZAC properties of the preamble.]
Purpose: [For information only.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Simulation Model
3rd and 5th order non-linearity modeled in PA

## Slide 3: System Parameters
Parameters
Symbol rate: 11 Mbaud
SRRC alpha: 0.3
SRRC span: +/- 4 symbols
Modulation: QPSK, OQPSK, and 64-QAM
RF architecture, sample rate, and center frequency chosen to simplify the simulation model

## Slide 4: Simulation Results
The difference in Peak-to-Average Ratio (PAR) between QPSK and OQPSK is ~0.5 dB at the PA input.

## Slide 5: Simulation Results
QPSK requires 3.2 dB back-off from P_1dB
OQPSK requires 2.7 dB back-off from P_1dB
PABO calculated for identical output power

## Slide 6: Conclusions
PAR reduction of OQPSK modulation is less than 0.5 dB over QPSK modulation.
PA back-off is reduced by 0.5 dB for OQPSK.
This slight reduction eliminates CAZAC properties of the preamble: gain slight reduction in complexity of RF design at the expense of incurring large increase in complexity of BB/algorithm design.
QPSK should be used instead of OQPSK for the preamble, header, and 22 Mbit/s data mode.