## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Adaptive Frequency Hopping, a Non-collaborative Coexistence Mechanism
Date Submitted: 16th, May, 2001
Source: Bandspeed Inc, Integrated Programmable Communications, Inc., TI – Dallas, TI - Israel
Address:
E-Mail: {h.gan, b.treister} @bandspeed.com.au, {kc,hkchen} @inprocomm.com, {orene, batra} @ti.com
Re: Submission of a no-collaborative coexistence mechanism
Abstract: [The documentation presents a non-collaborative coexistence mechanism - Adaptive Frequency Hopping.
Purpose: [This is a submission to IEEE 802.15.2 of a Recommended Practice for a Non-collaborative Coexistence Mechanism.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Adaptive Frequency Hopping A Non-collaborative Coexistence Mechanism
Bandspeed (Bijan Treister, Hong Bing Gan et. al)
IPC (K.C Chen, H. K. Chen et. al)
TI (Dallas) (Anuj Batra et. al) TI (Israel) (Oren Eliezer et. al)

## Slide 3: Structure of AFH (1)
Frequency synthesizer
Partition mapping
Original hopping sequence generator
Hop clock
RF input signal
partition sequence

## Slide 4: Structure of AFH (2)
Partitioning channels into good/bad channels
  Possibly unused channels
Mode H:
  Partition sequence are designed to support traffic
Mode L:
  when the number of good channels are more than the required/desired number
  Using good channels only

## Slide 5
Components of the AFH Mechanism
Device Identification and Operation mode
Channel Classification
Exchange of Channel Information
Initiate/Terminate AFH
Mechanisms of AFH
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 6
1. Device Identification and Operation mode (1)
LMP Exchange verifying:
  Support of AFH and required mode of op.
  Command includes Nmin (minimum number of channels that must be used)
LMP_Support_AFH_Mode( )
Master
Slave
LMP_not_accepted
LMP_accepted

## Slide 7
1. Device Identification and Operation mode (2)
These information is exchanged when a new slave has joined the piconet.
AFH mode
  LMP_not_accepted means that slave does not use adaptive frequency hopping mechanism
  Low power devices may only support a simplified replacement of bad channels
  LMP_accepted means that slave accepts using adaptive frequency hopping mechanism

## Slide 8
2. Channel Classification (1)
Methods of classification include:
  CRC, HEC, FEC
  RSSI
  Packet Loss Ratio (PLR) vs. Channel
    If PLR is above threshold, declare a ‘bad’ channel
  Slave’s classifications data
  Transmission sensing
  Other techniques
Classification of the channels:
  ‘Good’ or ‘Bad’
  Possible extension in doc. 802.15-01/246r1

## Slide 9
2. Channel Classification (2)
Increased speed of classification
  Some links require that classification step is fast;
  Classification of N MHz wide channels;
  A ‘guilt by association’ method;
  Larger bandwidth interferers detected faster;
NB: An SCO link may require that the classification is done quickly to avoid
prolonged degradation of quality;
Option: continue classifying channels during AFH

## Slide 10
3. Exchange of Channel Information
Master makes final decision on channel classification.
  Good/Bad/Unused or Good/Bad (to be determined)
Master to Slave message
  Good/Bad/Unused or Good/Bad (to be determined)
Slave to Master message [optional]
  Good/Bad indication only

## Slide 11
4. Initiate /Terminate AFH (1)
Master
Slaves
LMP_Adaptive_Hopping_Request ( )
LMP_Accepted
LMP_Not_Accepted
Slaves may or may not accept adaptive hopping
Slaves
LMP_Regular_Hopping
LMP_Accepted
optional Re-classification of channels

## Slide 12
4. Initiate /Terminate AFH (2)
LMP request to initiate:
  Should carry extra parameters of the partition sequence in Mode H.
  The slave uses the new sequence after the success of this command
  The master knows which sequence to use for every slave.
LMP request to terminate
AFH will also be terminated after loss of synchronization.

## Slide 13: 5. Mechanism of AFH
Mode H: Baseline Document: 802.15-01/246r1
Channels are classified into 2 groups: (dynamic classification)
  Good channels (size = NG)
  Bad channels (size = NB = 79–NG)
Define Nmin to be the minimum number of channels that a Bluetooth device must hop over.
Depending on the relationship between Nmin, NG, and NB, only a portion of the previously defined groups need to be used:
  Nmin  NG: only use good channels in the HS (replace bad channels ~ Mode L)
  Nmin > NG: must use some or all of the bad, depends on Nmin
    If Nmin < 79, need to only use only a portion of bad channels (Nmin–NG)
    If Nmin = 79, must use all of the bad channels
When bad channels are used, “grouping/pairing” must be used.
When bad channels are not used, “grouping/paring” does not need to be used, only replacement of bad channels.

## Slide 14: Mode H: Partitions
In Mode H, use two partitions:
  Partition 1 is composed of the good channels (length = NG).
  Partition 2 is composed of the bad channels (length = NB).
  Let Nmin = min. frequencies defined by FCC and min. needed for frequency diversity.
Nmin  NG + NB  79
  Note that it possible some of the channels are unused, i.e., there are not in either partition.
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 15: Mode H: Partition Sequence for ACL Link
Consider the following hopping sequence with fixed block lengths:
For an ACL link, the sequence is completely described by parameters RG and RB.
  The equations for selecting RG and RB are give in next 2 slides.
For this link, the partition sequence is binary (either 1 or 2).
This sequence and the necessary parameters are then sent to each slave within the piconet.

## Slide 16: Mode H: Pseudo-random mapping
Mod Nj
Size of partition
Good
Nj
Selected channel number of original hopping sequence (0~78)
Current partition = j
(from partition sequence)
shifter signal
Mapping table of this partition
Bad
Channel in the original hopping sequence
Desired partition specified by the partition sequence
action
Good
Good
Keep the same
Good\Unused
Bad
Mapping
Bad \Unused
Good
Mapping
Bad
Bad
Keep the same
Channel
Mapping:
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 17: Mode H: Enhanced SHA for SCO Links
Fundamental:
  “Two layer structure” to modify hopping sequence.
  Pseudo-random mapping device.
  The idea of allocating good channels in the good partitions for the SCO link remains the same.
Features:
  The partitioning is dynamic, as was done for the ACL link.
  An algorithm to generate the new partition sequence.
Advantages
  Takes full advantage of the possibility that good channels may reside in the bad partition.
  Most effective for narrowband interference sources and possibly narrowband 802.11b signals.
  A unification for SCO and ACL (01/246r1)

## Slide 18: Mode H: Partition Sequence Example
The resulting partition sequence:
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32
These good MAUs are for a HV3 link
These good MAUs can be used for ACL link
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 19: Mapping of Mode L
When the channel is good and Nmin ≤ NG do not re-map the channel:
When the channel is bad in the HS and a good channel is needed:
BluetoothSelection
Kernel
Mod NG
CLK_N
(channels 0 - 56 are good)
good channel bank
0
1
2
.
.
.
54
55
56
‘bad’ channel
‘good’ channel
Quality?

## Slide 20: Example mapping of Mode L
Regular Bluetooth hopping sequence
Example of proposed 802.15.1 AFH sequence
20
60
53
62
55
66
6
64
8
68
57
70
59
74
10
72
12
76
23
60
53
62
55
66
24
64
25
68
57
70
59
74
26
72
27
76
Regular Bluetooth hopping sequence used when master addresses normal Bluetooth devices.
AFH used when master addresses proposed 802.15.1 Mode L devices.

## Slide 21
Conclusion
Merges ideas of proposals:
  An integrated AFH to handle different scenarios.
    Easy to implement as a module.
    Voice without loss even under 802.11b interference
    backward compatible to legacy devices
  Under current high power FCC regulations (Mode H)
    01/246R1 as the baseline
  Under current low power FCC constraints (Mode L)
    00/367R1 as the baseline
  Allows for FCC changes in the future as parameter changes in this mechanism.

## Slide 22
Reference documents:
  00367r1P802-15_TG2-Adaptive-Frequency-Hopping.ppt
  01057r1P802-15_TG2-Selective-Hopping-for-Hit-Avoidance.ppt
  01169r0P802-15_TG2-Adaptive-Hopping-for-FHSS-Systems.ppt
  01082r1P802-15_TG2-Intelligent-Frequency-Hopping.ppt
  01246r1P802-15_TG2-Merged IPC and TI Adaptive Frequency Hopping Proposal.ppt

## Slide 23
Summary of the Coexistence Mechanism
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 24
1. Collaborative or Non-collaborative
  Non-collaborative
2. Improved WLAN and WPAN performance
  Significant performance improvement for both WLAN and WPAN
3. Impact on Standard
  No changes or extensions to IEEE 802.11 standard.
  Few extensions to IEEE 802.15.1 Specifications to implement the mechanism
4. Regulatory Impact
  Legal for all classes and scalable depending on regulatory rulings
5. Complexity
  Low complexity

## Slide 25
6. Interoperability with systems that do not include the coexistence mechanism
  Fully interoperable, broadcast packets supported to some degree
7. Impact on interface to Higher layers
  No impact on 802.11 interface to higher layers
  No impact on Bluetooth interface to higher layers.
8. Applicability to Class of Operation
  Supports all the Bluetooth profiles
9. Voice and Data support in Bluetooth
  Supports both ACL (data) and SCO (voice) packets.
10. Impact on Power Management
  No impact, beneficial to power management