## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Media Access Control proposal for the 802.15.4 Low Rate WPAN Standard]
Date Submitted: [May 2001]
Source: [Phil Jamieson] Company: [Philips Semiconductors]
Address: [Cross Lake Lane, , Redhill, Surrey RH1 5HA, United Kingdom]
Voice:[+44 1293 815 265], FAX: [+44 1293 815 050], E-Mail:[phil.jamieson@philips.com]
Re: [ MAC layer proposal submission, in response of the Call for Proposals ]
Abstract: [This contribution is a highly flexible MAC proposal for a Low Rate WPAN intended to be compliant with the P802.15.4 PAR. It is intended to support both master-slave and virtual peer-to-peer communications for low data rate networks. It is designed to support ultra low power consumption for battery operated nodes at very low implementation cost. The network is capable of supporting 254 nodes and one master with 7 co-located networks operating at the same time. The number of devices in the network can be increased by using IEEE addresses.]
Purpose: [Response to IEEE 802.15.4 TG Call for Proposals]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Target Markets
Low Data Rate Radio Devices

TV

VCR

DVD

CD

Remote

Mouse

Keyboard

Joystick

Gamepad

Security

HVAC

Lighting

Closures

PETs

Gameboys

Educational

Monitors

Diagnostics

Sensors
Industrial & Commercial
Consumer Electronics
Personal Healthcare

Monitors

Sensors

Automation

Control
Toys & Games
Home Automation
PC Peripherals

## Slide 3: TG4 Drivers
Extremely low cost
Ease of installation
Reliable data transfer
Short range operation
Reasonable battery life
Simple but flexible protocol

## Slide 4: Protocol Overview
Topology Master/slave
Channel access CSMA/TDMA
Raw data rates 28kbps & 250kbps
Data throughput >10kbps & >100kbps
Basic capacity 254 nodes
Co-located networks 7

## Slide 5: Node Architecture
PURL On-air Protocol Stack
PURL PHY
RF
PURL API
PURL MAC
PURL DLC
PURL NWK

## Slide 6: Network Topology
Virtual links
Master node
Slave node
Communications flow
IEEE slave node

## Slide 7: Other Network Forms
Master node
Communications flow
Ad-hoc network
Gateway
Slave node
Gateway enabled network

## Slide 8: The Master Device
Transmits network beacons
Sets up a network
Manages slave devices
Stores slave device information
Routes messages between paired slaves
Receives constantly

## Slide 9: The Slave Device
Is generally battery powered
Searches for available networks
Transfers data from its application as necessary
Determines whether data is pending
Requests data from the master
Can sleep for extended periods

## Slide 10: Slave Device Addressing
64-bit unique (IEEE) address
  hard-coded per device
Network address
  taken from the network beacon
8-bit short allocated address
  allocated on network connection

## Slide 11: Capacity
One master unit
Up to 254 allocated nodes
64-bit IEEE nodes (only memory limited)
4 low latency devices
7+ co-located networks

## Slide 12: Supported Traffic Types
Periodic data
  application defined rate
Intermittent
  basic communication
Repetitive low latency data
  allocation of time slots

## Slide 13: Time Frame (High Data Rate)
15ms
Network beacon
Contention period
Beacon extension period
Slot 3
Allocate slot of 5 chunks Contention period is 11 chunks
Slot 2
Allocate slot of 3 chunks Contention period is 16 chunks
Slot 1
Allocated slot
Allocate slot of 3 chunks Contention period is 19 chunks

## Slide 14: Data Transfers (High Data Rate)
Network
Beacon
Data
Packet
Data
Handshake
Uplink transfer:
Data
Request
Data
Packet
Data
Handshake
Network
Beacon
Downlink transfer:
From
Slave
From
Master
Message
Transfers

## Slide 15: Data Transfers (Low Data Rate)
Data
Packet
Data
Handshake
Uplink transfer:
From
Slave
From
Master
Message
Transfers
Data
Packet
Data
Handshake
Data
Handshake
Data
Packet
Downlink transfer:
Data
Request
Data
Packet
Data
Handshake

## Slide 16: Frame Structures
Preamble
Start of Frame Delimiter
Device
Address
Control
Payload
Network
Address
Frame
Length
Checksum
16 bits
8 bits
8 bits
8 bits
16 bits
8/64 bits
8n bits
8/16 bits
Preamble
Start of Frame Delimiter
Device
Address
Control
Payload
Network
Address
Frame
Length
Checksum
128 bits
63 bits
8 bits
8 bits
16 bits
8/64 bits
8n bits
8/16 bits
Low Data Rate Frame Structure:
High Data Rate Frame Structure:

## Slide 17: Connecting to a Network
Master
Slave
CONNECT
CONNECT
ACK
CONNECT-CONF
ACK
BEACON
PERMIT-CONNECTION
CONNECT-CONF
NEW-DEVICE

## Slide 18: Registration/Authentication
Master
Slave
DATA-REQ
GET-DESC
ACK
GET-DESC
BEACON
GET-DESC
NEW-DEVICE
DESC-DATA
ACK
DATA
DESC-DATA
RESET
RESET
RESET

## Slide 19: Reliability
Authentication
  All data transfers must use the network address
Packet reliability
  Transfers are fully handshaked
Master stability
  Master capable nodes can act as backup masters
  Periodic health check for the master
  Devices can enter extended beacon search

## Slide 20: Slave Power Management
Protocol is design for low power devices
All transfers are slave initiated
Sleep periods are application defined
Slave devices wake on
  external interrupt from some user stimulus
  application defined interval
  health check cycle

## Slide 21: Pairing Links
Slaves do not store network information
  “phone book” requires storage space
  must be continuously updated
Slaves are able to request a connection
  intuitive user operation: 1st slave, 2nd slave
  master creates and manages link
Routing performed at the master device
Links can be broken in the same way

## Slide 22: MAC System Requirements
8-bit C, e.g. 80c51
Full protocol stack <32k
Slave only stack ~4k
Masters require extra RAM
  device database
  pairing table

## Slide 23: MAC Evaluation Matrix

## Slide 24: MAC Evaluation Matrix, cont….