## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [MAC proposal for the Low Rate 802.15.4 Standard]
Date Submitted: [7 May, 2001]
Source: [Ed Callaway] Company: [Motorola]
Address: [8000 W. Sunrise Blvd., M/S 2141, Plantation, FL 33322]
Voice:[(954) 723-8341], FAX: [(954) 723-3712], E-Mail:[ed.callaway@motorola.com]
Re: [WPAN-802.15.4 Call for Proposals; Doc. IEEE 802.15-01/135r1 , 01/188r0, 01/189r0]
Abstract: [This presentation represents Motorola’s proposal for the P802.15.4 MAC standard, emphasizing the need for a low cost system having excellent battery life.]
Purpose: [Response to WPAN-802.15.4 Call for Proposals]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: MAC Proposal for the Low Rate 802.15.4 Standard
Ed Callaway, Member of the Technical Staff
Motorola Labs
Phone: +1-954-723-8341
Fax: +1-954-723-3712
ed.callaway@motorola.com

## Slide 3: Mediation Device Concept Review
Node duty cycle is reduced to 0.1% to lower power consumption.
For an asynchronous system, how will two nodes communicate under this low duty cycle condition?
Mediation Devices (MDs), which can record and replay messages, are dispersed throughout the network to enable nodes to synchronize.
MD services may be dedicated (one device serves as MD) or distributed (every device serves as MD at some random time).
Combined with the ALOHA protocol, collisions are unlikely because of the short (1 ms) transmission times.
Refer to doc 01/188r1 “Mediation Device Operation” for detailed information.

## Slide 4
A
B
MD
When node B checks in with the MD, it finds out that A has a message, and when A will try to contact again.
Node B now knows A’s schedule, so they can now sync on the same time slot and start communication.
MD
Node A
Node B
MD Listen
1 s
Query
Ack
Replay
MD – A Simple Example
Node A sends an “I have traffic for node B” message, but B is sleeping. The MD intercepts node A’s message, including timing information.
1 ms
Comm
Req
Comm
Req
Query
Query
Ready
Data
Ack

## Slide 5: Cluster Tree Network Review
Network grows via inquiry/inquiry scan technique, similar to 15.1 (join / unjoin simplicity).
Each device is assigned a network address composed of the Designated Device ID, Cluster ID, and Node ID (total of 24 bits).
DD
1
0
2
3
4
6
7
8
12
10
11
9
13
14
20
22
5
CH1
Cluster ID = 1
1
2
3
4
5
6
7
Cluster ID = 0
9
Designated device assigns Cluster IDs; cluster heads assign Node IDs.
Refer to doc 01/189r0 “Cluster Tree Network” for detailed information.
A “Designated Device” (Gateway) initiates network formation by choosing Cluster Head 0 (may be separate from DD for reliability).
Mesh Topology

## Slide 6: Matrix Criteria
Transparent to upper layers
Ease of Use
  48-bit address storage available
  Join/ unjoin simplicity (with little or no user intervention required) using cluster tree network method
  Device registration handled at upper layers
Data Throughput (single cluster) from MAC to higher layer in 1s – from <<1 to 30 1-Byte messages / minute
Traffic types
  MD handles periodic, intermittent traffic
Topology
  Ad hoc network in a mesh configuration
  Each network has 255 clusters max; each cluster has 255 devices max
  Gateway access through the DD

## Slide 7: Matrix Criteria (con’t)
Reliability
  Cluster Head 0 can replace the DD (master redundancy)
Power management
  Duty cycle is 0.1% using MD method
Power consumption of MAC controller
  Tx, Rx: 1 mW
  Sleep: 10 uW
Security
  Authentication can be factory encoded for large orders
  Encryption is handled in upper layers
Location awareness
  implemented in upper layers, but MAC must support (include data in message field)

## Slide 8: Network Simulation
Dedicated Device
Generations 1 and 4
Generations 2 and 5
Generation 3
-63 nodes
-Lines signify parent-child relationship
(not communication links)
-area 80 x 80 meters, with DD at center
-range of individual devices is 10 meters

## Slide 9: Network Simulation
(63 nodes; range of each node 10 meters)

## Slide 10: Protocol Extension
Mesh topology is needed to support inventory management, industrial control and monitoring
For consumer applications, this design can be extended to become a star configuration: NID = even  cluster tree network; NID = odd  star network (for example)
We can adopt the type of superframe used by the 15.3 MAC, which provides Guaranteed Time Slots (GTS) for isochronous data (doc. IEEE 802.15-01/119r1)
GTS provides “guaranteed bandwidth with bounded latency and latency variation”
Also, devices only need to be awake for a fraction of the superframe (low power solution)

## Slide 11: General Solution Criteria
Criteria | Ref | Value
Unit Manufacturing Cost ($) | 2.1 | $2 for 10M units
Interference and Susceptibility | 2.2.2 | 30-2350 and 2.530-13 GHz, -50 dBm; Adj. Channel (10 MHz), 2400-2483 MHz, -45 dBm
Intermodulation Resistance | 2.2.3 | -20 dBm IIP3
Jamming Resistance | 2.2.4 | Can tolerate – +20 dBm 802.11b 10m away 0 dBm 802.15.1 1m away Microwave ovens in quiet half-cycle
Multiple Access | 2.2.5 | 
Coexistence | 2.2.6 | Low duty cycle systems, interference should be low

## Slide 12: General Solution Criteria
Criteria | Ref | Value
Interoperability | 2.3 | True
Manufacturability | 2.4.1 | Single chip solution in development
Time to Market | 2.4.2 | Samples available Q1 2002
Regulatory Impact | 2.4.3 | True
Maturity of Solution | 2.4.4 | MD demo and network simulations available SPW and Matlab simulations of CPM
Scalability | 2.5 | 4 of 5 areas listed + network size
Location Awareness | 2.6 | True

## Slide 13: MAC Protocol Criteria
Criteria | Ref | Value
Transparent to Upper Layer Protocols (TCP/IP) | 3.1 | True
Unique 48-bit Address | 3.2.1 | True
Simple Network Join / Unjoin Procedures for RF enabled devices | 3.2.2 | Self-organizing request-grant-ack for network association; no user intervention required
Device Registration | 3.2.3 | Handled at upper layers
Delivered data throughput | 3.3.2 | <<1 to 30 1-Byte messages / minute
Traffic Types | 3.4 | MD handles periodic, intermittent
Topology | 3.5.1 | Mesh; parent-child, peer-to-peer

## Slide 14: MAC Protocol Criteria
Criteria | Ref | Value
Max. # of devices | 3.5.2 | 254 clusters; 254 nodes in each cluster
Ad-Hoc Network | 3.5.3 | True
Access to a Gateway | 3.5.4 | True
Master Redundancy | 3.6.2 | True
Loss of Connection | 3.6.3 | True
Power Management Types | 3.7 | MD method using sleep mode (power reduced from 10mW to 20uW)
Power Consumption of MAC controller | 3.8 | Tx, Rx: 1 mW Sleep: 10 uW
Authentication | 3.9.1 | Can be factory encoded
Privacy | 3.9.2 | Handled in upper layers