## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Nokia PHY submission to Task Group 4]
Date Submitted: [07 May, 2001]
Source: [Jukka Reunamäki] Company [Nokia]
Address [Visiokatu 1, P.O.Box 100, FIN-33721 Tampere, Finland]
Voice:[+358 7180 35331], FAX: [+358 7180 35935], E-Mail:[jukka.reunamaki@nokia.com]
Re: [Original document]
Abstract: [Submission to Task Group 4 for consideration as the Low Rate PHY for 802.15.4]
Purpose: [IEEE 802.15.4 PHY proposal for evaluation]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Nokia PHYsical layer submission to IEEE 802.15 Task Group 4
Presented by
Jukka Reunamäki
Nokia

## Slide 3: Contents
Cost and power consumption requirements
Operation frequency band and channel structure
Bit rate, modulation and performance
Link budget
Susceptibility to interference
Implementation examples
Conclusions
Self-evaluation against criteria

## Slide 4: General PHY requirements
Minimized RF and BB complexity
Very low cost
Strongly minimized power consumption
Relaxed performance requirements
Unlicensed operation frequency band
FCC and ETSI compliance
Mature, low risk approach

## Slide 5: Cost requirements
Target applications necessitate sub-dollar solutions
  Addition of WPAN capability should not increase total cost of the solution notably
Minimized number of components
  Single-chip or dual-chip implementations
  Only few external components
Mature, bulk RF and/or digital IC processes to be used
Cost optimum most probably differs from power consumption and size optima

## Slide 6: Power consumption and operation time
Idle time power consumption assumed to be 1/1000 of power consumption in active mode.

## Slide 7: Implications of power consumption requirements
Transceiver should consume about 10-25 times less power than current Bluetooth approaches to be feasible for button batteries
  It is possible with very low duty cycles (<< 1%)
  In active mode the whole transceiver including digital processing should consume only ~4 mW with small button cell and ~12 mW with large button cell
  Idle time dominates power consumption in case of low duty cycles
  Synthesizer is also critical

## Slide 8: Spread spectrum vs. narrowband
Basically, SS does not provide any benefit against interference in the 2.4 GHz ISM band
  Though, SS enables higher TX powers and faster synchronization
Narrowband system is more seldom hit by Bluetooth transmission
  Narrower signal bandwidths signify lower sampling rates and smaller power consumption
  More non-overlapping channels in the system band
  Less complex baseband

## Slide 9: Operation frequency band
Default is 2.45 GHz ISM band
  Unlicensed, global and congested
  Quite high frequency from minimum implementation and propagation point of view
  Operation under FCC 15.249 (US) and ERC rec 70-03 SRD (Europe)
Optional bands: 902-928 MHz in US and 433.050 - 434.790 MHz in Europe
  Smaller propagation loss, potentially less interference
Any band wide enough and available for short-range devices can be used

## Slide 10: Channel structure in 2400-2483.5 MHz
83 channels, center frequencies at 2401 + k x 1 MHz, where k = 0...82
    Compatibility with Bluetooth
    Outermost channels benefitially located
2400
2401
2402
2403
2481
2482
2483
2480
Bluetooth channels
Channels of the
proposed system
IEEE 802.11b channel
in North America and Europe
IEEE 802.11b channel
in Europe

## Slide 11: Device classes for different applications
Smaller TX power => smaller operating space and power consumption
Fixed frequency => potentially simpler implementation
Generally, sensitivity is not the dominant item from power consumption point of view if the requirements are reasonable (i.e. NF  15)
Communication between different classes is possible

## Slide 12: Bit rate and modulation
Maximum physical layer bit rate 200 kbps
    Data rate scalability achieved with lower activity, shorter packets and possible repetition coding
    Long symbol duration results in small ISI in indoor channels
    200 kbps aggregate capacity considered adequate from application point of view
2GFSK modulation with modulation index h = 2...3 and BT = 0.5
    Constant envelope for low power TX architecture
    Spectrum efficiency sacrificed for minimum complexity and low power RX implementation
    Relaxed requirements for phase noise, I/Q imperfections and frequency drift

## Slide 13: Modulation spectrum
2GFSK modulation with modulation index h = 2.5, BT = 0.5

## Slide 14: Transmit spectrum with different modulation indexes

## Slide 15: Performance in AWGN channel
C/NBER = 1e-3 = 13 dB
C/NBER = 1e-3 = 13.5 dB
2GFSK, modulation index h = 2.5, BT = 0.5,
f-3 dB, highpass = 50 kHz, f-3 dB, lowpass = 300 kHz
C/NBER = 1e-4 = 15.0 dB
C/NBER = 1e-4 = 14.5 dB

## Slide 16: Performance in multipath channel: ISI
The exponentially decaying fading channel model defined in criteria document:
  Assumes at least four samples per symbol
  Sufficient number of fading taps = 10*TRMS/Ts
For the 200 kbps data rate with 4 samples per symbol the channel is flat fading when the delay spread is smaller than 250 ns

## Slide 17: Performance in flat fading Rayleigh channel
X % signifies that raw BER is equal to or better than that indicated by the curves at a corresponding C/N value in X % of flat fading Rayleigh channels.

## Slide 18: Channel coding
By default no channel coding of any kind utilized
    Coding does not help much when the transmitted frame is overlapped by high power interference in both frequency and time
    Increases baseband complexity
    No need to extend range by means of coding
    Real-time services are not in focus
Data reliability ensured by 32-bit CRC checks (providing error detection up to BER  1e-9) and upper layer retransmissions
If needed, repetition coding can be used

## Slide 19: Link budget at 2.45 GHz
Fading margin of 13 dB ensures that C/N = 14.5 dB or better in > 95% of
the channels at range of 25/10/3/1 m.

## Slide 20: Example: link budget of unbalanced link with directive antenna
A link formed between devices with different capabilities e.g. based on power supply constraints

## Slide 21: Scalability
Range
  More range can be achieved by means of higher TX power (only -10 dBm proposed)
  FCC 15.249 addresses average power!
    Low duty cycles => high TX powers possible
Data rate
  Scalability implemented through packet sizing and duty cycles
Frequency band of operation
  Narrow transmit bandwidth basically allows usage of a number of different frequency bands, e.g. 433 MHz (Europe), 868 MHz (Europe), 915 (US), 2.4 GHz (global)

## Slide 22: Susceptibility to interference
2.45 GHz ISM band will be congested
Low power system cannot compete with TX power
Relaxation in interference susceptibility accepted to alleviate RX linearity requirements
    RX linearity requirements similar to Bluetooth (IIP3 = -15...-20 dBm) would not result in low-power RX, since RX linearity directly affects power consumption
    In case of co-channel interference, strong adjacent channel interference, blocking or intermodulation, packets are retransmitted

## Slide 23: Co-channel and adjacent channel interference

## Slide 24: CW interference
Note: CW interferer @ 0 Hz offset does not deteriorate performance due to highpass filtering in zero-IF RX!

## Slide 25: Intermodulation resistance
Values
  IIP3 = -30 dBm
  C/IBER = 1e-4, sensitivity + 3 dB = 10 dB
PCW interferer = -51 dBm
IMD
C/I

## Slide 26: Intermodulation resistance – a strong function of IIP3
IMD
C/N
RX
TX
Bluetooth TX
Bluetooth TX

## Slide 27: RX IIP3 vs. relative supply current

## Slide 28: Bluetooth interference

## Slide 29: 802.11 DS WLAN interference

## Slide 30: Blocking when RX IIP3  -30 dBm
How far away should a simultaneous transmission occur not to block the receiver?
Assumption: P1dB  IIP3 - 10 dB
RX (IIP3 
-30 dBm)
Bluetooth TX
transmitting
at 0 dBm
TX
IEEE 802.11b
WLAN TX
transmitting
at 20 dBm
Another TX of the
proposed system
transmitting
at -10 dBm
0 m
0.3 m
1 m
10 m

## Slide 31: Frame structure and signal acquisition
Preamble should be long enough to assist frequency and symbol synchronization
  Preferably zero DC
Sync word indicates the start of the header
  3 consecutive Barker codes of length 7
Header and payload left to be defined in the MAC layer
Preamble
32 bits
Header + payload + strong CRC's etc.
(defined by MAC layer)
Sync
word
21 bits

## Slide 32: TX implementation example
UP-
CONVERSION
+
POWER
AMPLIFIER
CHANNEL
FILTER
DAC
LOWPASS
FILTER
DAC
90º
0º
LO

## Slide 33: RX implementation example

## Slide 34: Effect of finite I/Q image rejection

## Slide 35: Power consumption estimates
RX analog/digital parts (active peak) 9.5 mW / 2.0 mW
  Assuming NF = 15 dB, IIP3 = -30 dBm
TX analog/digital parts (active peak) 10.5 mW / 1.5 mW
  Assuming Pout = -20 dBm
Total idle time power consumption (analog & digital) 22 W
Average consumption (based on 0.34% duty cycle) 60 W

## Slide 36: Size and cost estimates
Total IC area ~ 6 mm2
Package size (W x L x H) 6 x 6 x 1 mm3
IC cost ~ $1
External component count (SMD passives) 5...10 pcs
Size of SMD passives 0.5 x 1.0 x 0.5 mm3/pc
Module size (without antenna) 1 cm2 with components on both sides of PWB

## Slide 37: Conclusions
Nokia IEEE 802.15.4 physical layer proposal comprising
  Primarily operates in the 2.45 GHz ISM band, 1 MHz channel separation
  200 kbps maximum data rate, scalability achieved by means of packet sizing
  Operation range from 1 to 10 meters
  2GFSK modulation with large modulation index
Spectrum efficiency, link performance and interference tolerance sacrificed for minimum power, minimum complexity PHY implementation

## Slide 38: Self-evaluation against IEEE 802.15.4 criteria document (revision 4)

## Slide 39: General solution criteria 1/3

## Slide 40: General solution criteria 2/3

## Slide 41: General solution criteria 3/3

## Slide 42: PHY Protocol Criteria