## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Adaptive Frequency Hopping Ad-hoc group update
Date Submitted: 16th, May, 2001
Source: Hongbing Gan, Bijan Treister, et al. Company: Bandspeed Inc.
Address: 7000 West William Cannon Drive, Austin, TX78735
Voice: 512 358 9000, FAX: 512 358 9001, E-Mail: {b.treister, h.gan}@bandspeed.com.au
Re: Submission of a coexistence mechanism, revisions of the document 802.15-00/367r0
Abstract: An Adaptive Frequency hopping framework for a combined submissions
Purpose: To give an update of the AFH ad-hoc group discussions
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: AFH ad-hoc group summary
  Channel Classification
  Reliable exchange of classification data
  Mechanism of Adaptive Hopping

## Slide 3
Constraints:
Throughput improvement without compromise of any party or service in the piconet
All devices must know how to re-order/re-map/change the sequence in the same way;
Uniform usage of ‘good’ channels;
Legacy devices will inter-operate with enhanced ones in the same piconet;
All devices maintain clock synchronisation with Master;
Minimise changes/additions to existing standard;
Minimise complexity of this mechanism;

## Slide 4: Channel Classification
Assessment of good/bad channels
  Using some type of measure
    Packet loss ratio (PLR) for each channel;
    Background Received signal strength indicator (RSSI);
    Etc.
  Classification procedure (PLR measure an example)
    Measurements done on packets received;
    Slaves can do classification as well;
    If PLR is over a threshold, declare a ‘bad’ channel;
    If PLR is under threshold, declare a ‘good’ channel;

## Slide 5: Speed of Channel Classification
Strive to classify each of the 79 channels
  This way, more interferers can be detected
  No unnecessary loss of useful channels
Speed of classification may be reduced by:
  Classification of N MHz wide channels;
  A ‘guilt by association’ system;
  Larger bandwidths interferers detected faster if required;

## Slide 6: Mechanism of Adaptive Hopping
  Replacement of bad channels under legacy hopping sequence
    Replace bad channels
    Still use legacy hopping sequence, replace bad channels with good ones
  Pairing/grouping of ‘bad’/’good’ channels
    No transmission in bad channels
    Re-shuffle current sequence
  Reduction of hopping sequence length
    Reduce length of sequence to avoid BT-BT interference

## Slide 7: Re-cap on replacement algorithm
channel 27
Bluetooth
Selection
Kernel
0
0
.
.
0
1
2
3
.
26
.
25
24
28
27
.
.
1
1
1
1
1
.
.
25
24
23
27
26
.
.
Original Hopping Channels
0
0
Adaptive Hopping
Mapping Sequence
Clear Channel Bank
channel 3
channel 1
channel 24
channel 27
bad channel, redirect
bad channel, redirect

## Slide 8
Legacy Bluetooth hopping sequence
Enhanced AFH sequence, only bad channels are replaced under legacy hopping sequence
20
60
53
62
55
66
6
64
8
68
57
70
59
74
10
72
12
76
23
60
53
62
55
66
24
64
25
68
57
70
59
74
26
72
27
76
With enhanced AFH sequence, both enhanced and legacy devices are supported seamlessly

## Slide 9: Re-cap on replacement algorithm
Backward compatible with legacy devices
Better support for broadcast packets
Throughput improvement without sacrificing any party or service in the piconet
Low Complexity
Clock synchronization of all devices in the piconet, which is essential
Applicable regardless of links in piconet

## Slide 10: Useful properties of proposals
Pairing/Grouping of ‘bad’ and ‘good’ channels
  Adheres to current FCC laws for high power devices
  Increases throughput for piconets which MUST use bad channels
  Good solution when ‘bad’ channels must be use;
Replacement of bad channels under legacy hopping sequence
  Legal for low power devices
  Not link dependant, generalised for all implementations
  Trivial complexity
  No compromise of any party or service in the piconet
  More frequent synchronisation of piconet

## Slide 11: Useful properties of proposals
Examples of implementation
  High power devices benefit most from pairing/grouping;
    High power devices (currently) must use at least 75 channels
  Low power devices benefit most from bad channel replacement;
    No restriction on number of channels used for low power;

## Slide 12: Limitations of proposals
Pairing/Grouping of ‘bad’ and ‘good’ channels
  Higher complexity
  Configurations for different scenarios;
  Non optimal for scenarios where channels may be discarded
Replacement of bad channels under legacy hopping sequence
  Non optimal for scenario where bad channels MUST be used

## Slide 13: Reliable exchange of classification data
Exchange of classification data after classification
All adhering slaves must have correct sequence
Exchange may occur at LMP level;
Regular return to original hopping sequence to allow for errors or reclassification;

## Slide 14: Conclusion
Good properties of all proposals can be integrated in final proposal;
Different implementation may require different solutions;
Framework of AFH has been agreed upon