## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Data Whitening in Base-band to Reduce PSD of UWB Signals]
Date Submitted: [9 May, 2003]
Source: [Shaomin Mo] Company [Panasonic -- PINTL]
Address [Two Research Way, Princeton, New Jersey, USA]
Voice:[609-734-7592], FAX: [609-987-8827], E-Mail:[smo@research.panasonic.com]
Re: [IEEE P802.15 Alternative PHY Call For Proposals, IEEE P802.15-02/372r8]
Abstract: [Base-band processing of whitening data to reduce power spectral density of UWB signals in IEEE 802.15.3 systems ]
Purpose: [Proposal of base-band processing of whitening data to reduce power spectral density of UWB signals in IEEE 802.15.3 systems.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Data Whitening in Base-band to Reduce PSD of UWB Signals
Presented by Shaomin Mo
Panasonic Information and Networking Technologies Laboratories

## Slide 3: Summary
Power Spectra Density (PSD) is an important issue in UWB
PSD suppression leads to
  Improved frequency efficiency
  Prevention of interference to existing systems
  Potential increase in rate, Tx power (distance)
The proposal contributes to aspect of PSD suppression
  Phase reversion
  Linear Feedback Shift Register

## Slide 4: Outline
Power Spectra Density (PSD) issue in UWB
Analysis of PSD of UWB signals
Mechanisms to reduce PSD
  Phase reversion in base-band to reduce PSD
  Using Linear Feedback Shift Register for pseudo randomization
  Phase reversion for SYNC
Conclusion

## Slide 5: PSD is an Important Issue in UWB Communication Systems
FCC limited authorization of UWB technology, Feb 14, 2002
  Use in restrict spectrum at restrict power
  Do not interfere with other wireless systems
Other agencies still have some reservations about whether UWB will interfere with other wireless systems such as cellular, air navigation and landing systems

## Slide 6: Containing PSD is an Important Part in UWB System Design
Repeat pulse trains may generate strong line spectra and high PSD
Traditional scramblers are not sufficient to contain PSD
PSD suppression leads to
  Improved frequency efficiency
  Prevention of interference to existing systems
  Potential increase in rate, Tx power (distance)

## Slide 7: Analysis of PSD of UWB Signals

## Slide 8: Model of Repeat Pulse Train
Signal model
Probability function of an

## Slide 9: PSD of Repeat Pulse Train
PSD of repeat pulse trains consists of
Sc(f) – continuous component
Sd(f) – discrete component
W(f)
Tc
p

## Slide 10: PSD with Different p Has Same Envelop but Different Level
PSD of single pulse
P = 0.25
P = 0.5
P = 1.0
Line spectra
peak = 15
peak = 9
peak = 3

## Slide 11: Objective of Design
Contain PSD
Reduce or eliminate discrete component of PSD  reduce PSD across whole spectrum
Make

## Slide 12: Conventional Narrowband TDMA Systems
Conventional narrowband communication systems make randomness inside a frame for timing recovery, equalization, etc.
Line spectra may not occur due to continuous nature of waveforms

## Slide 13: New Requirements to UWB Communication Systems
Repeat pulse train in finite length frame produces line spectra in UWB system
  Insufficient randomness for PSD in UWB
Further data whitening is required for UWB system

## Slide 14: How to Make Further Randomness Using Simple Circuit ?
0
100
200
300
400
-1
-0.5
0
0.5
1
(b): Waveform of data
7 pulses in each frame
In case of fully randomized frames
Repeated frames
Original stream: line spectra & peak = 17
Our motivation

## Slide 15: Propose 1 : Phase Reversion

## Slide 16: Phase Reversion Operation
A random sequence {bn} is generated with
cn = an ^ bn. It can be proved that
{cn} is used as the new data for transmission.

## Slide 17: Phase Reversion on Frames
Phase reversion on whole frames
Randomized reversion pattern eliminates lines in PSD
“reversion”
“reversion”
“no reversion”
Randomized reversion pattern

## Slide 18
Phase Reversion on Symbols
Phase reversion on symbols
Randomized reversion pattern eliminates lines in PSD
“reversion”
“reversion”
“no reversion”
Randomized reversion pattern
Pulses on this line form a repeat pulse train
“reversion”

## Slide 19: Using proposed scheme on frames, lines are eliminated and PSD is slightly reduced
Waveform of single pulse
PS of single pulse
PSD of original data (7 pulses/frame)
PSD of result data
Line spectra gone peak = 16
Line spectra & peak = 19

## Slide 20: Using proposed scheme on symbols, lines are eliminated and PSD is reduced
Waveform of single pulse
PS of single pulse
PSD of original data (7 pulses/frame)
PSD of result data
Line spectra gone peak reduced to 9
Line spectra & peak = 20

## Slide 21: Frame-based vs. Symbol-based Phase Reversion
Frame-based
  Final PSD depends on both pulse and data in frames
Symbol-based
  Final PSD depends only on used pulse
  Final PSD is independent from data in frames

## Slide 22: Data Whitening using Phase Reversion
Base-band coding technique
  Independent of pulse shape
  Applicable to PAM, PPM, BPSK, QPSK, Time-Hopping
  Applicable to Multi-band
  Easy to implement in CMOS architecture
    Simple digital circuit such as LFSR
Extendable for SYNC words

## Slide 23: Propose 1-1 : Phase Reversion for Multi-band

## Slide 24: Model of Repeat Pulse Train of Multi-band
Signal model

## Slide 25: Model of Repeat Pulse Train (cont.)
{wm} is a set of waveforms on sub-bands
Probability function of an, same on all sub-bands

## Slide 26: PSD of Repeat Pulse Train
PSD of repeat pulse trains consists of
Sc(f) – continuous component
Sd(f) – discrete component
W(f)
Tc
p
pn

## Slide 27: Parameters that Determine PSD
W(f) – pulse shape & Tx power
Tc – clock period or pulse rate
pm – probability in distribution function of sub-bands
p – probability in distribution function of waveforms
  Does not affect total PSD
  Changes distribution of PSD between continuous and discrete components

## Slide 28: Objective of Design
Contain PSD
Reduce or eliminate discrete component of PSD
Make
Contain PSD
Reduce or eliminate discrete component of PSD
Make

## Slide 29: To Make {wm} Evenly Distributed – Rotationally
w1
w4
w3
w2
w8
w7
w6
w5
Wm is waveform on sub-band m, 1  m  M

## Slide 30: To Make {wm} Evenly Distributed – Randomly
Another way to make {wm} evenly distributed is to randomly and evenly choose wm so that

## Slide 31: To Make {an} Evenly Distributed
A random sequence {bn} is generated with
cn = an ^ bn. It can be proved that
{cn} is used as the new data for transmission.

## Slide 32: PSD of BPSK with p=0.4 & Rotationally
Waveforms in multi-band
Original data, p = 0.4
PS of waveforms
Result data
peak = 4
Line spectra peak = 9

## Slide 33: PSD of BPSK with p=0.4 & Randomly
Waveforms in multi-band
Original data, p = 0.4
PS of waveforms
Result data
peak = 5
Line spectra peak = 10

## Slide 34: Propose 2 : Linear Feedback Shift Register

## Slide 35: Major Challenge in Implementing Phase Reversion
MATLAB was used in simulations as random numbers generators (RNG).
  Very good performance & can be used as ideal RNG.
  Too complicated for implementation.
Real implementation
  Simple way to generate random sequence
  Easy way to synchronize RNGs in both transmitters and receivers

## Slide 36: Using LFSR
LFSR stands for Linear Feedback Shift Registers
Easy implementation
Very suitable for semiconductor implementation

## Slide 37: LFSR – 1
LFSR is updated per symbol

## Slide 38: Synchronization of LFSR--1
State of LFSR is transmitted
Easy implementation
Fast initial access
Waste bandwidth after initial access

## Slide 39: LFSR – 2
LFSR is loaded with a RN per Frame & updated per symbol

## Slide 40: Synchronization of LFSR--2
Initial system channel access
  Random vectors are generated in advance & stored in an array
  Transmitters & receivers keep same array
  Index to a vector in the array is put in data to transmit
Initial traffic channel access
  Sequence number can be used

## Slide 41: 15-bit LFSR--2 vs. Ideal Low Bound
Phase reversion controlled by MATLAB RNG
Phase reversion controlled by proposed LFSR
10 runs 50 runs 200 runs
~2000 pulses/frame
  MATLAB is used as RNG & as reference of ideal low bound
LFSR is too short, strong line spectra exist

## Slide 42: 28-bit LFSR--2 vs. Ideal Low Bound
Phase reversion controlled by MATLAB RNG
Phase reversion controlled by proposed LFSR
10 runs 50 runs 200 runs
Same configuration as 15-bit LFSR
LFSR is long enough, line spectra is suppressed
Very close to the reference

## Slide 43: Proposal 3 : Phase Reversion on SYNC

## Slide 44: Phase Reversion on SYNC
Phase reversion on the whole SYNC
“reversion”
“reversion”
“no reversion”

## Slide 45: Phase Reversion on SYNC: eliminate lines but not ripples in PSD
One cycle of SYNC
PSD with phase reversion
PSD without phase reversion
Waveform of SYNC
Result: lines gone
Original: strong lines

## Slide 46: Self Evaluation
Item | Evaluation | Comments
Unit Manufacturing Complexity | + | Easy to implement
Interference & susceptibility | + | Reduced PSD
Manufacturability | + | Easy to implement
Time to market | + | Use proved technology
Regulatory impact | + | Reduced PSD

## Slide 47: Conclusion
Base-band data whitening proposal
Effective in reducing PSD of UWB signals
  Improved frequency efficiency
  Reduced interference to existing systems
  Potential increase in rate, Tx power (distance)
Allow cheap implementation
  All logical operations
  Very simple for semiconductor implementation

## Slide 48
Thank you

## Slide 49
Appendix

## Slide 50
Analysis of PSD of repeat pulse trains

## Slide 51: Model of Repeat Pulse Train
Signal model
Probability function of an

## Slide 52: PSD of Repeat Pulse Train
Ps is determined by w(t) and Tc
Ps is not affected by Pr{an}
Total PSD is determined by w(t) and Tc
Total PSD is not affected by Pr{an}

## Slide 53: PSD of Repeat Pulse Train
PSD of repeat pulse trains consists of
Sc(f) – continuous component
Sd(f) – discrete component
W(f)
Tc
p

## Slide 54: Parameters that Determine PSD
W(f) – pulse shape & Tx power
Tc – clock period or pulse rate
p – probability in distribution function
  Does not affect total PSD
  Changes distribution of PSD between continuous and discrete components

## Slide 55: Simplified Form of PSD

## Slide 56: Relationship between Continuous and Discrete Components

## Slide 57: Relationship between Continuous and Discrete Components
Because total PSD is constant
A(f) = B(f)
Max(Sc(f)) = Max(Sd(f))

## Slide 58: Relationship between Continuous and Discrete Components
Total continuous PSD equals total discrete PSD
The continuous distributes on all frequencies
The discrete distributes on those discrete frequencies separated by 1/Tc.
Continuous PSD is lower than that of discrete PSD on the same frequency components

## Slide 59: Objective of Design
Contain PSD
Reduce or eliminate discrete component of PSD  reduce PSD across whole spectrum
Make

## Slide 60
Simulation results for multi-band BPSK & QPSK

## Slide 61: PSD of BPSK with p=1 & Rotationally
Waveforms in multi-band
Original data, p = 1
PS of waveforms
Result data
peak = 4
Line spectra peak = 21

## Slide 62: PSD of BPSK with p=0.25 & Rotationally
Waveforms in multi-band
Original data, p = 0.25
PS of waveforms
Result data
peak = 4
Line spectra peak = 17

## Slide 63: PSD of BPSK with p=0.4 & Rotationally
Waveforms in multi-band
Original data, p = 0.4
PS of waveforms
Result data
peak = 4
Line spectra peak = 9

## Slide 64: PSD of BPSK with p=1 & Randomly
Waveforms in multi-band
Original data, p = 1
PS of waveforms
Result data
peak = 5
Line spectra peak = 22

## Slide 65: PSD of BPSK with p=0.25 & Randomly
Waveforms in multi-band
Original data, p = 0.25
PS of waveforms
Result data
peak = 5
Line spectra peak = 15

## Slide 66: PSD of BPSK with p=0.4 & Randomly
Waveforms in multi-band
Original data, p = 0.4
PS of waveforms
Result data
peak = 5
Line spectra peak = 10

## Slide 67: PSD of QPSK with p=1 & Rotationally
Waveforms in multi-band
Original data, p = 1
PS of waveforms
Result data
peak = 4
Line spectra peak = 19

## Slide 68: PSD of QPSK with p=0.25 & Rotationally
Waveforms in multi-band
Original data, p = 0.25
PS of waveforms
Result data
peak = 4
Line spectra peak = 12

## Slide 69: PSD of QPSK with p=0.4 & Rotationally
Waveforms in multi-band
Original data, p = 0.4
PS of waveforms
Result data
Line spectra peak = 7
peak = 4

## Slide 70: PSD of QPSK with p=1 & Randomly
Waveforms in multi-band
Original data, p = 1
PS of waveforms
Result data
peak = 5
Line spectra peak = 18

## Slide 71: PSD of QPSK with p=0.25 & Randomly
Waveforms in multi-band
Original data, p = 0.25
PS of waveforms
Result data
peak = 4
Line spectra peak = 13

## Slide 72: PSD of QPSK with p=0.4 & Randomly
Waveforms in multi-band
Original data, p = 0.4
PS of waveforms
Result data
Line spectra peak = 7
peak = 5