## Slide 1
  [Proposed Draft] IMT-ADVANCED WORKSHOP PRESENTATION ON IEEE 802.16m
Document Number: IEEE C802.16-08/022
Date Submitted: 2008-09-16
Source: Sassan Ahmadi sassan.ahmadi@intel.com
Minnie Ho
  Intel Corporation
  Venue: IEEE Session #57 Kobe, Japan
Base Contribution: None
Purpose: To provide baseline material for IEEE 802.16m presentation in IMT-Advanced workshop in October 2008 to be prepared and approved by IEEE 802 Working Group 16
Notice:
  This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein.
Release:
  The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16.
Patent Policy:
  The contributor is familiar with the IEEE-SA Patent Policy and Procedures:
      <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>.
  Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat >.
Notes: <number>

## Slide 2: Outline
Overview of IEEE 802.16m Program
IEEE 802.16m Development Schedule
IEEE 802.16m System Requirements
IEEE 802.16m Evaluation Methodology
IEEE 802.16m Network Architecture and Reference Model
IEEE 802.16m Advanced Features
References

## Slide 3
Overview of IEEE 802.16m Program

## Slide 4: Overview of IEEE 802.16m Program
Since January 2007, the IEEE 802.16 Working Group has embarked on development of a new amendment of the IEEE 802.16 standard (i.e., IEEE 802.16m) in order to develop an advanced air-interface to meet the requirements of ITU-R/IMT-Advanced for 4G systems as well as the next generation mobile network operators.
The IEEE 802.16m air-interface utilizes OFDMA as the preferred multiple access method in the downlink and uplink.
Depending on the available bandwidth and antenna configuration, IEEE 802.16m will enable over-the-air data transfer rates in the excess of 1 Gbps and will support a wide range of high-quality and high-capacity IP-based services and applications while maintaining full backward compatibility with the existing mobile WiMAX systems to preserve investments and continuing support for first generation products.
The active participation of a great number of companies from several countries across the globe adds more credibility to IEEE 802.16 efforts to create a worldwide radio access technology to satisfy 4G system and service requirements.
The IEEE 802.16m will provide the state-of-the-art broadband wireless access in the next decade and can satisfy the growing demand for advanced wireless multimedia applications and services.
The standardization of IEEE 802.16m and release 2.0 of mobile WiMAX profile are expected to complete by the end of 2010.

## Slide 5
IEEE 802.16m Development Schedule

## Slide 6
Call for stage 2 details issued in Jul ’08
First Call for Proposals for 802.16m Stage 3 issued in Sept’08
Sep ’07*
Jan’08*
Nov 08*
Initial P.
Working Doc
Mar ’09
Letter Ballot
Sponsor Ballot
Sep ’09
Nov ’08
Nov ’07
Jan ’09
IEEE 802.16m
802.16m
Amendment
IMT
Advanced
Proposal
System
Description
System
Requirements
Evaluation
Methodology
ITU-R IMT Advanced
IMT.TECH
IMT.EVAL
IMT. RADIO
Jun ’08
Oct ’08
Proposal Submission
Jan’09
First Call for Proposals for SDD issued in Sept ‘07
Circular
Letter
Jun ’08
Proposal Evaluation & Consensus Building
Develop Recommendation
Q2
Q3
Q4
Q1
Q2
Q3
Q4
2007
2008
2009
Q1
Q2
Q3
Q4
Apr
May
Jun
Jul
Aug
Sep
Oct
Nov
Dec
Jan
Feb
Mar
Apr
May
Jun
Jul
Aug
Sep
Oct
Nov
Dec
Jan
Feb
Mar
Apr
May
Jun
Jul
Aug
Sep
Oct
Nov
Dec
Jan
Feb
Mar
Apr
May
Jun
Jul
Aug
Sep
Oct
Nov
Dec
Q1
Q2
Q3
Q4
2010
Oct ’09
Jun ’10
Final Proposal
Sept ’09*
*System Requirements and Evaluation Methodology, System Description, IMT-Advanced Proposal Documents may be further updated based on ITU output (shown by dotted lines). Ŧ 802.16m amendment is dependent on the 802.16Rev2 Project completion
ITU based Updates
Refinements
Apr
May
Jun
Jul
Aug
Sep
Oct
Nov
Dec
Jan
Feb
Mar
Apr
May
Jun
Jul
Aug
Sep
Oct
Nov
Dec
Jan
Feb
Mar
Apr
May
Jun
Jul
Aug
Sep
Oct
Nov
Dec
Jan
Feb
Mar
Apr
May
Jun
Jul
Aug
Sep
Oct
Nov
Dec
IEEE 802.16
ITU-R WP5D
Mar ’10
ITU based Updates
IEEE 802.16m standardization complete
Notes: <number>
<number>

## Slide 7
IEEE 802.16m System Requirements

## Slide 8: IEEE 802.16m System Requirements
Additional Requirements | IMT-Advanced | IEEE 802.16m
Peak data rate (b/s/Hz/sector) | DL: 15 (4x4) UL: 6.75 (2x4) | DL: 8.0/15.0 (2x2/4x4) UL: 2.8/6.75 (1x2/2x4)
Cell spectral efficiency (b/s/Hz/sector) | DL (4x2) = 2.2 UL (2x4) = 1.4 (Base coverage urban) | DL (2x2) = 2.6 UL (1x2) = 1.3 (Mixed Mobility)
Cell edge user spectral efficiency (b/s/Hz) | DL (4x2) = 0.06 UL (2x4) = 0.03 (Base coverage urban) | DL (2x2) = 0.09 UL (1x2) = 0.05 (Mixed Mobility)
Latency | C-plane: 100 ms (idle to active) U-plane: 10 ms | C-plane: 100 ms (idle to active) U-plane: 10 ms
Mobility b/s/Hz at km/h | 0.55 at 120 km/h 0.25 at 350 km/h | Optimal performance up to 10 km/h “Graceful degradation” up to 120 km/h “Connectivity” up to 350 km/h Up to 500 km/h depending on operating frequency
Handover interruption time (ms) | Intra frequency: 27.5 Inter frequency: 40 (in a band) 60 (between bands) | Intra frequency: 27.5 Inter frequency: 40 (in a band) 60 (between bands)
VoIP capacity (Active users/sector/MHz) | 40 (4x2 and 2x4) (Base coverage urban) | 30 (DL 2x2 and UL 1x2)
IEEE 802.16m functional and performance requirements are more
comprehensive and more stringent than IMT-Advanced requirements
Notes: <number>

## Slide 9: IEEE 802.16m System Requirements
Additional Requirements | IMT-Advanced | IEEE 802.16m
Antenna Configuration | Not specified | DL: 2x2 (baseline), 2x4, 4x2, 4x4, 8x8 UL: 1x2 (baseline), 1x4, 2x4, 4x4
Cell Range and Coverage | Not specified | Up to 100 km with optimal performance up to 5 km
Multicast and Broadcast Service (MBS) | Not specified | 4 bps/Hz for ISD 0.5 km and 2 bps/Hz for ISD 1.5 km
MBS channel reselection interruption time | Not specified | 1.0 s (intra-frequency) 1.5 s (inter-frequency)
Location based services (LBS) | Not specified | Location determination latency < 30 s MS-based position determination accuracy < 50 m Network-based position determination accuracy < 100 m
Operating bandwidth | Up to 40 MHz (with aggregation) | 5 to 20 MHz (up to 100 MHz through band aggregation)
Duplex scheme | Not specified | TDD, FDD (support for H-FDD terminals)
Operating frequencies | IMT bands | IMT bands (below 6 GHz)
IEEE 802.16m is suitable for a large set of usage models, applications, and services
Notes: <number>

## Slide 10
IEEE 802.16m Evaluation Methodology

## Slide 11: IEEE 802.16m Simulation Components
Evaluation Criteria
Modeling Requirements
Link Level Model
System Level Model
Propagation and Channel Model
Antenna Pattern
Traffic Model
Fairness Criterion
Performance Metrics
Simulation
Simulation Framework
Simulation Methodology
Simulation Procedure
Simulation Results and Evaluation Report
The objective of IEEE 802.16m evaluation methodology is to define link-level and system-level simulation models and associated parameters that shall be used in the evaluation and comparison of technology proposals for IEEE 802.16m. Proponents of any technology proposal using this methodology shall follow the evaluation methods defined in this document and report the results using the metrics defined in this document.

## Slide 12: IMT-Advanced Evaluation Scenarios
Deployment scenario for the evaluation process | Urban Macro-cell | Urban Micro-cell | Indoor Hotspot | Rural Macro-cell | Suburban macro-cell (optional)
Layout | Hexagonal grid | Hexagonal grid | Indoor floor | Hexagonal grid | Hexagonal grid
Inter-site distance | 500 m | 200 m | 60 m | 1732 m | 1299 m
Channel Model | Urban macro model | Urban micro model | Indoor hotspot model | Rural macro model | Suburban macro model
User distribution | Randomly and uniformly distributed over area. 100% of users outdoors in vehicles | Randomly and uniformly distributed over area. 50 % users outdoor (pedestrian users) and 50 % of users indoors | Randomly and uniformly distributed over area | Randomly and uniformly distributed over area. 100% of users outdoors in high speed vehicles | Randomly and uniformly distributed over area. 50 % users vehicles and 50 % of users indoors
Center Frequency | 2 GHz | 2.5 GHz | 3.4 GHz | 800 MHz | Same as urban macro
User speeds | 30 km/h | 3 km/h | 3 km/h | 120 km/h | Indoor User Terminals 3 km/h, outdoor: 90 km/h
Notes: <number>

## Slide 13: IEEE 802.16m Evaluation Scenarios
Scenario/ Parameters | Baseline Configuration (Calibration & D) TDD and FDD | NGMN Configuration TDD and FDD | Urban Macrocell TDD and FDD
Requirement | Mandatory | Optional * | Optional
Site-to-Site Distance | 1.5 km | 0.5 km | 1 km
Carrier Frequency | 2.5 GHz | 2.5 GHz | 2.5 GHz
Operating Bandwidth | 10 MHz for TDD / 10 MHz per UL and DL for FDD | 10 MHz for TDD / 10 MHz per UL and DL for FDD | 10 MHz for TDD / 10 MHz per UL and DL for FDD
BS Height | 32 m | 32 m | 32 m
BS Tx Power per sector | 46 dBm | 46 dBm | 46 dBm
MS Tx Power | 23 dBm | 23 dBm | 23 dBm
MS Height | 1.5 m | 1.5 m | 1.5 m
Penetration Loss | 10 dB | 20 dB | 10 dB
Path Loss Model | Loss (dB) = 130.19+37.6log10(R) (R in km) ** | Loss (dB) = 130.19+37.6log10(R) (R in km) ** | Refer to Section ‎3.2.3.1
Lognormal Shadowing Standard Deviation | 8 dB | 8 dB | 8 dB
Correlation Distance for Shadowing | 50m | 50m | 50m
Mobility | 0-120 km/hr | 0-120 km/hr | 0-120 km/hr
Channel Mix | ITU Ped B 3 km/hr – 60% Veh A 30 km/hr – 30% Veh A 120 km/hr – 10% (Refer to Section ‎3.2.9 ***) | Low Mobility: 3km/hr UL: Typical Urban, DL: SCM-C Mixed Mobility: ITU Ped B 3 km/hr – 60% Veh A 30 km/hr – 30% Veh A 120 km/hr – 10% (Refer to Section ‎3.2.9 ***) | 3 km/hr – 60% 30 km/hr – 30% 120 km/hr – 10%
Spatial Channel Model | with spatial correlation (Refer to Section ‎3.2.9 ***) | Low Mobility: 3km/hr SCM Mixed Mobility: ITU with spatial correlation (Refer to Section ‎3.2.9 ***) | Urban Macrocell CDL (Refer to Table 9 in Section ‎3.2.5.1) with spatial correlation (Appendix A)
Error Vector Magnitude (EVM) | 30 dB | N/A | 30 dB

## Slide 14: IEEE 802.16m Evaluation Scenarios
Scenario/ Parameters | Suburban Macrocell | Urban Microcell | Indoor Small Office | Indoor Hotspot | Outdoor to Indoor | Rural
Requirement | Optional | Optional | Optional | Optional | Optional | Optional
Site-to-Site distance | 1.5 km | 0.5 km | 50 m | 80 m | TBD | 10 km
Carrier Frequency | 2.5 GHz | 2.5 GHz | 2.5 GHz | 2.5 GHz | 2.5 GHz | 2.5 GHz
Operating Bandwidth | 10 MHz for TDD / 5 MHz per uplink and downlink for FDD | 10 MHz for TDD / 5 MHz per uplink and downlink for FDD | 10 MHz for TDD / 5 MHz per uplink and downlink for FDD | 10 MHz for TDD / 5 MHz per uplink and downlink for FDD | 10 MHz for TDD / 5 MHz per uplink and downlink for FDD | 10 MHz for TDD / 5 MHz per uplink and downlink for FDD
BS Height | 32 m | 12.5 m | 1-2.5m | 1~2.5m | TBD | 50 m
BS Tx Power | 46 dBm TDD 43 dBm FDD | 46 dBm TDD 43 dBm FDD | TBD | TBD | 46 dBm | 46 dBm
MS Tx Power | 23 dBm | 23 dBm | 23 dBm | 23 dBm | 23 dBm | 23 dBm
MS Height | 1.5 m | 1.5 m | 1.5m | 1.5m | 1.5m | 1.5m
Penetration Loss | 10 dB | 10 dB | 0 dB | TBD | 0 dB | 10 dB
Path Loss Model | Refer to Section 3.2.3.2 | Refer to Section 3.2.3.3 | Refer to Section 3.2.3.4 | Refer to Section 3.2.3.5 | Refer to Section 3.2.3.6 | Refer to Section 3.2.3.7
Lognormal Shadowing Standard Deviation | NLOS: 8 dB | NLOS: 4 dB LOS: 3 dB | NLOS (Room to corridor): 8 dB NLOS (Through light wall): 6 dB NLOS (Through heavy wall): 8 dB | LOS: TBD NLOS: TBD | 7 dB | LOS (near) 4dB LOS (far) 6 dB NLOS 8 dB
Correlation distance for shadowing | 50m | 50m | TBD | TBD | TBD | LOS 40 m NLOS 120 m
Mobility | 0-120 km/hr | TBD | TBD | 0-3 km/hr | TBD | 0-120 km/hr
Channel Mix | 3 km/hr-60% 30 km/hr -30% 120 km/hr-10% | Stationary 0 km/hr - 60%, 3 km/hr -20%, 30 km/hr- 20% | Stationary 0 km/hr - 80%, 3 km/hr -20% | Stationary 0 km/hr - 80%, 3 km/hr -20% | TBD | 3 km/hr-60% 30 km/hr -30% 120 km/hr-10%
Spatial Channel Model | Refer to Section 3.2.5.2* | Refer to Section 3.2.5.3* | Refer to Section 3.2.5.4* | Refer to Section 3.2.5.5* | Refer to Section 3.2.5.6* | Refer to Section 3.2.5.7*
* IEEE 802.16m Evaluation Methodology Document

## Slide 15: IMT-Advanced Service Requirements
User Experience Class | Service Class | Service Parameters (Numerical Values) | 
Conversational | Basic conversational service | Throughput: | 20 kbit/s
 |  | Delay: | 50 ms
 | Rich conversational service | Throughput: | 5 Mbit/s
 |  | Delay: | 20 ms
 | Conversational low delay | Throughput: | 150 kbit/s
 |  | Delay: | 10 ms
Streaming | Streaming Live | Throughput: | 2 – 50 Mbit/s
 |  | Delay: | 100 ms
 | Streaming Non-Live | Throughput: | 2 – 50 Mbit/s
 |  | Delay: | 1 s
Interactive | Interactive high delay | Throughput: | 500 kbit/s
 |  | Delay: | 200 ms
 | Interactive low delay | Throughput | 500 kbit/s
 |  | Delay | 20 ms
Background | Background | Throughput: | 5 – 50 Mbit/s
 |  | Delay: | < 2s
IEEE 802.16m functional and performance requirements guarantees
satisfaction of IMT-Advanced service requirements
Notes: <number>

## Slide 16
IEEE 802.16m Network Architecture and Reference Model

## Slide 17: Overall WiMAX Network Architecture
Access Service Network
R8
R6
R1
R2 (logical interface)
Access Service Network
Gateway
R6
802.16e
MS
BS
BS
R1’
802.16m
MS
Other Access Service Networks
R4
Connectivity
Service
Network
Connectivity
Service
Network
R3
R5
Access Service Provider Network
(Internet)
Access Service Provider Network
(Internet)
Home Network Service Provider
Visited Network Service Provider
Layer 1 and Layer 2 to be specified by IEEE 802.16m
Core Network

## Slide 18: IEEE 802.16m Reference Model
IEEE 802.16m
Data/Control Plane
IEEE 802.16f/g NetMAN
Management Plane
Physical Layer
(PHY)
PHY SAP
Security Sub-Layer
Medium Access
Control Functions
Radio Resource
Control
and
Management Functions
MAC SAP
Convergence
Sub-Layer
CS SAP
Security Sub-Layer
Management Layer
Common Part
Sub-Layer
Management Entity
Physical Layer
Management Entity
Service Specific
Convergence Sub-Layer
RAN
Control
and
Transport
Functions
WiMAX NWG
RAN
Architecture
External
Networks
MAC Common-Part Sub-Layer
Outside IEEE 802.16m Scope

## Slide 19
IEEE 802.16m Advanced Features

## Slide 20: Unified Single-User/Multi-User MIMO Architecture
User
1
data
User
2
data
User P
data
User i
data
MIMO
Encoder
Beam-former
/Precoder
IFFT
OFDM Symbol
Construction
IFFT
IFFT
Precoding Vector
/Matrix
Encoder
Encoder
Encoder
Encoder
Encoder
Encoder
Layer
control
Scheduler
Resource
Mapping
Feedback
CQI
CSI
ACK / NACK
Mode / Rank / Link Adaptation
IEEE 802.16m supports various advanced multi-antenna processing techniques including open-loop and closed single-user/multi-user MIMO schemes (single stream and multi-stream), a number of TX diversity techniques, and TxBF with rank/mode adaptation capability. Multi-cell MIMO techniques are also supported.
Notes: <number>

## Slide 21: IEEE 802.16m Air-Interface Protocol Stack
<number>
QoS
Convergence Sub-Layer
Physical Layer
PHY Protocol (FEC Coding, Signal Mapping, Modulation, MIMO processing, etc.)
Medium Access Control Functions
MAC PDU Formation
Radio Resource
Control &
Management
Functions
L2
L1
Idle Mode Management
Relay Functions
Mobility Management
Radio Resource Management
Network Entry
Management
Multi-Carrier Support
MBS
Data and Control Bearers
CS SAP
Multi-Radio Coexistence
Location Management
ARQ
Control and Signaling
Security Sub-Layer
MAC Common Part Sub-Layer
Physical Channels
Fragmentation/Packing
Ranging
Control Plane
Data Plane
Self-Organization
Security Management
System Configuration
Management
Link Adaptation
Interference
Management
PHY Control
Sleep Mode Management
Scheduling & Resource
Multiplexing
Classification
Header Compression
Connection Management

## Slide 22: Multi-Carrier Support
Data Plane
Control Plane
Radio Resource Control
& Management Functions
CS Sub-Layer
Medium Access Control Functions
PHY 1
RF Carrier 1
PHY 2
RF Carrier 2
PHY n
RF Carrier n
CS SAP
Data and Control Bearers
Physical Channels
Physical Channels
…
Physical Channels
L2
L1
MAC Common Part Sub-Layer
Security Sub-Layer
Dynamic/Static Mapping
Support of multi-carrier operation in IEEE 802.16m basic frame structure
Some MAC messages sent on one carrier may also apply to other carriers.
The RF carriers may be of different bandwidths and can be non-contiguous or belong to different frequency bands.
The channels may be of different duplexing modes, e.g. FDD, TDD, or a mix of bidirectional and broadcast only carriers.
Support of wider bandwidths (up to 100 MHz) through aggregation across contiguous or non-contiguous channels.
The RF carriers can be fully or partially configured.
A generalized protocol architecture for support multicarrier operation with single MAC entity

## Slide 23: Multi-Hop Relay-Enabled Architecture
More aggressive radio resource reuse by deploying RS in IEEE 802.16m network
Relays can enhance transmission rate for the MS located in shaded area or cell boundary
Coverage extension by deploying
RS in a IEEE 802.16m network

## Slide 24: Support of Femto-Cells and Self-Organization
IEEE 802.16m provides
Very high data rates and service continuity in smaller cells including indoor pico cells, femto cells, and hot-spots. The small cells may be deployed as an overlay to larger outdoor cells.
Self-configuration by allowing real plug and play installation of network nodes and cells, i.e. self-adaptation of the initial configuration, including the update of neighbor nodes and neighbor cells as well as means for fast reconfiguration and compensation in failure cases.
Self-optimization by allowing automated or autonomous optimization of network performance with respect to service availability, QoS, network efficiency and throughput.
Femto-cells are low power cellular base stations deployed in homes
Mobile stations can be used inside homes with the home broadband connection as backhaul
Femto-cells are an alternative way to deliver the benefits of Fixed Mobile Convergence. The distinction is that most FMC architectures require a new (dual-mode) handset which works with existing home/enterprise Wi-Fi access points, while a femto-cell-based deployment will work with existing handsets but requires installation of a new access point.
Macro Network
Operator Core Network
Internet
Femto-Cell
Access
Macro-Cell Access
Operator Core Network

## Slide 25: Enhanced Multicast and Broadcast Service
eMBS can be multiplexed with unicast services or deployed on a dedicated carrier

## Slide 26: Multi-RAT Operation and Handoff
Adjacent Channel Coexistence with UTRA LCR-TDD (TD-SCDMA)
        Adjacent Channel Coexistence with E-UTRA (LTE-TDD)
IEEE 802.16m supports interworking functionality to allow efficient handover to other radio access technologies including IEEE 802.11, 3GPP GSM/EDGE, UTRA (FDD and TDD), E-UTRA (FDD and TDD), and 3GPP2 CDMA200

## Slide 27: Multi-Radio Coexistence Support
Multi-Radio Device with Co-Located IEEE 802.16m MS, IEEE 802.11 STA, and IEEE 802.15.1 device
IEEE 802.16m provides protocols for the multi-radio coexistence functional blocks of MS and BS to communicate with each other via air interface.
MS generates management messages to report its co-located radio activities to BS, and BS generates management messages to respond with the corresponding actions to support multi-radio coexistence operation.
The multi-radio coexistence functional block at BS communicates with the scheduler functional block to operate properly according to the reported co-located coexistence activities.

## Slide 28: Advanced Interference Mitigation
  IEEE 802.16m provides
  Interference-aware BS co-ordination:
  BS exchange information across network backbone to manage radio resources such that inter-cell interference is minimized
  Fractional frequency reuse
  Multiple reuse settings possible within a cell to improve cell
  edge capacity and/or average cell capacity. Ex. cell-edge
  users are assigned reuse 3, while cell-center users benefit
  from reuse 1
  Interference aware scheduling
  Scheduler allocates resources based on interference aware CQI
  metrics
  Uplink power control:
    Subscribers adjust transmit power based on interference caused to other cells
  Interference randomization
    Transmitted signal is randomly spread the across entire frequency band such that aggregate interference from multiple transmitters on the average looks like Gaussian white noise
  TX Beamforming:
    Transmitter forms spatial beams & nulls to improve SINR particularly for cell-edge users
BS1
BS2
MS1
MS2
BS1 forms beam towards MS1 & null towards MS2
RRM
Manager
  Fractional Frequency Reuse
  TX Beamforming

## Slide 29: References
IEEE 802.16m-07/002r5, IEEE 802.16m System Requirements, http://ieee802.org/16/tgm/index.html, July 2008.
IEEE 802.16m-08/004r2, IEEE 802.16m Evaluation Methodology Document, http://ieee802.org/16/tgm/index.html , March 2008.
WiMAX Forum™ Mobile System Profile, Release 1.0 Approved Specification (Revision 1.4.0: 2007-05-02), http://www.wimaxforum.org/technology/documents.
WiMAX Forum Network Architecture Stage 2 - 3: Release 1, Version 1.2 (http://www.wimaxforum.org/technology/documents).
PART 16: AIR INTERFACE FOR BROADBAND WIRELESS ACCESS SYSTEMS, P802.16Rev2/D6, Revision of IEEE Std 802.16-2004 and consolidates material from IEEE Std 802.16e-2005,IEEE Std 802.16-2004/Cor1-2005,IEEE Std 802.16f-2005 and IEEE Std802.16g-2007, July 2008.
ITU 2008a Draft new Report ITU-R M.[IMT.EVAL], Guidelines for evaluation of radio interface technologies for IMT-Advanced [IMT.EVAL], June 2008.
ITU 2008b Draft new Report ITU-R M.[IMT.TECH], Requirements related to technical system performance for IMT-Advanced radio interface(s) [IMT.TECH], June 2008.
IMT-Advanced submission and evaluation process http://www.itu.int/ITU-R/index.asp?category=study-groups&rlink=rsg5-imt-advanced&lang=en.