## Slide 1
  Heterogeneous Networking for Future Wireless Broadband Networks
IEEE 802.16 Presentation Submission Template (Rev. 9)
Document Number:
  IEEE C802.16-10/0003r1
Date Submitted:
  2010-01-11
Source:
  Nageen Himayat, Shilpa Talwar, Kerstin Johnsson, E-mail: nageen.himayat@intel.com
  Kamran Etemad, Jose Puthenkulum, Vivek Gupta, Lily Yang, Minyoung Park, Geng Wu, Caroline Chan, Intel Corporation
Venue:
  San Diego, CA, USA
Base Contribution:
  None
Purpose:
  For discussion in the Project Planning Adhoc
Notice:
  This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein.
Release:
  The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16.
Patent Policy:
  The contributor is familiar with the IEEE-SA Patent Policy and Procedures:
      <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>.
  Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat >.

## Slide 2: Heterogeneous Networking for Future Wireless Broadband Networks Input for 802-wide Tutorial in March
Notes: <number>

## Slide 3: Agenda
Motivation
Challenges and Current Approaches
Preliminary Requirements
Summary & Recommendations
Notes: <number>

## Slide 4: Heterogeneous Networks
Exploit multiple radio interfaces at network or client
  Ex: Co-located WiFi/WiMAX interfaces in operator controlled femto-cell networks
Utilize licensed and unlicensed spectrum
  Virtual WiMAX carrier available through WiFi
  Multi-network access possible for single-radio client
Improve throughput by 2-3x in addition to coverage and QoS
WiMAX/WiFi Mobile
Internet Device
WiMAX
Integrated WiFi/ WiMax
Femtocell
Simultaneous
Multi
-
radio Operation
WiFi
WAN
WiFi
WiFi
Mobile Hotspot
MyFi
Multi
-
radio device
WiMAX/WiFi Mobile
Internet Device
WiMAX
Integrated WiFi/ WiMax
Femtocell
Virtual Carrier (WiFi)
WiFi
WAN
WiFi
WiFi
Mobile Hotspot
MyFi
Multi
-
radio device
Notes: <number>

## Slide 5: Heterogeneous Networks Deployment Scenarios
Enterprise
Integrated
Femto-AP
Laptop w/
WiFi & WiMAX
Hotspot
Integrated
Pico-cell
Home
Integrated Femto-AP
Multi-radio
Smart-Phone
Multi-radio
Device
Mobile Hotspot
Laptop w/
WiFi & WiMAX
Notes: <number>

## Slide 6: Heterogeneous Network Techniques
Idea | Enhanced Interworking Techniques | Description | Target Gains
Virtual WiMAX carrier | Interference Avoidance | Dynamically switch between WiFi & WiMAX to avoid interference | Increases system throughput ~3x
 | Diversity/Redundancy Transmission | Use added spectrum to improve diversity, code rates with incremental redundancy | Increases SINR ~3-5 dB, decreases cell-edge outage
 | Carrier Aggregation | Use added spectrum to transmit independent data streams | Increases peak throughput ~2-3x
 | QoS/ Load Balancing | QoS-aware mapping of apps to different spectrum | Improves QoS, system capacity
 | Energy Efficiency | Use virtual carrier to lower overall transmit power | Improved energy efficiency
 | Reduced Overhead w/ Unified Control | Streamline access, paging, other control procedures across networks | Improves power consumption, overhead
Multi-network access | Routing/Access | Provide connectivity between heterogeneous protocols | Improves connectivity, coverage
Notes: <number>

## Slide 7: Advantages of Heterogeneous Networks: Summary
Network | User
Improved cell capacity (> 2x) Improved cell-edge rates (> 2x) Reduced Overhead Lower deployment costs (TBD) | Higher Peak Rates (>2 x) Improved QoS (TBD) Reduced distortion for video (TBD) Power savings (TBD)

## Slide 8: Heterogeneous Network Challenges
GLL
WLAN
WiMAX
OTHER
MRRM
Network (AP/BS)
GLL
WLAN
WiMAX
OTHER
MRRM
Multi-Radio Client
* FP6: Ambient Network Framework
Multi-radio protocols & interfaces required
Define Generic Link Layer (GLL) *
  Manage interworking between heterogeneous links
Define Multi-Radio Resource Management (MRRM) *
  Manage radio resources across heterogeneous links
Determine depth of interworking across the protocol stack
Example: spectrum aggregation
Available in WiMAX & WiFi currently
  WiFi channel bonding at PHY layer w/ MAC coordination
  WiMAX carrier aggregation at MAC layer
Example: WiFi Off-load
3GPP considering IP layer interworking between WiFi & LTE
  Develop integrated multi-radio protocol design for 802.16/11
Notes: <number>

## Slide 9: Example: Channel Bonding in 802.11n
PHY layer bonding of adjacent 20 MHZ channels for 40 MHz channel
  Single FFT across 40 MHz
MAC layer coordination for 40 MHz channel access
Enhancements in 11ac, to support 80 MHz channels
Wait for PIFS < DIFS for secondary channel clear channel assessment (priority access)
802.11n Contention Based MAC

## Slide 10: Example: Carrier Aggregation in 802.16m
Aggregate N “fully” or “partially” configured “non-contiguous” carriers
MAC layer aggregation, w/ dynamic scheduling across carriers
Designate “Primary” carrier for main control interface
Restricted PHY layer segmentation (for contiguous bands)

## Slide 11: Example: WiFi-Offload Discussion in 3GPP
3GPP considering “IP flow mobility and seamless WLAN offload,” (TS 23.261)
Simultaneous connectivity across multiple access systems (3GPP, WLAN) with multi-mode devices.
Aggregation at IP layer
Multiple IP flows to a user can be routed through different access networks (3GPP or WLAN) based on operator control
Mobility support: only selected IP flows may be handed off

## Slide 12: Tradeoffs in Integrating Multi-radio Protocols
Attribute | PHY Layer Integration | MAC Layer Integration | IP Layer Integration
Track dynamic link variations | Yes | Yes | Average link variations only
Suitable Techniques | PHY layer combining, channel coding, MAC layer scheduling | MAC layer scheduling, Interference avoidance | QoS-aware mapping, Load Balancing
Synchronization | Tight Synchronization | Reduced Synchronization | Minimal Synchronization
Control Overhead Reduction | Reduced | Reduced | Limited Reduction
Flexible Spectrum Usage | Contiguous spectrum required | Flexible | Flexible
Co-location Requirement | Co-located interfaces required | Co-located interfaces required | Flexible mapping across distributed air interfaces
Notes: <number>

## Slide 13: Requirements to Enable Virtual Carrier
Aggregate “N” licensed and “M” un-licensed non-contiguous carriers (e.g. WiFi & WiMAX)
Enable tighter interworking for co-located interfaces (WiFi & WiMAX)
  Allow for dynamic channel tracking
  Minimize changes to existing protocol stacks
  Enable information exchange across protocol stacks
Minimize control interfaces, and designate an “Anchor” protocol
Design extensible protocols for distributed scenarios

## Slide 14: Summary & Recommendations
Heterogeneous networking techniques for WiFi & WiMAX promise significant improvements in network throughput and user QoS
Next generation 802.16 standard should develop protocols to synergistically enable use of additional un-licensed WiFi carriers