## Slide 1
  Client Cooperation in Future Wireless Broadband Networks
IEEE 802.16 Presentation Submission Template (Rev. 9)
Document Number:
  IEEE C802.16-10/0005
Date Submitted:
  2010-01-10
Source:
  Kerstin Johnsson, Nageen Himayat, Shilpa Talwar E-mail: kerstin.johnsson@intel.com
  Intel Corporation
Venue:
  San Diego, CA, USA
Base Contribution:
  None
Purpose:
  For discussion in the Project Planning Adhoc
Notice:
  This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein.
Release:
  The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16.
Patent Policy:
  The contributor is familiar with the IEEE-SA Patent Policy and Procedures:
      <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>.
  Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat >.

## Slide 2: Client Cooperation in Future Wireless Broadband Networks Input for 802-wide Tutorial in March
Notes: <number>

## Slide 3: What is Client Cooperation?
Poor WWAN link
Good WWAN link
Good WLAN link
WWAN BS
Laptop with WWAN & WLAN
MID with WWAN & WLAN
Client Cooperation (CC) is a MAC technique where clients interact to jointly transmit/receive data in wireless environments.
Idea: Exploit client clustering and peer-to-peer communication to transmit/receive data over multiple paths between source and destination.
Benefit: Performance improvement in throughput, capacity and reliability without increased infrastructure cost.
Usage: Clusters of stationary/nomadic clients that share the same WWAN service provider. Peer-to-peer link can be WWAN or WLAN.

## Slide 4: Use Cases
Other stores
Stranger devices in public assembly areas: Users deep inside cafés/stores/airports/arenas with very poor signal quality can receive a rate boost from performing CC with users closer to entrance or windows. Even if café has free WiFi (not all do), there are/will be services that are WiMAX specific, which require broadband rates.
Same client devices at home: Devices with poor signal quality within multi-level homes can receive significant rate increase from other devices belonging to same user in better signal locations.
M2M deployments: Meters in poor locations can receive rate boost and energy savings from meters in better locations, saving the owner deployment costs.
Tall buildings

## Slide 5: Business Models for Use Cases
Same client devices
  One owner guarantees full participation by all devices
  Net power savings across network
  Rate improvement to devices in poor locations
Stranger devices
  Service provider must dimension system based on non-cooperation to guarantee service
  CC boosts service above minimum guarantees
  Clients encouraged to participate by promise of
    Improved total throughput during subscription period
    Improved energy efficiency during low power periods
    Protection from rate degradation during traffic periods and power degradation during low power periods
M2M – same benefits as same client case

## Slide 6: CC Architecture Assumptions
WiMAX between ABS and AMSs; WiFi between AMSs
One WiFi hop between originating and cooperating AMSs
All AMSs are associated with the same ABS
ABS controls WiMAX scheduling
AMSs controls 3 fundamental protocols of CC: neighbor discovery, cooperator selection/assignment, and cooperation scheduling

## Slide 7: Goodput
[3.5]
>8x increase in cell-edge rates with small user clusters
Full-power cooperation (originator & cooperator transmit at max power) outperforms low-power cooperation (originator transmits low power, cooperator transmits high power)
Gains decrease with increased channel correlation among clients
[5]
[6.5]
[Average number of users within WiFi range]

## Slide 8: Power Consumption
Total network power consumption decreases
CC conserves power for originating AMS by requiring fewer retransmissions and supporting higher MCS; it consumes power from cooperator, but result is a net power savings
CC extends battery of clients w/ poor channels (where “power cost per bit” is high)
[3.5]
[5]
[6.5]
[Average number of users in WiFi range]

## Slide 9: Security
Potential security concerns
  Cooperator must know originator’s STID in order to detect transmit/receive allocations - may encourage denial of service attacks
  Cooperator receives bursts from/to originator – is there risk of cooperator viewing/altering bursts?
Resolution
  Resolve concern regarding denial of service attack by enabling ABS to create “cooperation STID” when CC is implemented between two AMSs
  Bursts are encrypted and keys are never shared with cooperator, thus there is no risk of cooperator viewing/altering bursts
<number>

## Slide 10: Mobility
07/28/26
<number>
  AMS can lose CC support due to mobility
    Mobility does not result in lost tx opportunities for AMS or changes in scheduling; if cooperator lost, AMS will simply tx on its own
    If AMS loses contact with cooperator, AMS will search for new cooperator
  Overhead results from having to find new cooperator for AMS
    Mobile AMSs shall not engage in CC
    Even semi-stationary AMSs move at times; however overhead from having to reassign cooperator small compared to gain from CC
Large number of low mobility scenarios
    Stationary scenarios such as M2M
    Semi-stationary scenarios such as laptops in homes, cafés, offices, etc.

## Slide 11: WiMAX/WiFi TDM for CC
MAP + DL Data Burst
(MS & Coop check for allocations given to their Coop STID and listen for bursts)
0
1
2
3
4
0
1
2
WiMAX frame
DL subframe index
UL subframe index
WiFi:
Coop tx rec’d DL burst to MS. MS tx UL burst to Coop.
BS
MS
Cooperator
HARQ + UL Data Burst
(MS tx burst)
UL Data Burst
(If Coop successfully rec’d burst from MS, it tx it at same time)

## Slide 12: Standards Impacts
WiFi
  Peer-to-peer WiFi connectivity required
  Neighbor Discovery and Cooperator Selection/Assignment protocols need to be enabled in P2P WiFi mode
WiMAX
  Enable coordinated Neighbor Discovery opportunities
      Speeds up WiFi Neighbor Discovery – saves power
      Increases probability of discovery – improves cooperator selection
  Provide shared STID for originator and cooperator AMSs when engaging in CC
      Establishes cooperative relationship without sharing AMS’s STID
      Allows central entity to do accounting

## Slide 13: Summary & Recommendations
Client Cooperation in Heterogeneous WiMAX/WiFi Networks promise significant improvements in cell-edge user goodput and network energy efficiency
Next generation 802.16 standard should develop protocols to facilitate Client Cooperation in Heterogeneous WiMAX/WiFi networks

## Slide 14: Backup

## Slide 15: SLS assumptions
We analyze cell-edge spectral efficiency (bps/Hz)
WiMAX multi-cellular network analysis
    cell radius = 500m
    realistic broadband channel models (Erceg-Greenstein path loss model, lognormal shadowing std=8, frequency-selective fading 4-tap channel with K-factor=1, exponential power delay profile)
    co-channel interference (only consider 1st-tier interference from neighboring ABSs) assuming reuse 1
    OFDMA signaling
    Typical WiMAX link budget
    BS antenna height = 12.5m, MS antenna height = 2m
    AMS power = 23 dBm (200 mW)
    ABS has two antennas and all AMSs have a single antenna
    SNR limit = 20 dB (i.e. any gain above this yields no goodput gain since this is max MCS level)
    ABS-to-AMS channels uncorrelated
    AMSs are located randomly throughout WiMAX cells
    Round Robin scheduling
    Gain combining of originating and cooperating AMS signals at ABS receiver
    Cooperation is for upstream traffic in UL subframes
WiFi analysis
    Receive radius = 200m (i.e. this is the AMS cluster radius)
    AMS power = 23 dBm (200 mW)
    RTS-CTS scheduling
    WiFi transmissions are only during WiMAX UL subframes

## Slide 16: More Use Cases
Airport terminal
Airports: In airports, or any public waiting area, there will be many locations with poor signal. These can be significantly improved by receiving CC support from users in good locations.