## Slide 1
  Enhancing Mobile Video Service Capabilities over Next-Generation WiMAX
IEEE 802.16 Presentation Submission Template (Rev. 9)
Document Number:
  IEEE C802.16-10/0007
Date Submitted:
  2010-01-10
Source:
  Ozgur Oyman, Jeffrey Foerster E-mail: {ozgur.oyman, jeffrey.r.foerster}@intel.com
  Intel Corporation
Venue:
  San Diego, CA, USA
Base Contribution:
  None
Purpose:
  For discussion in the Project Planning Adhoc
Notice:
  This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein.
Release:
  The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16.
Patent Policy:
  The contributor is familiar with the IEEE-SA Patent Policy and Procedures:
      <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>.
  Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat >.

## Slide 2: Mobile Video Services
Important key trends
  Mobile traffic is growing significantly, will be dominated by video and data
  Mobile devices are getting more powerful…new usages possible
  Mobile graphics is getting better
  Continuum of screen sizes exist
BUT, Wireless capacity still limited
  Still long ways from true IPTV/video-on-demand to mobile devices
  Traffic trends and new usages will continue to stress capacity further
Figure 1. Cisco Forecasts 2 Exabytes per Month of Mobile Data Traffic in 2013*
Figure 2. Laptops and Mobile Broadband Handsets Drive Traffic Growth*
*Source: Cisco Visual Networking Index, Oct. 2009
*Source: Cisco Visual Networking Index, Oct. 2009
Notes: http://www.cisco.com/en/US/solutions/collateral/ns341/ns525/ns537/ns705/ns827/white_paper_c11-520862.html
Video content delivery over wireless networks is expected to grow exponentially in the coming years, driven by the desire to have ubiquitous access to TV content and interactive video services across multiple platforms, including TVs, PCs, mobile devices, and embedded devices (i.e., vehicles). This trend is supported by recent studies (Cisco Visual Networking Index) which predict that the potential traffic going to mobile devices in the future is expected to increase by a factor of 66 times by 2013. Much of this future traffic will be video based services which will include more than just streaming TV content to mobile devices, but also internet video, video on demand, personal video streaming, video sharing applications (from mobile to mobile), video conferencing, live video broadcasting (cloud to mobile as well as mobile to cloud), video Twitter, and video blogging. Although traditional wireless broadcast networks may play a role in delivering some of the content, this will not be suitable for more personalized content as well as real-time interactive services. Given the high-throughput demands of video content, we expect these new services and growing desire for ubiquitous access to video content will significantly stress the capacity of both the downlink and uplink of future wireless communications systems.
<number>

## Slide 3: Mobile Content Delivery Methods
Internet (Hulu, Joost,
Netflix, Blockbuster)
Broadcast
Networks
Home
(Slingbox)
IPTV, cable,
telecom carrier
WiFi Hotspot
Broadband wireless
(e.g., WiMAX)
Broadcast
(Terrestrial, Sat.)
Multiple
Devices
Mobile content delivery methods:
  Streaming: unicast, broadcast
  Download: kiosk, STB, over-the-air
New usage models
  Video conferencing, video share
  Video twitter, video blogging
  Live video broadcasting, video upload
Kiosk
Key
criteria:
Quality
Latency
Throughput
Capacity
Scalability
Cost
Multiple
Networks
Multiple
Content
Sources
Car
Notes: iPhone Consumes 50% World's Mobile Data Traffic
http://www.tomsguide.com/us/iPhone-Apple-RIM-HTC-Smartphone,news-5206.html
The floodgates open for 3G video broadcasting on iPhone
http://arstechnica.com/apple/news/2009/12/are-the-floodgates-opening-for-3g-video-broadcasting-on-iphone.ars
Apple’s iPhone 3GS powers 400% surge in YouTube mobile video uploads
Thursday, June 25, 2009 - 04:05 PM EST
http://macdailynews.com/index.php/weblog/comments/21594/
Mobile Video & Mobile TV to Soar Over the Next 5 Years
Mark R Robertson | May 31, 2009
http://www.reelseo.com/mobile-video/
O2's network in meltdown from smartphone usage
http://www.fiercewireless.com/europe/story/o2s-network-meltdown-smartphone-usage/2009-11-18?utm_medium=nl&utm_source=internal
watching a YouTube video on a smartphone can use the same capacity on the network as sending 500,000 text messages simultaneously.“
<number>

## Slide 4: Outline
This talk addresses the following two key challenges for enhancing mobile video service capabilities over next-generation WiMAX:
  Capacity: Can WiMAX support high-bandwidth video applications? How many video users can WiMAX serve in the presence of voice and data traffic?
  QoS: How should next-generation WiMAX standard better manage QoS for mobile video services?
  Another key mobile video challenge (not addressed in this talk):
  Adaptability and Scalability: How can the network adapt and scale to support time-varying conditions and multiple device classes?

## Slide 5: 1- Video Capacity over WiMAX
Assess the viability of mobile video services over current (16m) and next-generation (16x) WiMAX networks
Evaluate the video service capacity of current and future WiMAX-based networks with voice and data traffic present
In the capacity analysis, we consider the following services over WiMAX:
  Unicast video services
  Multicast/broadcast services (MBS)
Our key assumptions for this analysis are as follows:
  16x networks will support higher channel bandwidths in the order of 40-80 MHz.
  16x networks will provide 2X higher spectral efficiency than 16m.
  Consider the same amount of service overheads in 16m and 16x.

## Slide 6: MBS Video Capacity Evaluation Methodology
The number of MBS video channels for WiMAX is computed based on the following formula:
Number of usable OFDMA subcarriers for data transmission
Number of DL OFDMA symbols per frame allocated for MBS
Percentage of overhead for MBS
MBS spectral efficiency in bps/Hz
Data rate in bps for the MBS video channel
Frame duration in seconds

## Slide 7: MBS Video Capacity
WiMAX System | MBS Spectral Efficiency (bps/Hz) | MBS Video Channels for R = 384 kbps | MBS Video Channels for R = 768 kbps | MBS Video Channels for R=1.536 Mbps
802.16m (4x2 MIMO) @ 10 MHz bandwidth | 4 | 20 | 10 | 5
802.16x @ 40 MHz Bandwidth (lower bound) | 4 | 83 | 41 | 20
802.16x @ 80 MHz Bandwidth (upper bound) | 8 | 334 | 167 | 83
Maximum of 50% of total available DL OFDMA resources allowed for streaming video to allow for concurrent voice and data services, DL:UL ratio = 2:1.

## Slide 8: Unicast Video Capacity Evaluation Methodology
The number of unicast users per sector for DL video transmission is computed based on the following formula:
Number of usable OFDMA subcarriers for data transmission
Number of DL OFDMA symbols per frame for unicast video
Percentage of overhead for DL unicast video
DL unicast video spectral efficiency in bps/Hz/sector for n-th scheduled user among N users in the sector (n=1,…,N)
Data rate in bps for the unicast video service
Frame duration in seconds

## Slide 9: WiMAX Unicast Coverage and Capacity
* Maximum of 50% of total available DL OFDMA resources allowed for streaming video to allow for concurrent voice and data services, DL:UL ratio = 2:1.
** Note: Typical PER for video should be ~1%, so coverage and throughputs are optimistic.
WiMAX Unicast capacity | .16m, 10 MHz, 4x2, 10% PER** | .16x, 40 MHz, 2x16m, 10% PER** | .16x, 80 MHz, 2x16m, 10% PER**
384 Kbps | 6 | 39 | 79
768 Kbps | 4 | 19 | 39
1.536 Mbps | 2 | 10 | 19
WiMAX capacity for DL Unicast video streaming at different rates
(average # of unicast video users per sector which can be serviced)
WiMAX coverage for DL Unicast video streaming at different rates
WiMAX Coverage* | .16m, 10 MHz, 4x2, 10% PER** | .16x, 40 MHz, 2x16m, 10% PER** | .16x, 80 MHz, 2x16m, 10% PER**
384 Kbps | 95% | 99% | 99%
768 Kbps | 80% | 99% | 99%
1.536 Mbps | 50% | 99% | 99%
Notes: <number>

## Slide 10: Observations
Current network capacity limits number of simultaneous video streams.
With more bandwidth and higher spectral efficiency, next-generation WiMAX can provide much higher capacity for serving more video users and supporting larger number of video streams.

## Slide 11
2- Optimizing Video Quality
Quality-aware networking for video communications to
  optimize user experience
  ensure end-to-end robustness of content delivery
Quality degradation may be caused by high distortion, limited bandwidth, excessive delay, power constraints, complexity & cost limitations
Application-aware optimization needed:
In the network to ensure end-to-end robustness of video content delivery
  Ex: transmission reliability based on “perceptual importance” of video bits
  Ex: app QoS-driven cross-layer design approaches for resource allocation and management – leads to new notions of efficiency and fairness
At the client to ensure user experience driven optimization (PHY-APP cross layer design)
  Ex: application rate, codec adaptation based on predicted link & network conditions, joint source-channel coding optimizations
Application
Layer
Client
IP
TCP
UDP
Cross-Layer
Optimization

## Slide 12
Distortion-Aware PHY/MAC Design for Enhanced Multimedia Delivery
For video communication, users’ perceived quality for multimedia content is dictated by end-to-end distortion.
Goal: PHY/MAC layer design to minimize end-to-end distortion.
Our analysis suggests that this design goal significantly modifies how PHY/MAC components work compared to current system designs.
  Distortion-awareness requires new design methods than more standard optimizations, such as maximizing spectral efficiency or throughput.
  Relevant topics for distortion-aware processing:
    Cross-layer design (PHY/MAC/NET/APP)
    Joint source-channel coding

## Slide 13
Distortion-Aware PHY/MAC Design for Enhanced Multimedia Delivery

## Slide 14
Joint Source-Channel Coding (JSCC)
Separate source-channel coding: Source coding independent of channel structure & channel coding independent of source structure
Joint source-channel coding (JSCC) aims to jointly optimize source compression and channel coding.
JSCC goal: Minimize end-to-end distortion by simultaneously accounting for the impact of both source quantization errors and channel-induced errors.

## Slide 15: Distortion-Aware Link Adaptation
Let R be channel coding rate associated with a given MCS in bps/Hz.
It is assumed that the distortion-rate function D(R) for the multimedia source/codec is made available at the radio level for PHY/MAC optimizations.
Classical system design approach aims to maximize throughput or goodput (possibly subject to a target PER):
Proposed distortion-aware MCS selection criterion
Interested in peak SNR (PSNR) defined as (determines user’s perceived quality of video):

## Slide 16: Peak SNR Performance Comparison

## Slide 17: Observations
Distortion-aware link adaptation ensures robust user quality of experience (QoE):
  Enables reduced PSNR variability and graceful PSNR increase/decrease with changing link conditions
  High PSNR fluctuation and variable QoE with the throughput-maximizing approach.
  Operate at lower PER, reliability is relatively more important than rate.
  Significant PSNR penalty from throughput-maximizing link adaptation over distortion-aware link adaptation
Distortion-awareness requires new PHY/MAC design methods than more standard optimizations, such as maximizing spectral efficiency or throughput.

## Slide 18: Conclusions and Recommendations
Dominance of video content over wireless networks in future creates unique opportunity to optimize WiMAX for video applications.
Initial results show significant gains possible with distortion-aware processing and cross-layer optimizations.
Recommendations for Next Generation WiMAX:
  Optimizing video capacity and QoS should be a key focus area toward developing new PHY/MAC specifications.
  New system requirements should be established for mobile video services (e.g., minimum number of video users, etc.)
  New performance evaluation methodologies and target requirements are needed to account for various video quality metrics (e.g., distortion, PSNR, etc.)
  Video-enhancing techniques such as JSCC and distortion aware processing, should be adopted to anticipate future growth of video services.