## Slide 1
  Future Wireless Broadband Networks: Challenges and Possibilities
IEEE 802.16 Presentation Submission Template (Rev. 9)
Document Number:
  IEEE C802.16-10/0009r1
Date Submitted:
  2010-01-10
Source:
  Shilpa Talwar, Kerstin Johnsson, Nageen Himayat, E-mail: {shilpa.talwar, kerstin.johnsson, nageen.himayat}@intel.com
  Jose Puthenkulam, Geng Wu, Caroline Chan, Feng Xue, Minnie Ho, Rath Vannithamby, Ozgur Oyman, Wendy Wong, Qinghua Li, Guangjie Li, Sumeet Sandhu, Sassan Ahmadi, Hujun Yin, Yang-seok Choi, Apostolos Papathanassiou, Muthaiah Venkatachalam
  Intel Corporation
Venue:
  San Diego, CA, USA
Base Contribution:
  None
Purpose:
  For discussion in the Project Planning Adhoc
Notice:
  This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein.
Release:
  The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16.
Patent Policy:
  The contributor is familiar with the IEEE-SA Patent Policy and Procedures:
      <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>.
  Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat >.

## Slide 2: Future Wireless Broadband Networks Challenges and Possibilities Input for 802-wide Tutorial in March
Notes: <number>

## Slide 3: Agenda
Motivation
Promising Technologies
Technology Details
Summary & Recommendation
Notes: <number>

## Slide 4: Motivation
Notes: <number>

## Slide 5: Summary of November contribution
Future broadband networks will need to provide very high capacity at low network cost
  Capacity demand is driven by
  a) Large screen devices,
  b) New high rate applications (mobile video)
  c) More connected users & devices
  Promising technologies were identified
Future broadband networks will need to increase revenue through enhanced or new services
  Machine-2-Machine communications
  Enhanced user experience for mobile video and emerging mobile internet applications

## Slide 6: Challenge – Very High Capacity
  Future networks will require Innovations at all levels to meet capacity demand
*Source: Cisco Visual Networking Index, Oct. 2009
*Source: Cisco Visual Networking Index, Oct. 2009
Mobile data traffic is expected to grow by 66x between 2008-2013 (Source: Cisco*)
    Laptops & Mobile broadband handsets drive traffic growth
    Video & data will be dominant sources of traffic
Spectral Efficiency gains are typically limited to 2-3x every generation of Air Interface
Notes: <number>

## Slide 7: Challenge – Lower Revenue Per Bit
  Future networks need to drastically lower Cost per Bit, and enable new Services
Service providers are facing challenges at both ends
    Invest in network capacity to meet demand
    Increase revenue with new applications and services
Cost of Network deployments to meet demand is increasing faster than revenue
Notes: <number>

## Slide 8: Service provider options – the big picture
Invest in Capacity
Ration
Network Usage
Create New Revenue
Buy more spectrum
Split Cells
Deploy new technologies
Deploy multi-tier networks
Exploit multiple protocols
Tiered service levels
Traffic shaping
Exclusive devices
Enterprise Services
Applications Store
Enhanced QOS
M2M – new business
  Focus of this presentation is on Technologies with Standards implications
Notes: <number>

## Slide 9: Promising Technologies
Notes: <number>

## Slide 10: Investing in Capacity
Technique | Status/Issues | Possibilities
Deploy more spectrum | Low frequency spectrum is limited & expensive | Target higher frequencies (3.5-4.9 GHz), wider channels (40-80 MHz) Synergistic use of unlicensed spectrum (802.11)
Reuse Spectrum | Simple cell splitting is limited by Cost Low cost infrastructure, Femto & Relays in 16m | Smart multi-tier networks reusing same spectrum, self-organizing Interference Management
Link capacity | Theoretical link capacity nearly achieved (Shannon) MIMO (8x8) in 16m DL, (2x4) in UL | Higher order MIMO in UL Higher order modulation
Cell capacity | Significant gains harnessed in 802.16m: MU-MIMO (4 users), MAC enhancements | Higher order MU-MIMO (8 users) Client co-operation
Multi-cell/Network Capacity | Simple techniques included in 16m: FFR, uplink multi-cell Power Control, Coordinated BF | Network MIMO Interference Alignment
Notes: 3.5 GHz: FDD: DL = 80 MHz, UL = 40 MHz contiguous
3.5 GHz: FDD: DL = 40 + 40; UL = 20 + 20, non-contiguous
3.5 GHz: TDD: 100 MHz contiguous
2.3 GHz: TDD: 100 MHz contiguous

## Slide 11: Potential Requirements & Technology Possibilties
Metric | Potential Target | Potential Technologies
Peak Data Rate (bps) | 1 to 5 Gbps Baseline (16m) – ITU submission Peak rate ~ 356 Mbps, 4x4 MIMO, 20MHz Peak rate ~ 712 Mbps, 8x8 MIMO MIMO Carrier Aggregation up to 100 MHz ~3.6 Gbps | Higher BW support (40 MHz) Peak Rate ~ 16m rate x 2 = 1.4Gbps
 |  | Carrier aggregation across licensed & unlicensed bands Peak Rate ~ 1.4 Gbps x 6 carriers @ 20 MHz = 5.7Gbps 802.11 radio is used in conjunction with 802.16
 |  | Improvement in Peak Spectral Efficiency (below)
Peak Spectral Efficiency (bps/Hz) | Downlink: 45 bps/Hz Uplink: 22 bps/Hz [These are ~ 3x IMT-advanced requirements] Baseline (16m) – ITU submission DL Peak SE ~ 35.6 bps/Hz, 8 MIMO streams UL Peak SE ~ 9.4 bps/Hz, 2 MIMO streams | Higher order MIMO in UL (4 streams) UL Peak SE ~ 16m SE x 2 = 18.8 bps/Hz
 |  | Higher modulation (up to 256 QAM) DL Peak SE ~ 16m SE x (8/6) = 47.5 bps/Hz UL Peak SE ~ 16m SE x (8/6) x 4 = 25 bps/Hz
Notes: <number>
3.5 GHz: FDD: DL = 80 MHz, UL = 40 MHz contiguous
3.5 GHz: FDD: DL = 40 + 40; UL = 20 + 20, non-contiguous
3.5 GHz: TDD: 100 MHz contiguous
2.3 GHz: TDD: 100 MHz contiguous

## Slide 12
Metric | Potential Target | Potential Technologies
Average SE (bps/Hz/cell) | Downlink: > 2x with 4x4 (or 8x4) Uplink: > 2x with 4x4 (or 4x8) Baseline (16m) – IMT-adv Requirements DL Avg SE = 2.2 bps/Hz/sector, 4x2 UL Avg SE = 1.4 bps/Hz/sector, 2x4 (Urban-coverage scenario) | Network MIMO DL Avg SE ~ 3x with 4x4 UL Avg SE ~ TBD
 |  | Higher order MU-MIMO (8 users DL, 4 users UL) DL Avg. SE ~ TBD UL Avg. SE ~ TBD
Cell-edge user SE (bps/Hz/cell/ user) | Downlink: > 2x with 4x4 (or 8x4) Uplink: > 2x with 4x4 (or 4x8) Baseline (16m) – IMT-adv Requirements DL Cell-edge SE = 0.06 bps/Hz/sector, 4x2 UL Cell-edge SE = 0.03 bps/Hz/sector, 2x4 (Urban-coverage scenario) | Client co-operation DL Cell-edge SE ~ 1.3 to 2x UL Cell-edge SE ~ 1.3 to 2x
 |  | Interference Alignment DL Cell-edge SE ~ TBD UL Cell-edge SE ~ TBD
Potential Requirements & Technology Possibilties (Continued)
Notes: <number>
Average SE
DL: Has been shown 3.7bps/Hz/sector with 4x4, which is nearly 2x (4.4bps/Hz/sector). 16m ITU numbers are close to requirements.
UL: 16m ITU submission shows 2.7bps/Hz/sector, which is nearly 2x (2.8bps/sector)
Cell-edge SE
DL: 16m ITU numbers are close to requirements (no FFR)
UL: 16m ITU numbers 0.11 ~ 3x

## Slide 13
Metric | Potential Target | Potential Technologies
Areal Capacity (bps/m^2) | Areal capacity = Sum throughput delivered by multiple network tiers / Coverage area Areal capacity should be greater than single tier (macro) capacity | Same Frequency Relays Heterogeneous Networks (WiFi & WiMAX) Femtocell Networks Areal Capacity ~ N_femto_AP x Avg 16m rate
Outdoor & Indoor Average SE* (bps/Hz/cell) | Outdoor Avg SE should be equal or greater than SE w/o multi-tier (offloading) Indoor Avg SE should be greater than some required minimum | Same Frequency Femtocell Network Prelim results, SISO, static SLS Outdoors Avg. SE ~ 1.5x Cell-edge SE remains same Indoors Avg SE ~ 0.6 to 1 bps/Hz/cell Cell-edge SE ~ TBD
Outdoor & Indoor Cell-edge SE* (bps/Hz/cell/user) | Outdoor Cell-edge SE should not be reduced by multi-tier operation Indoor Cell-edge SE should be greater than some required minimum | 
New Requirements for Multi-tier Networks
* Same frequency Macro + Femto Network
Notes: <number>

## Slide 14
Creating Revenue through Services
Technique | Status/Issues | Possibilities
Machine-to-Machine Connectivity | M2M offers oppty to connect 10x devices compared to users Cellular networks today can meet needs of some M2M applications Broad range of applications pose challenges on air interface & network | Standards are needed to improve cost-efficiency of fragmented M2M markets Optimize air interface & network for most promising set of applications
Enhanced Mobile Internet Experience | Current QoS mechanisms are not scalable for emerging Mobile Internet applications Best-Effort QOS class is popular from flat Rate model perspective, but without QoE | Define QOE metrics for Mobile Internet applications Develop air interface hooks to improve application QoE
Mobile Video | Mobile video projected to be major source of traffic by 2013 Today’s networks optimize throughput, not video quality or number of video users that can be supported | Optimize QOS & capacity for video users QOS: End-to-end Distortion metric Video Capacity: N active users/ sector/MHz
Notes: Mobile internet applications - Gaming, social networking, Skype…

## Slide 15: Technology Details
Notes: <number>

## Slide 16: Promising Technologies & Potential Gains
Capacity Improvement |  | Peak Rate | Spectral Efficiency (Macro) |  | Areal Capacity | Indoor Coverage | Energy Efficiency
 |  |  | Avg. | Cell-edge |  |  | 
More Spectrum | Heterogeneous Networks | Primary |  | Secondary |  | Primary | Secondary
Reuse Spectrum | Multi-tier Networks |  | Secondary |  | Primary | Primary | Secondary
Cell Capacity | Client Co-operation |  |  | Primary |  | Secondary | Secondary
Network Capacity | Network MIMO |  | Primary | Primary |  |  | Secondary
 | Interference Alignment |  | Secondary | Primary |  |  | 
Notes: <number>

## Slide 17: Promising Technologies & Potential Gains (Continued)
Advanced Services | User Experience | Application Capacity | New Applications
Machine-2-Machine |  | Primary | Primary
Mobile Internet | Primary | Secondary | 
Mobile Video | Primary | Secondary | 
Notes: <number>

## Slide 18: Heterogeneous Networks
Idea
Exploit multiple radio interfaces available at network or client
  WiFi/WiMAX interfaces in operator controlled femto-cell networks
Utilize licensed and unlicensed spectrum
  Virtual WiMAX carrier available through WiFi
  Multi-network access possible for single-radio client
WiMAX/WiFi Mobile
Internet Device
WiMAX
Integrated WiFi/ WiMax
Femtocell
Simultaneous
Multi
-
radio Operation
WiFi
WAN
WiFi
WiFi
Mobile Hotspot
MyFi
Multi
-
radio device
WiMAX/WiFi Mobile
Internet Device
WiMAX
Integrated WiFi/ WiMax
Femtocell
Virtual Carrier (WiFi)
WiFi
WAN
WiFi
WiFi
Mobile Hotspot
MyFi
Multi
-
radio device
More Spectrum
Notes: <number>

## Slide 19: Heterogeneous Network Techniques
Idea | Enhanced Spectrum Utilization Techniques | Description | Target Gains
Virtual WiMAX carrier | Interference Avoidance | Dynamically switch between WiFi & WiMAX to avoid interference | Increases system throughput ~3x
 | Diversity/Redundancy Transmission | Use added spectrum to improve diversity, code rates with incremental redundancy | Increases SINR ~3-5 dB, decreases cell-edge outage
 | Carrier Aggregation | Use added spectrum to transmit independent data streams | Increases peak throughput ~2-3x
 | QoS/ Load Balancing | QoS-aware mapping of apps to different spectrum | Improves QoS, system capacity
Multi-network access | Routing/Access | Provide connectivity between heterogeneous protocols | Improves connectivity, coverage
More Spectrum
Notes: <number>

## Slide 20: Multi-tier Networks
Idea
Overlay multiple tiers of cells, macro/pico/femto, potentially sharing common spectrum
Client-to-client communication can be viewed as an additional tier (see client co-operation)
Tiers can be heterogeneous (802.16 and 802.11)
Macro-BS
Femto-AP
(Indoor coverage & offload macro-BS)
Pico-BS
(Areal capacity)
Relay
Femto/WiFi-AP
(Offload Macro-BS)
Coverage Hole
Client Relay
Wireless backhaul
Wireless Access
Reuse Spectrum
Notes: <number>

## Slide 21: Advantages of Multi-tier Networks
Significant gains in areal capacity via aggressive spectrum reuse and use of unlicensed bands
  E.g.: Co-channel femto-cells provide linear gains in areal capacity with increasing number of femto-AP’s in a multi-tier deployment
Cost structure of smaller cells (pico and femto) is more favorable
Indoor coverage is improved through low cost femto-cells
  Significant potential savings in cost per bit via multi-tier networks
Source: Johansson at al, ‘A Methodology for Estimating Cost and Performance of Heterogeneous Wireless Access Networks’, PIMRC’07.
Reuse Spectrum
Notes: <number>

## Slide 22: Client Co-operation
Poor WWAN link
Good WWAN link
Good WLAN link
WWAN BS
Laptop with WWAN & WLAN
MID with WWAN & WLAN
Client Cooperation is a technique where clients interact to jointly transmit and/or receive information in wireless environments.
Idea: Exploit client clustering and P2P communication to transmit/receive information over multiple paths between BS and client
Usage: Clusters of stationary/nomadic clients with WLAN P2P connectivity that share WWAN service provider
Benefits:
1) Performance improvement in cell-edge capacity and reliability without increased infrastructure cost 2) Extend battery of clients with poor channels, for whom “power cost per bit” is high
Cell Capacity
Notes: <number>

## Slide 23: Client Cooperation Gains
Cell Capacity
Goodput
Energy-efficiency
[8]
[11]
[15]
[19]
[8]
[11]
[15]
[19]
[Average number of users in WiFi range]
[Average number of users in WiFi range]
>8x increase in cell-edge rates with small user clusters
Total network power consumption decreases

## Slide 24: Network MIMO
Idea
Network MIMO algorithms enabled by central cloud processing
Cooperative MIMO, Distributed Antennas
Converged wireless Cloud
Processing server
Fiber
DAS with 4 distributed antennas show
nearly 300% gain over CAS by utilizing
MU MIMO protocol in system evaluation
Distributed Antennas
Network Capacity
Notes: <number>

## Slide 25: Interference Alignment
Idea
Align transmit directions so that interfering signals all come from the same “direction” (subspace)
Alignment can be across antennas, frequency, time
Benefits: Improves uplink and downlink transmissions of cell-edge users;
Low receiver complexity
Challenge: Practical schemes that can achieve theoretical gain
Performance (theory) in high SNR regime: If there are K pairs and each node has M antennas, then KM/2 degrees of freedom are achievable. For comparison, perfect resource sharing achieves 1 degree of freedom.
(Cadambe & Jafar 2008)
Signal
subspace
Interf. subspace
Tx signal
Rx signal
Network Capacity
Notes: <number>

## Slide 26
M2M enables large set of applications by embedding every day devices with mobile transceivers
Opens a new dimension to connectivity: Anywhere, Anytime, ANYTHING
Cellular M2M can offer significant advantage for new services and applications
  Ubiquitous coverage
  Mobility support
  Broadband rates
  Lower cost through standardization
Machine-2-Machine
M2M: automated flow of data from machine to machine
Advanced Services

## Slide 27
Different M2M applications will have distinct (perhaps opposing) requirements
Need to carefully select required features for most promising applications
PHY/MAC changes possible to improve M2M performance (needs careful benchmarking)
Air Interface Optimization for M2M
 | Low Mobility | High Mobility | Small Data Transmissions | Group-based Transmissions | Mobile Originated | Monitoring | Low Power Consumption
Vehicular Infotainment |  | Y |  |  |  |  | 
Pay-As-You-Drive |  |  |  |  | Y |  | 
Multimedia marketing | Y |  |  | Y |  |  | 
eHealth |  |  |  | Y | Y | Y | 
Anti-theft video surveillance | Y |  |  |  |  | Y | 
Advanced Metering |  |  | Y | Y |  | Y | Y
Advanced Services

## Slide 28
Enhanced Mobile Internet Experience
Advanced Services
Mobile Internet applications have dynamic traffic characteristics and time-varying performance requirements
  Variable packet size, inter-arrival time, and arrival rate due to end-2-end congestion control like TCP, and other network factors)
Today’s QoS Mechanisms are not scalable for emerging Mobile Internet Applications
  Ex: Difficult to map Skype application to existing QOS class
Define QOE metrics for Mobile Internet applications
Develop air-interface hooks to maintain “good” Mobile Internet Application user QoE
  Ex. exchange application level information with radio/network for better resource scheduling
  Ex. exchange radio/network level information with application for better application adaptation

## Slide 29
Mobile Video
Dominance of video content in future networks creates unique opportunity to optimize for video applications
Goal of ‘quality-aware’ video communications is to
  Enhance user experience
  Ensure end-to-end robustness of content delivery
Relevant technologies for enhancing QoS for mobile video
  Joint source-channel coding (JSCC)
  Distortion-aware processing
  Cross-layer design (PHY/MAC/NET/APP)
Initial results show significant gains possible with distortion-aware processing and cross-layer optimizations
Advanced Services

## Slide 30: Summary & Recommendations
Notes: <number>

## Slide 31: Summary of Key Technical Features
Very high throughput (> 1Gbps)
  40Mhz bandwidth support
  Use of unlicensed bands (WiFi)
  High-order modulation
  Higher MIMO configuration
Higher spectral efficiency (> 2x)
  Advanced MIMO
  Multi-cell co-operation
  Client Co-operation
High Areal Capacity & Indoor coverage
  Multi-tier Network Architectures
  Heterogeneous Networks
M2M support
Enhanced user experience

## Slide 32: Recommendations
New system/technology needed to drive increased capacity
New radio network topologies needed for lower cost per bit
Protocols needed to create new and differentiated services
Plan for next generation 802.16 standard needed
Notes: <number>

## Slide 33: Backup
Notes: <number>

## Slide 34: Mobile Performance Today
  802.16m leads in performance. 802.16e leads in performance and availability
Technology | Required Spectrum | Standards Completion (Expected) | Peak Throughput (Mbps) |  | Avg. Spectral Efficiency (bits/sec/Hz/Sector) |  | Sleep to Active Latency
 |  |  | DL | UL | DL | UL | 
802.16e/Mobile WiMAX Release 1.0 2x2 MIMO TDD | 10 MHz (5:3) | Dec. 2005 | 40 | 17 | 1.4 | 0.7 | < 40 ms
HSPA (Release 6) FDD | 2x5 MHz | Mar. 2005 | 14 | 6 | 0.5 | 0.3 | 250 ms
HSPA+ (Release 8) 2x2 MIMO FDD | 2x5 MHz | Dec. 2008 | 42 | 12 | 0.8 | 0.5 | 50 ms
LTE (Release 8) 2x2 MIMO FDD | 2x10 MHz | Mar. 2009 | 86 | 38 | 1.6 | 0.8 | 10 ms
LTE (Release 10) 4x4 MIMO FDD | 2x10 MHz | (Q1 2011) | 160 | 80 | 2.4 | 2.1 | <10ms
802.16m 4x4 MIMO TDD | 20 MHz (5:3) | (Q3, 2010) | 170 | 90 | 2.9 | 2.5 | <10 ms
All peak throughput numbers (except for WiMAX 1.0) exclude the impact of control & coding overhead
3GPP data rate numbers are from 3GPP document TR 25.912, page 55 and average of NGMN documents for LTE
3GPP Latency numbers are from 3GPP 25.999 & 3GPP 36.912
3GPP LTE Release 10 numbers are from the 3GPP ITU-R IMT-Advanced submission TR 36.912 with L=3 for pragmatic overhead calculation
WiMAX Release 1.0 uplink assumes virtual MIMO
802.16e/WiMAX 1.0 spectral efficiency numbers are based on NGMN evaluation methodology
802.16m is based on ITU-R IMT-Advanced submission evaluation and for urban macro –cell
Notes: <number>

## Slide 35: Commercial Broadband Standards
IEEE 802.3 Standards*
IEEE 802.11 Standards*
IEEE 802.16 Standards*
LANs
Wireless LANs
Wireless MANs
Current Peak: 10Gbps
Current Peak: 600Mbps
Current Peak: 300Mbps
Target Peak
IEEE P802.3ba : 40/100 Gbps
Target Peak
IEEE P802.11ac (5GHz): >1 Gbps
IEEE P802.11ad (60GHz):>1-3 Gbps
Target Peak
>1 Gbps?
+Logos and trademarks belong to the other entities
802.11b (2.4 GHz)
802.11g (2.4 GHz)
802.11a (5 GHz)
802.11n (2.4, 5 GHz)
*Not a complete list of IEEE 802 standards
+
+
+
+
+
802.16e (Licensed <6 GHz)
P802.16m (Licensed <6 GHz)
(under development)
  Peak Rates of >1 Gbps potential target for Wireless Broadband

## Slide 36: What is happening in the marketplace?
Broadband traffic is growing exponentially with introduction of new devices: iPhones and Netbooks
Larger screen mobile devices drive up data usage: eg. iPhone consumes 30x data
Morgan Stanley, Economy + Internet Trends, Oct 2009
Morgan Stanley
iPhone
Netbook
Notes: <number>

## Slide 37: Fixed to mobile transition is happening
  Consumers prefer wireless devices over wired
  Voice: Users moving from landline to mobile for cost & convenience (ex. Finland has 60% mobile-only households)
  Internet: “Mobile internet adoption has outpaced desktop” (Morgan Stanley)
Notes: <number>

## Slide 38: Opportunity to connect more devices
  Boost number of mobile subscribers and devices connected to Internet (e.g. 700M now in China, 450M in India)
  “In the longer term, small wireless sensor devices embedded in objects, equipment and facilities are likely to be integrated with the Internet through wireless networks that will enable interconnectivity anywhere and at anytime”
  - OECD Policy Brief, June 2008
Notes: <number>

## Slide 39: QOS Classes in 16e
Table 1. IEEE 802.16e-2005 QoS classes Note: The base station and the subscriber station use a service flow with an appropriate QoS class (plus other parameters, such as bandwidth and delay) to ensure that application data receives QoS treatment appropriate to the application.
Service | Abbrev | Definition | Applications
Unsolicited Grant Service | UGS | Real-time data streams comprising fixed-size data packets issued at periodic intervals | T1/E1 transport
Extended Real-time Polling Service | ertPS | Real-time service flows that generate variable-sized data packets on a periodic basis | VoIP
Real-time Polling Service | rtPS | Real-time data streams comprising variable-sized data packets that are issued at periodic intervals | MPEG Video
Non-real-time Polling Service | nrtPS | Delay-tolerant data streams comprising variable-sized data packets for which a minimum data rate is required | FTP with guaranteed minimum throughput
Best Effort | BE | Data streams for which no minimum service level is required and therefore may be handled on a space-available basis | HTTP
Notes: <number>