## Slide 1
  Distributed antenna system for future 802.16
IEEE 802.16 Presentation Submission Template (Rev. 9)
Document Number:
  IEEE C802.16-10/0018
Date Submitted:
  2010-03-15
Source:
  Jiwon Kang , Bin-Chul Ihm, Wookbong Lee E-mail: {jw.kang, bc.ihm, wookbong.lee}@lge.com
  LG Electronics
Venue:
  Orlando, FL, USA
Base Contribution:
  None
Purpose:
  For discussion in the Project Planning Committee
Notice:
  This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein.
Release:
  The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16.
Patent Policy:
  The contributor is familiar with the IEEE-SA Patent Policy and Procedures:
      <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>.
  Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat >.

## Slide 2: Distributed Antenna System for Future 802.16
Notes: <number>

## Slide 3: Agenda
Introduction
Definition and Benefits
Applications
Expected Performance Enhancement
What to Do in Standard
Conclusions
Notes: <number>

## Slide 4: Introduction
  Demand for high data rate service anytime and anywhere
    Wireless network data usage demand is expected to grow by 5x - 20x in next 5-10 years
    High data rate such as mobile video becomes more important
    Number of connected user devices and machines keeps increasing exponentially
  Approaches for the goal
    More Spectrum – Carrier aggregation, Heterogeneous network, Multi-tier network
    Cooperative strategy – Client cooperation, Network MIMO
    Higher dimensional system – Higher order MIMO, Distributed Antenna System
  What is “distributed antenna system” and its advantage?
Notes: <number>

## Slide 5: Definition
A distributed antenna system or DAS is a network of spatially separated antennas called “nodes” connected to a common source via a transport medium that provides wireless service within a geographic area or structure. [1]
Centralized Antenna System (CAS)
Distributed Antenna System (DAS)
Macrocell BS
Antenna node
Macrocell BS
Notes: <number>

## Slide 6: Benefits of DAS
Extended coverage
  By installing antenna nodes near users, dead spots are removed and more stable connection is guaranteed. Also, DAS is one of the easiest way to extend cell coverage.
Increased energy efficiency
  Due to the reduced path loss and high quality line-of-sight connection between BS and MS, the power efficiency is increased at both uplink and downlink.
    Reduced power consumption of BS in downlink: ‘Green radio’
      If a given area is covered by N distributed antenna elements rather than a single antenna, then the total radiated power is reduced by approximately a factor N1-a/2 where a simple power law path loss model with path loss exponent a is assumed[2].
    Reduced power consumption of MS in uplink: ‘Longer battery life’
Notes: <number>

## Slide 7: Applications of DAS
Indoor DAS
  DAS has been installed at diverse in-building applications such as airport, hospital, convention center to extend coverage of femto/micro/picocell BS
Outdoor DAS
  DAS can be a viable complement to traditional macro-cell sites and a solution to the deployment of wireless services in challenging environments [3].
Outdoor DAS installation: Extenet systems, Inc.
(Bloomfield, Michigan, USA)
Notes: <number>

## Slide 8: Outdoor Applications
WiMAX train field trial [4]
  Application of 802.16e to Taiwan High Speed Rail Bullet train system. (~300km/h)
  Radio-over-Fiber distributed antenna system was developed to handle the critical issues of handover and coverage increment.
Traditional area coverage approach
Radio-over-fiber distributed antenna system approach
Notes: <number>

## Slide 9: Outdoor Applications
Deploying DAS on campus [5]
  More capacity and consistent connections are required for students who want wireless communication anywhere in campus for information, entertainment and etc
  Distributed antenna system with reasonable cost is deployed at several campuses like the university of Texas at Austin and university of Michigan.
Notes: <number>

## Slide 10: Evolution of DAS
DAS has been deployed for coverage extension. Besides the coverage benefits, we need to focus on the capacity benefit of DAS. Theoretically, DAS increases average link capacity by approximately 2x using simple antenna selection [6].
In order to enhance system capacity further, DAS should support the transmission of independent data stream per antenna node.
Macrocell BS
Macrocell BS
Replicas from entire antenna nodes
Independent data stream per antenna node
Notes: <number>

## Slide 11: Expected Performance Enhancement
    Contrary to the conventional applications, additional scheduling effort to reap the gain from distributed antenna system is introduced based on antenna selection by users.
      Independent data streams are transmitted at each antenna node.
    SFBC comparison in CAS and DAS
Simulation environment
      ISD: 500m
      Channel: UMa
      24MS/cell
Centralized antenna system
      3 sector/cell
      Directional antennas per sector
      Tx Power per sector, Psector = 46dBm
        Pcell = 50.7dBm
      Antenna gain = 17dBi
      4x2 precoded SFBC in DRU
Distributed antenna system
      8 nodes/1 cell
      All node have two omni antennas
      Total Tx Power, Pcell = 50.7dBm
      Antenna gain: 0dBi
      2x2 SFBC
Notes: <number>

## Slide 12: Advanced network architecture
One possible way of upgrading legacy CAS is to link the BS with remote antenna nodes via fiber optic cables so that the system is evolved into a DAS system.
Advanced features such as relay and femtocell can be overlaid on DAS as on CAS.
Relay Station
Femtocell
:Wireless connection
DAS evolved from CAS with other advanced technologies
Remote antenna node
Notes: <number>

## Slide 13: What to Do in Standard
Challenges & Requirements
  Antenna selection & channel measurement
  Multiple antenna node cooperation
  Mobility management across antenna nodes within a cell
  Interference management among antenna nodes
  Uplink power control with multiple antenna nodes
Notes: <number>

## Slide 14: Conclusions
Distributed antenna system can provide significantly higher throughput than centralized antenna system thanks to more often LOS cases and reduced path loss between antenna node and user device at reasonable cost.
Distributed antenna system should be considered for future 802.16 project in order to achieve very high throughput of 1Gbps~5Gbps.
To enjoy the advantages of distributed antenna system, standard should support various PHY and MAC issues.
Notes: <number>

## Slide 15: References
[1] www.wikipedia.com
[2] P. Chow, A. Karim, V. Fung, and C. Dietrich, “Performance advantages of distributed antennas in indoor wireless communication systems”, IEEE VTC, pp.1522-1526, 1994.
[3] www.thedasforum.org
[4] B. Chow, M.-L. Yee, M. Sauer, and A. Ng’Oma, “Radio-over-fiber distributed antenna system for WiMAX bullet train field trial,” Mobile WiMAX Symposium, pp.98-101, 2009
[5] www.thedasforum.org, “Campus Solutions for Next Generation Wireless Services”, The DAS Forum, 2009
[6] W. Choi and J. G. Andrews, “Downlink performance and capacity of distributed antenna systems in a multicell environment,” IEEE Trans. Wireless Comm., vol. 6, pp. 69–73, Jan. 2007.
Notes: <number>