| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Support of the Secondary Connection |
| Date Submitted | 2011-03-06 |
| Source(s) | Ronald Mao Huawei Technologies | E-mail: rmao@huawei.com |
| Re: | Call for contributions for 802.16n AWD |
| Abstract | This contribution proposes an amendment text in supporting a secondary communication path between the HR-MS and the HR-BS |
| Purpose | To be adopted by 802.16n |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Copyright Policy | The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Support of the Secondary Connection

Ronald Mao

Huawei Technologies

Introduction

In advanced metering such as Smart Grid, it is expected that under normal operations the majority of traffic from/to the MS will be regular as opposed to being ad-hoc in nature. This deterministic type of behavior allows for optimizing the operation of the mobile station (MS) in that the MS can be scheduled to connect or re-connect to the network only at specific time instances and only for a limited period of time. Such time controlled operation means better air interface utilization, reduced interference, conserved network resources, and possibly increased battery life, etc. However, a limitation with time controlled operation is that as the MS is not monitoring the air interface outside its pre-defined connection interval, the network cannot contact the MS outside of this interval. This contribution proposes a solution to mitigate this problem by allowing the network to alternatively send a notification to a neighboring MS that is currently in a connected state, and then have that MS use the secondary connection to relay the notification to the target MS.

Proposed Text

Data delivery to a disconnected MS

In the case that there is a secondary connection between the target MS and its neighboring MS, the base station (BS) may utilize the communication path on the secondary connection to initiate a data delivery to the target MS when the target MS is not connected to the BS. This procedure is illustrated in Figure 1.

Figure 1: Activate a disconnected MS over secondary communication path

As the figure illustrates, to deliver data to a target MS (MS1) currently disconnected from the BS, the BS sends a notification to the neighboring MS (MS2), which in turn forwards such notification to the target MS over the secondary communication path. Upon receipt of this notification the target MS connects to the BS and receives any pending messages from the BS.

The secondary connection may be a wireless access connection supports direct P2P communication over an unlicensed spectrum or a wired connection over power lines. In either case, the MS continuously monitors the secondary connection. For security concerns, only a notification is forwarded from the BS to have the target MS establish a connection with the BS. The neighboring MS shall not relay actual data via the secondary connection.

The data delivery described here relies on the availability of an MS in connected state and the existence of a secondary connection between this MS and the MS for which the indication is to be sent. In the absence of these conditions, the BS will buffer the data until such period that either the target MS is connected to the network or an alternate MS within reach of the desired MS enters into a connected state. To allow the BS to identify a suitable relaying MS, topology information regarding MS secondary connectivity is available at the BS. The topology can be configured at BS through operator network management procedures. Alternatively, this information can be stored on the core network and transferred to the BS during notification delivery.