## Slide 1: Service Requirement
Minsung, Kim
Korea Telecom
Jun 9th

## Slide 2
Main Service
  Presence Service
  SMS & MMS
  1:1 or 1:N Conversation or Conference Service
  File Transfer Service
Delay: Max.150ms (Video/Voice) ; Max.400ms (Text)
BER: Max.10e-4 (Video/Voice) ; Max.10e-5 (Text)
; Max.10e-6 (File Transfer)
Session Level Seamless HO
Power Saving Mode Support
Messaging Service

## Slide 3
Main Service
  1:1 or 1:N Video/Voice Conservation Service
  Instant Voice Transmission Service for Specific Group
  Presence Service
  Multimedia Date Transmission Service
Delay: Max.150ms (Video/Voice)
BER: Max.10e-4 (Video/Voice)
Session Level Seamless HO
Power Saving Mode Support
Push To Talk (PTT) Service

## Slide 4
Main Service
  Music & Music Video Streaming
  Real-time Audio/Video Broadcast Service
Delay: Max.150ms (Buffer Can Be Used)
BER: Max.10e-5
IP Multicast support
Session Level Seamless HO
Media Streaming Service

## Slide 5
Main Service
  Network Storage File Upload / Download & Searching Service
  Folder Sharing Service
Delay: Not Critical
BER: If Error Exists, Retransmission Is Mandatory (Max.10e-6)
Network Storage Service

## Slide 6
Main Service
  Online Real-time Game Service
  Interactive Real-time Communication Among Players
Delay: Max.100ms or Less
BER: Max.10e-6
; Retransmission May Be Meaningless Because of Delay Constraints
Session Level Seamless HO
Interactive Game Service

## Slide 7
0%
Packet Loss
Command/ control
(egTelnet, Interactive
games)
Conversational
voice and video
Voice/video
messaging
Streaming
audio/video
Transactions
(eg E-commerce,
Web-browsing, E-mail access)
Messaging, Downloads
(eg FTP,
still image)
Fax
Background
(eg Usenet)
5%
100 msec
1 sec
10 sec
100 sec
Zero
loss
Delay
ITU-T G.1010