## Slide 1: PINGPONG Criteria
Jungje Son, Changhoi Koo
Samsung Electronics

## Slide 2: PINGPONG Circumstance

## Slide 3: Timing diagram for HO
After actual HO starts, if the CINR value of target BS remains below PINGPONG threshold in comparison with CINR measured at actual HO start, MSS consider that it should return to serving BS and it transmits PINGPONG_Report Message.

## Slide 4: Proposed Text changes
Add the parameter in SBC-RSP at TLV field.
  PINGPONG threshold - a level in dB, by which the target BS is lower than the one measured before for an HO to return to serving BS. This value shall be less than Hysterisis threshold.
Add the below text at the end of line 47, page 47.
After actual HO start, if the CINR value of target BS remains below PINGPONG threshold in comparison with CINR measured at actual HO start, MSS recognizes that ping pong situation has occurred and it should return to serving BS.