| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Multiple Interleaved Legacy and New TDD Time Zones |
| Date Submitted | May 13, 2008 |
| Source(s) | Shailender Timiri Sassan Ahmadi Intel Corp | E-mail: shailender.b.timiri@intel.com sassan.ahmadi@intel.com *<http://standards.ieee.org/faqs/affiliationFAQ.html> |
| Re: | Call for contributions on IEEE 802.16m System Description Document IEEE 802.16m Frame Structure |
| Abstract | This contribution proposes a TDD time zone structure for legacy support that allows for flexible per-frame allocations for legacy and new zones while fixing the location and periodicity of the start of the new super-frames. |
| Purpose | To be discussed and adopted by TGm for incorporation in the IEEE 802.16m |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Multiple Interleaved Legacy and New TDD Time Zones

Shailender Timiri, Sassan Ahmadi

Intel Corp

# Background

The current IEEE 802.16m super-frame description in C80216m-08_003r1 requires legacy support in TDD support where the downlink legacy and new zones can be partitioned dynamically on a per-frame basis. Figure 11.4-5 from C80216m-08_003r1 describes this scenario and is reproduced below.

As a consequence, the start of the new zones within a frame can vary on a per-frame-basis and therefore, the periodicity of the new preamble (assumed to be at the start of the new DL zone within a frame) is no longer a fixed quantity. This is illustrated in Fig 2, where the new preamble appears in sub-frame 3 in one frame and in sub-frame 2 in the following frame.

# Proposal

To avoid the problem described above while still maintaining the ability to divide resources flexibly between the legacy and new devices, it is proposed that multiple TDD time zones with alternating legacy and new zones be permitted. This is illustrated in Fig 3, where the new preamble appears at a fixed location and at regular 5ms intervals while allowing for flexible per-frame resource partitioning between legacy and new devices.

Proposed Text for SDD (to replace Figure 11.4-5):

----------------Start of the proposed text------------------------------

For legacy support, multiple TDD time zones with alternating legacy and new zones may be employed. This will enable the new preamble’s location and periodicity to be fixed while allowing for the flexible per-frame resource partitioning between legacy and new devices.

Figure 11.4-5 Time Zones in TDD mode

----------------End of the proposed text------------------------------

# Text boxes

Figure 1. Proposed Description of Legacy and New Time Zones in TDD mode

Figure 1. Current Description of Legacy and New Time Zones in TDD mode

Figure 2. Issue with Current Description of Legacy and New Time Zones in TDD mode