| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Interference Measurement Mechanisms for IEEE 802.16m |
| Date Submitted | 2008-07-07 |
| Source(s) | I-Kang Fu, Yih-Shen Chen, Kelvin Chou, Dora Chen, Stanley Hsu, Paul Cheng MediaTek Inc. No.1, Dusing Rd. 1, Hsinchu Science Park, Hsinchu, Taiwan, R.O.C. | IK.Fu@mediatek.com |
| Re: | IEEE 802.16m-08/024, “Call for Comments and Contributions on Project 802.16m System Description Document (SDD),” Interference Mitigation |
| Abstract | This contribution proposes the interference measurement mechanisms to support various interference management functions in IEEE 802.16m |
| Purpose | Propose interference measurement mechanisms to enable various interference management functions by providing the information on interference characteristics |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Interference Measurement Mechanisms for IEEE 802.16m

I-Kang Fu, Yih-Shen Chen, Kelvin Chou, Dora Chen, Stanley Hsu, Paul Cheng

MediaTek Inc.

- Introduction

Fractional Frequency Reuse (FFR) is expected to be a mandatory feature of IEEE 802.16m based mobile WiMAX 2.0 system, but the current measurement schemes defined in 16e can not satisfy the requirement by FFR. This contribution aims to investigate the possible measurement schemes which can provide the necessary information on interference characteristics for better FFR operation and system performances. Note that the following discussion will base on the background introduction in IEEE C802.16m-08/558.

In C802.16m-08/558, the introduction shows that the system may apply different frequency reuse factor (1/K) for each FFR zone. So that the interfering sources when serving the MSs in different zone will also be different like Fig.1.

Fig.1 The interfering source will be different for the MS when served by different FFR zone

This will result in one problem, i.e. the received interference level for each MS will be different from one zone to another, which may not necessarily positive correlated to frequency reuse factor due to shadow fading. That means, MSs are expected to experience lower interference level when served by the FFR zone with higher K. However, this may not always be true because the MS may unfortunately have LOS (Line-Of-Sight) condition with specific interfering source when K=7 (take Fig.1 for example) but having NLOS (Non-Line-Of-Sight) to each interfering source when K=4. Therefore, scheduling the MS into different FFR zone according to the RSSI or CINR over preamble measurement may result in wrong decision because the preamble cannot reflect the real interfering situation in each FFR zone.

In addition, the real interfering situation is also difficult be reflected by CQI report. Because the BS still cannot pre-estimate the real interfering situation before scheduling the MS into specific zone. Therefore, the interference measurement over each FFR zone can provide much more accurate information on interference statistics for better decision on network reconfiguration for FFR or for possible interference mitigation techniques like beamforming.

- Possible Interference Measurement Mechanisms for Interference Management Support

- Solicited/Unsolicited Interference Measurement Mechanisms

Follow the ideas of scanning mechanism, the interference measurement can also be solicited or unsolicited. The basic idea is explained in Fig.2.

Fig.2 Solicited/Unsolicited interference measurement

- Autonomous Interference Measurement Mechanism

Follow the idea of autonomous preamble scanning mechanism defined in IEEE 802.16e; the autonomous interference measurement mechanism is another feasible mechanism for IEEE 802.16m.

Fig. 3 Autonomous interference measurement

- Text Proposal

--------------------------------------------------------Start of the Text------------------------------------------------------------

[Add the following text into IEEE 802.16m-08/003r3]

X. Interference Measurement to Support Interference Management

X.1 Solicited/Unsolicited Interference Measurement Mechanism

X.2 Autonomous Interference Measurement Mechanism

---------------------------------------------------------End of the Text------------------------------------------------------------