| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Modification to DL non-adaptive precoding in OL MIMO region |
| Date Submitted | 2009-07-06 |
| Source(s) | Kiran Kuchi, J Klutto Milleth, Vinod R, Divagar , Padmanabhan M S, Bhaskar R ¦ CEWiT, India | E-mail: kkuchi@cewit.org.in (+91 9962045186) klutto@cewit.org.in (+91 9444107970) |
| Re: | Call for Comments on IEEE 802.16m-09/0010r2 IEEE 802.16m Amendment text/Area: Chapter 15.3.7.2.3.2 (DL-MIMO) |
| Abstract | Amendment text for Non-adaptive precoding in OL MIMO region |
| Purpose | For inclusion in AWD |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Modification to DL non-adaptive precoding in OL MIMO region

Kiran Kuchi, J Klutto Milleth, Vinod R, Divagar , Padmanabhan M, Bhaskar R

CEWiT, India

# Introduction:

In OL MIMO region, N1 cycling is used for subbands based on logical subband index and N2 cycling is used for mini bands as well as DRU permutations based in logical PRU index

## ……………………..Start of Text……………………………………………………….

Non-adaptive precoding inside the OL region

For subband CRU permutation, the non-adaptive precoding, the matrix W(k) applied on subcarrier k in subband with logical index       is selected as the codeword of index i in the open-loop codebook subset of rank MaxMt, where i is given by

(205)

For DRU and miniband CRU permutation, the Nt×1 precoding matrix W(k) applied on subcarrier k in PRU with logical index  in subframe number t is selected as the codeword of index i in the open-loop codebook subset of MaxMt,, where i is given by

(206)

## ……………………..End of Text……………………………………………………….