| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Corrections to Tables 693 and 694 (DL 2Tx codebook) |
| Date Submitted | 2009-07-06 |
| Source(s) | David Mazzarese, Hokyu Choi, Heewon Kang Samsung Electronics | d.mazzarese@samsung.com *<http://standards.ieee.org/faqs/affiliationFAQ.html> |
| Re: | Category: AWD comments / Area: Chapter 15.3.7 (DL-MIMO) |
| Abstract | Implementation issue relative to comment 286 in database 80216m-09_0023r3, where contribution C80216m-09/0944r1 was accepted. |
| Purpose | To be discussed and adopted by TGm for the 802.16m amendment |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Corrections to Tables 693 and 694 (DL 2Tx codebook)

David Mazzarese et Al.

Samsung Electronics

# Introduction

This is an editorial implementation issue relative to comment 286 in database 80216m-09_0023r3, where contribution C80216m-09/0944r1 was accepted.

There are sign errors on the coefficients of the codebook in Tables 693 and 694. One half row is also missing in Table 694.

# References

[1] IEEE 802.16m-09/0010r2, “IEEE 802.16m Amendment Working Document (AWD)”, 2009-06-31.

[2] IEEE 802.16m-07/002r8, “802.16m System Requirements”, 2009-01-15.

[3] IEEE 802.16m-08/003r9a, “The Draft IEEE 802.16m System Description Document”, 2009-05-31.

[4] IEEE 802.16m-08/004r5, “The IEEE 802.16m Evaluation Methodology Document”, 2009-01-15.

[5] IEEE 802.16m-08/043, “Style guide for writing the IEEE 802.16m amendment”, 2008-09-18.

# Text proposal for inclusion in the 802.16m amendment

<Modify Tables 693 and 694 on page 245 as follows. The positions of erroneous values in the AWD have been highlighted in yellow for clarity.>

-------------------------------  Text Start  ---------------------------------------------------

Table 693 – C(2,1,3)

| Binary Index | m |  |
| --- | --- | --- |
|  |  | c1 | c2 |
| 000 | 0 | 0.7071 | -0.7071 |
| 001 | 1 | 0.7071 | -0.5000 - 0.5000i |
| 010 | 2 | 0.7071 | - 0.7071i |
| 011 | 3 | 0.7071 | 0.5000 - 0.5000i |
| 100 | 4 | 0.7071 | 0.7071 |
| 101 | 5 | 0.7071 | 0.5000 + 0.5000i |
| 110 | 6 | 0.7071 | 0.7071i |
| 111 | +7 | 0.7071 | -0.5000 + 0.5000i |

Table 694 – C(2,2,3)

| Binary Index | m |  |
| --- | --- | --- |
|  |  | c11 c21 | c12 c22 |
| 000 | 0 | 0.7071 0.7071 | -0.7071 0.7071 |
| 001 | 1 | 0.7071 0.7071 | -0.5000 - 0.5000i 0.5000 + 0.5000i |
| 010 | 2 | 0.7071 0.7071 | - 0.7071i 0.7071i |
| 011 | 3 | 0.7071 0.7071 | 0.5000 - 0.5000i -0.5000 + 0.5000i |
| 100~111 | 4~7 | - | - |

-------------------------------  Text End  ---------------------------------------------------