| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | SON trigger events for self optimizing Femto BS (15.4) |
| Date Submitted | 2009-08-28 |
| Source(s) | Sok-Hyong Kim, Yong-Sung Kim, Joo-Young Baek, Young-Joo Suh POSTECH | shkimm@postech.ac.kr, freekys@postech.ac.kr nalsunia@postech.ac.kr yjsuh@postech.ac.kr |
| Re: | “P802.16m/D1 SON,” in response to the TGm Call for Contributions on Project 802.16m Amendment Content, IEEE 802.16m-09/0037 |
| Abstract | This contribution discusses SON trigger events for self optimizing Femto BS |
| Purpose | To be discussed and adopted by TGm for the 802.16m amendment |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

SON trigger events for self optimizing Femto BS (SON)

Sok-Hyong Kim, Yong-Sung Kim, Joo-Young Baek, and Young-Joo Suh

POSTECH

# Introduction

This contribution proposes Self Organizing Network (SON) trigger events for self optimizing Femto BS.

A femto BS is a low-power base station that uses the fixed broadband connection for backhaul. Network Access Provider (NAP) is in charge of femto BS management. In femto BSs, there are many dynamic changeable factors such as channel conditions, interference, user distribution, traffic load, etc. To provide an efficient network access, femto BSs handle radio transmission parameters according to these dynamic changeable factors. The method for handling radio transmission parameters is self optimization. Thus, Femto BSs have Self Organizing Network (SON) function to achieve the self optimization. In addition, WiMAX Forum document “IEEE 802.16m System Description Document [Draft]“ states the self optimization in section 16.2 [1].

For the efficient self optimization, it is important to consider SON trigger events that execute SON functions of femto BSs. A femto BS receives measurement information (e.g., channel condition and interference) from associated MSs and it checks whether it is necessary to re-configure its radio transmission parameters itself or not. If the femto BS determines the necessity of self optimization, it generates a SON trigger event itself, and then the SON function of the femto BS executes to find optimal values of radio transmission parameters. The method for finding optimal values of radio transmission parameters is FFS. If necessary, the femto BS can send control messages to associated MSs to notify the changed radio transmission parameters.

The SON trigger events are generated by two methods: periodic based method and threshold based method. The periodic based method generates SON trigger events periodically and the threshold based method generates SON trigger events when values of radio transmission parameters exceed pre-defined thresholds. For SON trigger event of each transmission parameter, periodic based method and threshold based method can be used, according to characteristics of radio transmission parameters.

# References

[1] IEEE 802.16m-09/0034, “IEEE 802.16m System Description Document (SDD)”, Jul. 27, 2009.

# Proposed text

[Insert subclause into the 802.16m Amendment Draft Standard as indicated:]

### 15.4.x SON trigger events for self optimizing Femto BS

In a femto BS, based on the reported SON measurements from associated MSs, Self Organizing Network (SON) trigger events can be generated by the femto BS itself to execute SON function in the femto BS. When a SON function of the femto BS receives the generated SON triggers, it determines that it is necessary to re-configure radio its transmission parameters. In the SON function, the method for finding optimal values of radio transmission parameters is FFS. If necessary, the femto BS can send control messages to associated MSs to notify the changed radio transmission parameters.

The SON trigger events are generated by two methods: periodic based method and threshold based method. The periodic based method generates SON trigger events periodically and the threshold based method generates SON trigger events when values of radio transmission parameters exceed pre-defined thresholds. According to the characteristics of radio transmission parameters, the SON trigger event are generated by periodic based method or threshold based method. The classification of radio transmission parameters according to two methods is FFS.