| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Proposed Changes to Drops during HO (15.2.5.10.7) |
| Date Submitted | 2009-08-28 |
| Source(s) | Kelvin Chou, Yih-Shen Chen, I-Kang Fu and Paul Cheng MediaTek Inc. | Kelvin.Chou@mediatek.com |
| Re: | Letter Ballot #30 on the Draft Amendment (IEEE P802.16m/D1) |
| Abstract | This contribution proposes some clarification to the MCHO section |
| Purpose | Propose to be discussed and adopted by TGm for the 802.16m Amendment |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Proposed Changes to Drops during HO (15.2.5.10.7)

Kelvin Chou, Yih-Shen Chen, I-Kang Fu and Paul Cheng

MediaTek Inc.

- Proposed Text

{Apply the following text modification to P802.16m/D1, Section 15.2.5.10.7 at page 102, line 35 as follows:}
---------------------------------------------------------- Text Start ---------------------------------------------------------------

15.2.57.10.7 Drops during HO

A drop is defined as the situation where an AMS has stopped communication with its serving ABS (either in the DL or in the UL) before the normal HO procedures with the serving ABS has been completed.

An AMS can detect a drop by its failure to demodulate the DL, or by exceeding the AAI_RNG-REQ retries limit allowed for the periodic ranging mechanism. An ABS can detect a drop when the Number of retries limit allowed on inviting ranging requests for the periodic ranging mechanism is exceeded.

When the AMS has detected a drop during network reentry with a target ABS, the AMS follows the procedures defined below to recover its connection:

- If HO_Reentry_Mode = 1 and Disconnect Time has not expired, the AMS sends AAI_HO-IND message with HO Event Code = 0b11 to cancel HO. When AMS transmits and serving ABS receives AAI_HO-IND message with HO Event Code = 0b11 within Disconnect Time, regardless of AMS attempt at HO, the AMS and serving ABS shall continue normal communication. In case of HO Reentry_Interleaving Interval > 0, the serving ABS cancels HO Reentry Iteration of the AMS.

- If HO_Reentry_Mode = 1 and Disconnect Time has expired, or HO_Reentry_Mode = 0, the AMS follows the procedures defined below to recover its connection:

  - If Resource Retain Time has not expired, the AMS sends AAI_HO-IND message with HO Event Code = 0b11 (HO cancel). When AMS transmits and serving ABS receives AAI_HO-IND message with HO Event Code = 0b11 within Resource Retain Time, regardless of AMS attempt at HO, the AMS and serving ABS shall continue normal communication.

  - If Resource Retain Time has expired, the AMS attempts network reentry with its preferred target ABS as through cell reselection, which includes performing network reentry at the serving ABS.

When the serving ABS has detected a drop, it shall react as if a AAI_HO-IND message has been received with HO Event Code = 0b10 indicating AMS unable to stay connected to serving ABS until expiration of disconnect time.

----------------------------------------------------------- Text End ---------------------------------------------------------------