| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Proposed Change to Emergency Service Flow (15.3.7.4) |
| Date Submitted | 2009-08-29 |
| Source(s) | Hyunjeong Kang, Jaehyuk Jang, Jungje Son Samsung Electronics | hyunjeong.kang@samsung.com |
| Re: | IEEE 802.16m-09/0044, “IEEE 802.16 Working Group Letter Ballot #30: Announcement” |
| Abstract | The contribution proposes a clarification on texts of emergency service flow in 16m/D1. |
| Purpose | To be discussed and adopted by TGm for 802.16m/D2 |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Proposed Change to Emergency Service Flow (15.3.7.4)

Hyunjeong Kang, Jaehyuk Jang, Jungje Son

Samsung Electronics

# Introduction

According to section 15.3.7.6 in 16m/D1[1] which describes emergency service operation during the connected state, if there is no pre-defined emergency service flow in connected state, then emergency service flow setup procedure is initiated through an emergency service notification in the AAI_DSA-REQ message. But in the general description on emergency service flow of section 15.3.7.4, an indicator in bandwidth request initiates the DSA procedure to setup emergency service flow.

AAI_DSA-REQ/RSP messages are used to establish a service flow, so the same messages can be used to setup a flow for emergency service if there is no pre-defined emergency service flow.

Therefore, we should fix a description of emergency service flow setup during connected state in section 15.3.7.4 to align with the emergency service flow setup procedure defined in 15.3.7.6.

Reference

[1] P802.16m/D1, Draft amendment to IEEE Standard for Local and metropolitan area networks Part 16: Air Interface for Broadband Wireless Access Systems, July 2009

# Suggested remedy

-------------------------------  Text Start  ---------------------------------------------------

[Modify the sentence from line 35 to line 37 on Page 162 in section 15.3.7.4 Emergency service flow:]

During the connected state, if an emergency FID is not pre-defined, the ABS shall allocate the emergency service FID through AAI_DSA-RSP upon receiving the emergency service indication in the AAI_DSA-REQ message bandwidth request.

[Add the following field into Table 704 on Page 93 of section 15.2.5.9:]

| Emergency Indication | 1 | Indicates the associated flow is used for emergency purposes. |
| --- | --- | --- |

-------------------------------  Text End  ---------------------------------------------------