| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Proposed text on Relay Support in IEEE 802.16m |
| Date Submitted | 2009-08-28 |
| Source(s) | Kaibin Zhang, Jimin Liu, Gang Shen Alcatel-Lucent Shanghai Bell Co., Ltd. | kaibin.zhang@alcatel-sbell.com.cn |
| Re: | IEEE 802.16m-09/0037, “Call for Comments and Contributions on Project 802.16m Amendment Content.” [AWD – Relay] |
| Abstract | This contribution . |
| Purpose | For member’s review and adoption into P802.16m Amendment Working Document (AWD) |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Proposed text on Relay Support in IEEE 802.16m

Kaibin Zhang, Jimin Liu, Gang Shen

Alcatel-Lucent Shanghai Bell Co., Ltd.

# Introduction

- Introduction

This contribution proposes a short overview section for the Relay support section in IEEE802.16m amendment. It is proposed that both transparent and non-transparent shall be supported.

- Text Proposal

Insert the following text in 802.16m-09_0010r2:

-------------------------------------------------Start of the Text-----------------------------------------------------

15.5 Support for Multi-hop Relay

15. 5.1 General description

Relaying is performed using a decode and forward paradigm in IEEE802.16m. The ABS and ARSs deployed within a sector operate using either time division duplexing (TDD) or frequency division duplexing (FDD) of DL and UL transmissions. An ARS operates in time-division transmit and receive (TTR) relaying mode.

ARSs may operate in transparent mode or non-transparent mode. The ABS shall support the co-existence of the transparent and the non-transparent ARSs.

Non-transparent ARS transmits PREAMBLE, SFH and A-MAP. Transparent ARS does not have its own PREAMBLE, SFH and A-MAP transmitted to the subordinate AMS, and is limited to the scenario where the superordinate station is a non-transparent ARS or an ABS. The subordinate AMS shall get PREAMBLE, SFH and A-MAP from the transparent ARS’s superordinate station directly.

A non-transparent ARS can operate in both centralized and distributed scheduling mode, while a transparent ARS can only operate in centralized scheduling mode. In centralized scheduling, an ABS schedules the radio resource in its cell, and AMS can get the A-MAP from the ABS directly. In distributed scheduling, ARS may schedule the radio resources of its subordinate link within the radio resources assigned by the superordinate station (ABS or non-transparent ARS), while the superordinate station may exercise additional control over the scheduling of its subordinate ARSs.

Cooperative relaying is a technique whereby either the ABS and one or more ARSs, or multiple ARSs cooperatively transmit or receive data to/from one subordinate station or multiple subordinate stations. Cooperative relaying may also enable multiple transmitting/receiving stations to partner in sharing their antennas to create a virtual antenna array. The ARSs may transmit data to the superordinate and subordinate station(s) using the same LRU. Both transparent ARS and non-transparent ARSs can support the cooperative relaying.

---------------------------------------------------End of the Text-----------------------------------------------------