| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Limitations on burst allocations to an AMS |
| Date Submitted | 2009-11-09 |
| Source(s) | Tom Harel Jong-Kae (JK) Fwu Amir Rubin Intel corp. | Voice: +972-54-7884132 E-mail: tom.harel@intel.com |
| Re: | Comments on IEEE P802.16m/D2 for IEEE 802.16 Working Group Letter Ballot Recirc #30a |
| Abstract | The contribution proposes limitation on allocations to an AMS |
| Purpose | To be discussed and adopted by the IEEE 802.16 Working Group |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Limitations on burst allocations to an AMS

Tom Harel, Jong-Kae (JK) Fwu, Amir Rubin

Intel corp.

# Background

Since the scheduler is part of the ABS, its decisions are naturally adapted to the ABS processing capabilities. For the AMS it is desired to limit the possible allocation scenarios to avoid implementation complexity without substantial gain.

In WiMAX-1.0 these limitations were mainly stated in the WiMAX profile. However, it is better to define it in the IEEE standard, since this kind of restrictions is required for implementation, and without it the standard is not self contained.

The proposed limitations are shown in the table below, with comparison to WiMAX-1.0 and LTE for reference. The limitations apply to the allocations for one AMS. For AMS that supports Multi-Carrier aggregation, the limitations are applicable for each carrier separately.

|  | Limit on | Proposed value | Rational | WiMAX 1.0 | LTE |
| --- | --- | --- | --- | --- | --- |
|  | Number DL data bursts in subframe(*) | ≤3 | 1 burst for broadcast transmission, a new burst and burst re-transmission (or otherwise 2 bursts for different QoS) | 5 per frame | 1 |
|  | Number of UL data bursts in subframe(**) | ≤2 | A new burst and a re-transmission (or otherwise Long TTI and default TTI) | 2 per frame | 1 |
|  | Number of A-A-MAP IEs for AMS per subframe(***) | ≤6 | Allocate 2-3 DL bursts, ~2 UL bursts and UL control channels |  | 4 |
|  | Sum of allocation sizes (in LRUs) of UL bursts that start in subframe (Default or Long TTI) | ≤# of LRUs in subframe | Long TTI isn’t intended to be used for allocating huge bursts, but for exploiting subchannelization gain (UL only) and opportunistic scheduling. | N/A | N/A |
|  | Number of UL Fast Feedback channels (SFBCH and PFBCH) in frame | ≤2 | All MIMO feedback modes can be supported by 1 SFBCH and 1 PFBCH | N/A | N/A |

(*) Includes unicast and broadcast (control and E-MBS), first transmission and HARQ re-transmissions, default TTI and any portion of Long TTI bursts. Doesn’t include control channels (A-MAP).

(**) Includes first transmission and HARQ re-transmissions, default TTI and any portion of Long TTI bursts. Doesn’t include UL control channels.

(***) Includes all of the STIDs that are required to be checked by the AMS (its STID, group ID of GRA and composite PA, Broadcast ID). For a segmentable IE (IE that occupies more than 1 MLRU in QPSK ½), each segment is counted as 1 IE.

# References

[1] P802.16m/D2: Advanced Air Interface

# Proposed text change

--------------------------------------------Begin Proposed Text Change 1----------------------------------------------------

<< Add the following text to section 15.3.3.1 Basic frame structure, pp 266, line 29>>

A data burst shall occupy either one AAI subframe (i.e. the default TTI transmission) or contiguous multiple AAI subframes (i.e. the long TTI transmission). The long TTI in FDD shall be 4 AAI subframes for both DL and UL. The long TTI in TDD shall be the whole DL (UL) AAI subframes for DL (UL) in a frame.

An AMS shall be capable to receive up to 3 data bursts per DL subframe (including broadcast, multicast and unicast transmissions) and transmit up to 2 data bursts per UL subframe.

Every superframe shall contain a superframe header (SFH). The SFH shall be located in the first DL AAI subframe of the superframe, and shall include broadcast channels.

--------------------------------------------End of Proposed Text Change 1----------------------------------------------------

--------------------------------------------Begin Proposed Text Change 2----------------------------------------------------

<< Add the following text to section 15.3.6.2.2.2 Assignment A-MAP, pp 335, line 8>>

All the unicast assignment A-MAP IEs intended for a particular AMS shall be transmitted in the same assignment A-MAP group. The DL/UL Basic Assignment A-MAP IEs are an example of unicast assignment A-MAP IEs. The number of A-MAP IEs intended for a particular AMS is less than or equal to 6, including unicast, broadcast and multicast IEs, in all of the A-MAP groups in the subframe.

--------------------------------------------End of Proposed Text Change 2----------------------------------------------------

--------------------------------------------Begin Proposed Text Change 3----------------------------------------------------

<< Add the following text to section 15.3.6.5.2.3 UL basic assignment A-MAP IE, pp 366, line 21>>

The Resource Index field in the UL Basic Assignment A-MAP IE is interpreted as in the DL Basic Assignment A-MAP IE, with 'DL' specific terminology replaced by 'UL' equivalents.

Long TTI Indication: Indicator to signal allocation spans multiple AAI subframes in time. The sum of sizes of bursts that are allocated to a specific AMS and start at a specific subframe shall not exceed the number of LRUs in the subframe.

--------------------------------------------End of Proposed Text Change 3----------------------------------------------------

--------------------------------------------Begin Proposed Text Change 4----------------------------------------------------

<< Add the following text to section 15.3.9.3.1 Fast feedback control channel, pp 522, line 31>>

Fast feedback allocations to an AMS can be periodic and the allocations are configurable. The number of UL Fast Feedback channels allocated to an AMS per frame is less than or equal to two (with one SFBCH and one PFBCH).

--------------------------------------------End of Proposed Text Change 4----------------------------------------------------