| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Proposal on PMI Coordination Support with Relays |
| Date Submitted | 2009-11-06 |
| Source(s) | Honggang Li Sydir Jerry Davydov Alexei Intel Corporation | Email: honggang.li@intel.com |
| Re: | Call for Contributions on Project 802.16m Amendment Content: IEEE802.16m-09/0037 |
| Abstract | The contribution proposes the text changes to enable interference mitigation techniques in presence of a relay station’s operation. |
| Purpose | To be discussed and adopted by TGm for P802.16m/D2 Amendment text |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

Proposal on PMI Coordination Support with Relays

Honggang Li, Sydir Jerry, Davydov Alexei

Intel Corporation

# Introduction

This contribution proposes modifications to the P802.16m/D2 text that enable Relay stations be consistent with the PMI-based interference mitigation mechanisms currently defined in P802.16m/D2 [1]. Currently [1] specifies several PMI-based interference mitigation algorithms including PMI recommendation and PMI restriction. Similar mechanisms can be implemented between the ABS and the set of ARSs in the same cell and neighboring cells.

# Multi BS/RS PMI coordination with Relays

The deployment of relays will introduce more interference than non-relay scenario as well as the improvement of coverage and throughput, PMI coordination with Relays can be a complement to inter-BS coordination and both intra-cell and inter-cell coordination can be integrated together to benefit from the interference mitigation with Relays. Most definition and description in section 15.3.14.3 can be reused for relay-related PMI coordination, considering the specials of PMI coordination with relays, some modifications should be considered in AWD texts.

- Types of multi-BS/RS coordination with relays

Considering both inter-cell and intra-cell PMI coordination with relays, there are five types of PMI coordination as shown in table XXX. In current D1 texts, type C is supported, we propose besides type C, coordination type A, B, D, E should be taken as supportive types of Multi BS/RS PMI coordination with Relays in the AWD texts.

Table 1, types of multi-BS/RS coordination with relays

| Type | Coordination parties | Description |
| --- | --- | --- |
| A | ABS-ARS | The ABS and ARSs are deployed and coordinated in a same cell |
| B | ARS-(ABS)-ARS | The ARSs are deployed in a same cell and coordinated via the super-ordinate ABS in the same cell |
| C | ABS-ABS | Inter-BS coordination defined in D2 texts |
| D | ARS-(ABS)-ABS | Coordination between an ARS and neighboring ABS via the super-ordinate ABS in the same cell the ARS locates |
| E | ARS-(ABS)-(ABS)-ARS | Coordination between the ARSs deployed in neighboring cells via the respective super-ordinate ABSs |

Figure 1, types of multi BS/RS coordination

- PMI coordination with relays, down selection from Multi-BS interference mitigation

To simplify the implementation and save the control overhead, we propose only PMI recommendation and restriction should be supported in multi-BS/RS coordination with relays, CL-MD and Co-MIMO should not be supported.

- Proposed PMI coordination mechanism

Because there is no direct link between two RSs, the signaling exchanging between BS/RSs should be via the super-ordinate BS in air interface.

Figure 2, an example: signaling exchange in PMI coordination with relays within a sector

In BS/RS PMI coordination as shown in figure 2, AMS may initially send the feedback request message to the server ABS/ARS, the serving ABS/ARS allocates the channel to the AMS to feedback the PMI recommendation/restriction message of neighboring ABS/ARSs, and upon receiving feedback messages from multiple AMSs, an ABS/ARS should communicate with neighboring ABS/ARSs to coordinate the usage of PMIs via higher layer signaling.

Figure 3, control flow in PMI coordination with relays

# References

- IEEE P802.16m/D2, “Part 16: Air Interface for Fixed and Mobile Broadband Wireless Access Systems – DRAFT Amendment to IEEE Standard for Local and metropolitan area networks”

- IEEE 802.16m-09/0034, “IEEE 802.16m System Description Document”

- IEEE 802.16m-08/004r1, “IEEE 802.16m Evaluation Methodology”

# Text proposal

-------------------------------  Text Start  ---------------------------------------------------

[Insert clause 15.6.x at the end of clause 15.6 on line 48 of page 576]

15.6.x Multi-BS/RS MIMO techniques

ARSs may participate in the same capacity as ABSs in the multi-BS coordination schemes described in section 15.5. All procedures that apply to ABSs in section 15.5 may also apply to ARSs.

-------------------------------  Text End  ---------------------------------------------------