| Project | IEEE 802.16 Broadband Wireless Access Working Group <http://ieee802.org/16> |
| --- | --- |
| Title | Clean up AAI_HO-REQ and AAI_HO-CMD attributes |
| Date Submitted | 2010-07-09 |
| Source(s) | Joey Chou Xiangying Yang Intel | E-mail: joey.chou@intel.com |
| Re: | TGm AWD: |
| Abstract | This contribution proposes text to fix AAI_HO-REQ and AAI_HO-CMD issues |
| Purpose | Adopt proposed text. |
| Notice | This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.16. |
| Patent Policy | The contributor is familiar with the IEEE-SA Patent Policy and Procedures: <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>. Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat>. |

# Clean up AAI_HO-REQ and AAI_HO-CMD attributes

# Joey Chou, Xiangying Yang

# Intel

- Introduction

This contribution is intended to clean up AAI_HO-REQ and AAI_HO-CMD attributes.

- Proposed text

II.1 Proposed text 1

------------------------------------------------- Start of proposed text I--------------------------------------------------

16.2.3.10 AAI_HO-REQ

Table 690—AAI_HO-REQ

| M/O | Attributes/Array of attributes | Size (Bits) | Value/Note | Conditions |
| --- | --- | --- | --- | --- |
| O | N_New_ABS_Full | 488 | The number of neighboring ABSs to be that are identified by full 48 bit ABS ID to be considered for handover, which is 48 bit ABSID. | Present of full ABS ID is used |
| O | Neighbor_ABS_Index_Array [1..255] | Variable | List of neighbor ABS Index | Present when N_New_ABS_Index is not 0. |
| O | A) Neighbor_ABS_Index | 8 | ABS index corresponds to AAI_NBR-ADV. | Present Shall be included when N_New_ABS_Index is not 0. |
| O | Neighbor_ABS_ID_Array [1..255] | Variable | List of full neighbor ABS ID | Present when N_New_ABS_Full is not 0. |
| O | A) Neighbor_ABS_ID | 48 | Indicate the 48 bit ABS ID of the target ABS the MS intends to perform network reentry in case of either target ABS selection or none of suggested target ABS is reachable | Present Shall be included when N_New_BS_Full is not 0 |
| O | ABS CINR mean | 8 | Indicate the CINR mean measurement of a MS-preferred target ABS not in the list of HO command | Shall be included if Report Metric Bit #0 is set to 0 |
| O | ABS RSSI mean | 8 | Indicate the RSSI mean measurement of a MS-preferred target ABS not in the list of HO command | Shall be included if Report Metric Bit #1 is set to 1 |
| O | Relative delay | 8 | Indicate the relative delay measurement of a MS-preferred target ABS not in the list of HO command | Shall be included if Report Metric Bit #2 is set to 1 |

------------------------------------------------- End of proposed text I --------------------------------------------------

II.2 Proposed text 2

------------------------------------------------- Start of proposed text II--------------------------------------------------

16.2.3.11 AAI_HO-CMD

Table 691—AAI_HO-CMD

| M/O | Attributes/Array of attributes | Size (Bits) | Value/Note | Conditions |
| --- | --- | --- | --- | --- |
| O | Target ABS Array [0..255] | Variable | List of target ABS information | Present if target ABS is available |
| O | A) TargetBSID | 48 | 48 bit ABS ID of target ABS | Present Shall be included for each target ABS when Mode=0b00 |
| O | B) Preamable Index | 10 | IDCell information of target ABS | Present Shall be included for each target ABS when Mode=0b00 |
| O | C) FA Index | 86 | PHY carrier index of the target ABS | Present Shall be included for each target ABS when Mode=0b00 |
| O | D) Action Time | 8 | Mode=0b00 Action Time included in this message is the absolute frame number at the serving ABS. When CDMA_RNG_FLAG is set to 1, it shall be set to the frame where either a normal or dynamic ranging channel is present. | Present Shall be included for each target ABS when Mode=0b00 Shall be included when Mode = 0b01. |
| O | E) CDMA_RNG_FLAG | 1 | If CDMA_RNG_FLAG=0, CDMA based ranging shall be skipped. Otherwise, if set to 1, it indicates that ranging shall be done. This parameter shall be included for each target ABS when Mode=0b00.; It shall be included when Mode = 0b01. If CDMA_RNG_FLAG is set to 0, pre-assigned STID at the target BS shall be assigned. | Present Shall be included for each target ABS when Mode=0b00 |
| O | N_Preassigned_Carriers | 3 | Number of pre-assigned secondary carriers at the target ABS. A value of 0 means no secondary is pre-assigned. | Shall be included when Carrier Preassignment Indication = 1 |
| O | Pre-assigned secondary carrier information array[0..7] | variable | List of pre-assigned secondary carrier Carrier information of each pre-assigned secondary carrier, which includes: Carrier Status Bitmap: indicating whether this pre-assigned carrier will be activated immediately after HO procedure is done; Physical carrier index of pre-assigned secondary carriers; Logical carrier index, which is assigned implicitly in the order of Carrier information of each pre-assigned secondary carriers. | Present if Pre-assigned secondary carrier is present Shall be included when N_Preassigned_Carriers > 0 |
| O | A) Carrier Status Bitmap | ? | indicating whether this pre-assigned carrier will be activated immediately after HO procedure is done | Present if Pre-assigned secondary carrier is present |
| O | B) Physical carrier index | 6 | Physical carrier index (see Table 761) of the pre-assigned secondary carrier for use at the target ABS | Present if Pre-assigned secondary carrier is present |
| O | C) Logical carrier index | ? | is assigned implicitly in the order of Carrier information of each pre-assigned secondary carriers. | Present if Pre-assigned secondary carrier is present |

------------------------------------------------- End of proposed text II --------------------------------------------------