## Slide 1: Topology/Protection Comment Resolution Summary
Jason Fan, Section Editor
(jason@luminous.com)
Jim Kao, Technical Editor
(jkao@cisco.com)

## Slide 2: Clause 10
154 comments
  39 technical binding
  25 technical non-binding
  90 editorial
Adhoc group resolution (technicals)
  48 accepted, accepted/mod, accepted/dup
  6 superceded
  3 deferred (2 technical binding)
  1 rejected (1 technical binding)
  5 punted to WG (3 technical binding)
  1 punted to OAM
Editorial license requested

## Slide 3: Clause 11, Annex J
74 comments
  14 technical binding
  19 technical non-binding
  41 editorial
Adhoc group resolution (technicals)
  27 accepted, accepted/mod, accepted/dup
  4 superceded
  1 deferred
  1 punted to OAM
Editorial license requested

## Slide 4: Issues Covered: Highlights
PICS to be added
Description of topology database to be enhanced
Station will alarm based on duplicate MAC address detection but will not intentionally drop frames
State machines to be modified to use C code
State machine to be added defining topology database updates
Topology message split into vendor-specific TLV and station TLV messages
Station weight TLV optional, not mandatory

## Slide 5: Issues Covered: Highlights
A jumbo frame preferred station on an RPR ring will behave as a non jumbo frame preferred station if any station on that ring reports that it is not jumbo frame preferred. The behavior of a non jumbo frame preferred station will be defined in Clause 6 as the following:
  The stage queue processing state machine will discard any frame larger than the currently permitted MTU, which never exceeds the jumbo frame size specified in Clause 8.
  The transit path has the option of either passing or discarding frames larger than the currently permitted MTU.
Wrapping will be used on an RPR ring if all stations on that ring report that they prefer wrapping

## Slide 6: Issues Covered: Highlights
In vendor-specific TLV, vendor will be identified by a 24-bit OUI and a 24-bit OUI-dependent field
TLV periodic timer default value will be changed from 100 ms to 1 second
Chief Editor is requested to provide guidance on where the conversion equations between clause-specified values and MIB defined values is specified. Likely candidates include the clause which specifies the value or the MIB clause.
In case of the failure of a station’s pass-through path, a station shall not wrap on both sides.
  Additional description of how internal equipment failures may affect the externally visible behavior of a station will be provided by the PAH to the editors of the implementation guidelines annex.

## Slide 7: Issues Covered: Highlights
Wrap preferred and jumbo preferred bits will both be contained in the protection message. The station capabilities TLV will be removed.
Additional description to be added describing triggering of protection messages
Editors will provide clarification of what is needed at protection state machine running on one side of station from protection state machine running on the other side of the station
Protection state machine cleanup
Protection message modified to contain protection information from both the east and west sides of a station.

## Slide 8: Summary of Deferrals and Rejections
1017, 2239: Deferred to PAH
  Definition of MAC address duplication checks
1137: Deferred to PAH
  Definition of additional state machines for topology
21491: Deferred to PAH
  Additional overview needed for topology and protection
21477: Rejected (commenter agrees)
  Commenter believes dynamic bandwidth reservation can be handled at a later date

## Slide 9: Punts
5 punts to WG
  988, 1011 (TB), 1067, 1087 (TB), 1106 (TB)
Punted to OAM
  1010, 1491 (TB)
Punted from MAC
  334 (input provided and punted back)
Punted from PHY
  1297 (TB)
    Accepted/modified