## Slide 1: Section 2 (MAC) CRG Summary
John Lemon
Steve Wood
David James

## Slide 2: Summary
545 comments for Clauses 5, 6, 8, F, G, H, I
All technical comments addressed
32 comments deferred to WG
Editorial license granted on editorial comments

## Slide 3: Issues Covered – Clause 5
Ringlet Selection moved from Control Sublayer to Datapath Sublayer
Strict and relaxed frames both required to be supported, and strict mode forces all frames to be strict
Exact delay/jitter bounds not yet specified, felt to be possible to express, Editor’s Note still remains asking for contributions
Several “Editorial, Binding” comments

## Slide 4: Issues Covered – Clause 6
TTL setting clarifications
State table corrections and enhancements
  Especially flooding mode
STQ sizing
Delay and jitter bounds
Removed Cc shaper (redundant with FA)
All classA control frames are subclassA0
shaperD to shape nrXmitRate, but limit only add
SA hop count validation done only on Rx
Stations in passthrough still generate Idles
Bridge mode Rx, Tx rules moved from E to 6
Many “Editorial, Binding” comments

## Slide 5: Issues Covered – Clause 8
Realigned control frame with data frame
Frame format redefinitions: deferred
SA is always local to the ring
Control frames are never jumbo
Many “Editorial, Binding” comments

## Slide 6: Issues Covered – Annexes F,G,H,I
CRC16 changed back to initialization with all 1’s
  (same as CRC32)
Add Implementation Guidelines annex
  First entry is STQ sizing discussion

## Slide 7: Technical, Binding Rejected
269: Adding configuration via MA_control.requests
296: Create new MAC access control and fairness mechanisms
475: Add all state transitions into illustrative flow charts
521: frame.SA set to SA field of MA_DATA.request
624: Change the frame format to group all the RPR control fields together
664: Replace extRingControl field with source address consistency check

## Slide 8: Comments Deferred To WG (1)
259: Change ringletId0/1 to east/west in MA_Data.request / MA_Data.indication primitives
278: Do not pass SC-FCM to client
324: Ordering of frames within a microflow
364: Remove claims of delay/jitter bounds for classA and classB
365: Include subclassA0 and subclassA1 in Service Classes table
373: Specify how to measure/calculate RTT
386: Allow major priority inversions

## Slide 9: Comments Deferred To WG (2)
435: Require availability of simulation model
463: Evaluate frame.ps bit only for strict frames
465: Decrement TTL on opposing ringlet
467: Discard rule limited to frame.so?
530: When wrapping, bi-directional flooding should not be allowed
542: Add shaper to balance add/transit
614: Configurable MTU size
618: Minimum frame size of 64 bytes for Ethernet PHYs
634: How to display bit numbers in figures

## Slide 10: Comments Deferred To WG (3)
667: Replace frame.extRingControl field with an 8-bit SSID
671: Extended frames to be used only in strict frames
674: Reduce frame.ff field to 1 bit indicating flood/no_flood
679: Remove frame.ps field
680: Limit the frame.ps field to only strict order data frames generated by wrapping stations
685: Overload the frame.parity field to also be the frame.ps field for data frames
691: Change the 16-bit HEC to a 32-bit HEC

## Slide 11: Comments Deferred To WG (4)
708: Broadcast and multicast always considered remote
709: Unknown unicast always considered remote
713: Remove extended frame mode
719: Extended frame DA contains actual DA
759: Duplicate of 719?
772: Fairness frame format changes
1478: Remove H.3 (Spatial Queuing) and H.4 (Spatial Shaping) subclauses
809: Add separate transit path and FA for classB
1449: bridge mode is a superset of host mode

## Slide 12: Action Items
WG requested to provide contributions on latency bounds (see D1.0 #209, D2.0 #’s 241,242,245,360)
WG requested to provide performance text including delay for all service classes (see D1.2 #78)
Request input on defining RTT for three cases (Ring, Loop, Fairness-feedback)
Marc Holness requested to provide text describing context containment mechanism (see D2.0 #454)
Harry Peng requested to provide justification submission for default values of access delay timers (see D2.0 #524)

## Slide 13: Open Issues
More precise jitter bounds for classA and classB
Up to date illustrative code