## Slide 1
Provisioning in RPR Networks
Rodney Lindemeier
rodney.lindemeier@lglass.net
IEEE 802.17 Plenary Meeting
Vancouver, BC, Canada
July 2002

## Slide 2
Resilient Packet Ring (RPR)
A ring-based MAC (Media Access Control)
  Enables Private line and Data
Emerging Layer 2 solution designed for MAN fiber rings
  Reduced fiber usage
  Carrier-class service guarantees and resilience
    50 ms restoration; bounded delay and jitter
  Fair BW management and high BW efficiency
  Leverages Ethernet & SONET PHYs
  Scalable packet edge solution (622 Mbps to 10+ Gbps)
  Bandwidth reuse between segments of the ring
  Distributed switching across the ring
  Data flows in one direction on ring and control information flows in opposite direction
In highly congested implementations can it survive error free ??
Can it be cost competitive to Ethernet and SONET ??
Cable
Wireless
ISP
IP Backbone
Applications
ASP
IP Backbone
Applications
Resilient Packet Ring
(RPR)
10 Gbps
Metro Ethernet
Standard under
development
in IEEE 802.17

## Slide 3
RPR Failure Scenario
RPR
Core 5
RPR
Edge 1
RPR
Edge 4
RPR
Edge 2
Working and Protect
Paths
Customer
Interfaces
Customer
Interfaces
Customer
Interfaces
10Gb RPR
Ring
Fully loaded RPR ring
Traffic from Edge 1 to Edge 2
Traffic from Edge 1 to Edge 3
Traffic from Edge 2 to Edge 3
Traffic from Edge 3 to Edge 4
Traffic from Edge 4 to Edge 1
What happens after a cut
between Edge 2 and Edge 3
RPR
Edge 3
Customer
Interfaces
5Gb
5Gb
5Gb
X
Cut
10Gb
10Gb

## Slide 4
RPR Failure Scenario with Wrapping Protection
RPR
Core 5
RPR
Edge 1
RPR
Edge 4
RPR
Edge 2
Working and Protect
Paths
Customer
Interfaces
Customer
Interfaces
Customer
Interfaces
10Gb RPR
Ring
In this case the bandwidth demand between Edge 2 and Edge 4 is 20Gb which is twice the HS rate.
RPR
Edge 3
Customer
Interfaces
10Gb
5Gb
X
Cut
10Gb
10Gb
5Gb Protect path
5Gb Protect path
X
Cut

## Slide 5
RPR Failure Scenario with Steering Protection
RPR
Core 5
RPR
Edge 1
RPR
Edge 4
RPR
Edge 2
Working and Protect
Paths
Customer
Interfaces
Customer
Interfaces
Customer
Interfaces
10Gb RPR
Ring
RPR
Edge 3
Customer
Interfaces
5Gb
X
Cut
10Gb
10Gb
5Gb Protect path
5Gb Protect path
X
Cut
In this case the bandwidth demand between Edge 2 and Edge 4 is 20Gb which is twice the HS rate.

## Slide 6
    Two fibers do not allow for TDM 10 Gb / OC192c signal transport.
    Circuit Emulated TDM traffic on an RPR ring can not exceed 50% of the effective bandwidth on the RPR ring over any span
    It will be difficult for RPR to be Competitive against 4 fiber BLSR designs for TDM type traffic.
    For Data, will the through put be sufficient to compete against SONET?
Issues associated with Bandwidth provisioning

## Slide 7
Issues associated with Bandwidth provisioning
If Circuit Emulated TDM traffic on an RPR ring does exceed 50%, CE traffic will drop during a fiber switching event.
Should the provisioning section (there is not provisioning section), have rules for provisioning (only a small paragraph 9.10 that has pre-provisioning capability for HP traffic)?
Does this get addressed in the specification or is this a vendor implementation issue?

## Slide 8
Issues associated with Bandwidth provisioning
This will affect all RPR implementations whether they are only 2 fiber rings or ringlets, whether wrapping or steering applications.
It may be so simple that the general consensus is that one would not provision more than 50% CE traffic.
This has not been discussed and now is the time to inject provisioning rules into the specification if it is going to happen.