## Slide 1: Motion 2001-Nov-15-Number Time: HH:MM
The RPR header and data shall be individually protected by separate CRCs.
M: David V. James
S: Stein Gjessing
Y: N: A:

## Slide 2: Motion 2001-Nov-15-Number Time: HH:MM
The RPR MAC shall provide the client with sufficient information to support selection of packets based on the hop distance between the source and destination stations. As an example, this MAC-supplied information would allow the client to send a packet over 2 hops, while inhibiting sending of packets over 4 hops.
M: David V. James
S: Stein Gjessing
Y: N: A:

## Slide 3: Motion 2001-Nov-15-Number Time: HH:MM
The RPR MAC shall support the allocation of best-effort traffic using weighted fairness.
M: David V. James
S: Stein Gjessing
Y: N: A:

## Slide 4: Motion 2001-Nov-15-Number Time: HH:MM
The RPR MAC shall have idle management mechanims that ensure no packet loss with the assumption that each MAC may have independent clocks. Furthermore, these clocks may deviate by a physical-layer dependent amount, possibly as large as ±100PPM.
M: David V. James
S: Stein Gjessing
Y: N: A:

## Slide 5: Motion 2001-Nov-15-Number Time: HH:MM
The RPR MAC shall support wrapping and steering. The client shall be able to label individual frames, so that the desired protection mechanism can be selected on a per-frame basis.
M: David V. James
S: Stein Gjessing
Y: N: A:

## Slide 6: Motion 2001-Nov-15-Number Time: HH:MM
The RPR MAC capabilities shall not be compromised by the desire to support more than 2 ringlets on each ring. Specifically:
If ringID identifiers are mandated in the header, these identifiers shall have a 1-bit size.
Stations that support only two ringlets shall not be complicated by the desired to support N+1 ringlets.
M: David V. James
S: Stein Gjessing
Y: N: A:

## Slide 7: Motion 2001-Nov-15-Number Time: HH:MM
The RPR MAC shall support three classes of traffic, as follows:
Class-A: Provisioned BW & low latency (latency is not affected by ringlet circumference).
Class-B: Provisioned BW & latency (latency possibly affected by ringlet circumference).
Class-B: Unprovisioned. Residual opportunistic BW. Allocated based on weighted fairness.
M: David V. James
S: Stein Gjessing
Y: N: A:

## Slide 8: Motion 2001-Nov-15-Number Time: HH:MM
The RPR MAC shall support two forms of class-A (guaranteed-bandwidth low-latency bandwidth) bandwidth management protocols, called proactive and reactive. The proactive protocol has no (significant) lower-class transit buffer requirement and relies on prenegotiated transmission rates. The reactive protocol relies on a larger transit buffer to hold lower-class traffic while sending dynamic flow-control information upstream.
M: David V. James
S: Stein Gjessing
Y: N: A: