## Slide 1: Additional Secondary MAC Rules
These rules are in addition to what is currently in comments #386-#391
Ringlet selection, on a given ringlet, uses secondary MAC information that is contained in a valid topology entry, and that is marked in use.
If new secondary MAC address information is received and topology is valid, or when topology becomes valid:
  The new information is written into the topology database and is marked not in use
  Secondary MAC address validation is performed, taking into account all secondary addresses (whether or not in use).
  If validation passes, all secondary MAC addresses within the reachable topology are marked in use.
  If validation fails, there is no effect on secondary MAC addresses in the topology database.

## Slide 2: Additional Secondary MAC Rules
When topology becomes unstable or invalid:
  No effect on secondary MAC addresses in the topology database.
If new secondary MAC address information is received and topology is not valid:
  New secondary MAC address information is added to database, and is marked not in use.
When TP frame is received that duplicates a secondary MAC address of the local station:
  The duplicated secondary MAC address is marked not in use.
When a valid topology database entry becomes invalid or when the station MAC address in a valid entry is rewritten:
  All ATD information is cleared from that entry. This is needed because a new topology can be discovered well within a single ATD timer period.